## Slide 1: Pre RAN5#77 - 5G WG Status (after Oct 2017 bis meeting) – NSA Focus

## Slide 2: Status of Core Groups after Oct-17 bis meeting(s)
Summary
RAN2 Status
ASN.1 Status
CT1 Status
CT6, SA3 Status
Core Spec Updates and Applicability

## Slide 3: RAN2 Status
C-plane
  RAN2 made good progress during Oct bis meeting. Lots of TPs for RRC details (such as RRC reconfiguration procedures) were agreed.
  The NR RRC specification would be finalized by 5 email discussions to capture the agreements made in this RAN2 meeting, so it’s likely that a good quality of draft RRC spec would be available in Nov meeting (RAN2#100 Reno). This draft can be good starting reference for RAN5 TC.
  The discussion on MR-DC UE capability on track for completion as well.
U-plane
  For MAC, RAN2 UP session made good progress but still could not fully converge on a few topics. Email discussions underway.
  U-plane design should be available by Dec 2017 (apart from SDAP).
Risks for NSA Option3 Completion - There are still some open issues in RRM; important one is the RRM impact of BWP which looks challenging to be completed by Dec 2017.

## Slide 4: 5G System ASN.1
RRC, L1\L2
Option3 will have impact also on LTE ASN.1. Mar’18 ASN.1 freeze for option3 will target both NR RRC ASN.1 AND LTE RRC ASN1.
  The impact to LTE RRC is to add UE capabilities for NR, the transfer of NR RRC message encapsulated in LTE RRC, measurements for NR and so on.
RAN2 aiming at ensuring that the following will be achieved in Rel-15 LTE RRC ASN.1 in Mar’18.
  Compilable LTE RRC ASN.1.
  Full backwards compatibility to Rel-14 LTE RRC ASN.1: i.e. we can still use all pre-Rel-15 LTE features using the Mar’18 Rel-15 LTE RRC ASN.1.
Both ASN.1 needs to be considered for NR RRC WP

## Slide 5: CT1 Option 3 status overview
Changes needed in CT1 and Progress
  Definition of UE NAS capability for support of dual connectivity with NR -> Done
    Enables MME to select PGW/SGW which supports Option 3 data rates
  Definition of NAS indication from network to UE that dual connectivity with NR is restricted for the UE -> Done
  Extension of bit rates signaled in QoS IEs -> Done
  Potentially: enable signaling of UE’s NR security capabilities via NAS -> TBC
    Needed only if SA3 decides to use NAS signaling for this rather than RRC signaling
    Still under debate in SA3
Changes affect existing NAS specs (TS 24.301 and TS 24.008) which needs to be considered for RAN5 TC.
CT1 is on track to complete all changes\Specs for Option 3 by Dec-17

## Slide 6: CT6 Updates
Platform
  CT6 may evaluate the usage of the SSP platform for Rel.15. as an alternative to UICC. The availability of the SSP platform will not be clear until end of Q1 ’18 at least.
USIM application + USAT
  CT6 has started collecting requirements for the 5G USIM and USAT in TR 31.890, Expectation is that CT6 will simply work to complete the TR during the November meeting, and will start actual implementation of changes required for 5G system at the beginning on 2018.
  The reason is that many requirements were still not finalized or agreed in other groups, to allow CT6 to proceed with his work.
Rel-99 USIM
  It shall be possible to re-use Rel-99 USIM to access NSA option 3 and possibly 5GS. There has been no decision in SA3 till now that would prevent this from happening

## Slide 7: RAN2 Core Specs
Item No. | Core Specification and Short Description | Applicable to 5G NR NSA (Option 3, 7 and 4) | Applicable to SA 5G NR (Option 2, 5) | Notes
1. | TS 37.340 – Multi Connectivity | Yes | No | General
2. | TS 38.304 – Idle Mode | Option 3, 7 -No Option 4- Yes | Yes | 
3. | TS 38.306 – Capabilities | Yes | Yes | 
4. | TS 38.321 - MAC | Yes | Option 2-Yes Option 5 -No | May have mmW Beam acquisition impact
5. | TS 38.322 – RLC | Yes | Option 2-Yes Option 5 -No | 
6. | TS 38.323 – PCDP | Yes | Option 2-Yes Option 5 -Yes* | All NSA bearer options need to be considered
7. | TS 37.324 - SDAP | Option 3 -No Option 4,7 - Yes | Yes | Yes, for 7 and 4 but not for Option3
8. | TS 38.331- RRC | Option 3 – Partial Option 4,7 – Yes | Option 2 – Yes Option 5- Partial+ *(may be – TBD) | For NSA Option 3, only RRC Reconfiguration and Measurement Reporting applied (SCG can have SRB-3)
9. | TS 38.300 – Overall impact | Yes | Yes | User plane description for NSA
10 | TS 36.331 -LTE RRC | Yes | No | LTE impact for NR ASN.1 RRC Reconfiguration Message
11 | TS 36.300 | Yes | No | 

## Slide 8: CT1 Core Specs
Item No. | Core Specification and Short Description | Applicable to 5G NR NSA (Option 3, 7 and 4) | Applicable to SA 5G NR (Option 2, 5) | Notes
1. | TS 24.301 | Option 3- Yes Option 4, 7 - No | Yes | Extension of the maximum range of QoS values for Option 3 Possible security related updates for Option 3 Changes to Attach TAU procedure for the 5GS UE also supporting EPS are need to enable interworking between 5GS and EPS
2. | TS 27.007 | Option 3- Yes Option 4, 7 - No | Yes | - Potential updates for extension of the maximum range of QoS values for Option 3 - Potential extension of existing AT commands for 5GS, and definition of new AT commands for 5GS
3 | TS 24.008 - Mobile radio interface Layer 3 specification; Core network protocols; Stage 3 | Option 3- Yes Option 4, 7 - No | No | NAS Capability Bit Support for Dual Connectivity, QoS IE
4 | TR 24.890 – NAS Impact for 5G NR | Option 3- No Option 4, 7 – Yes | Option 2 – Yes Option 5 – Yes | Study item 60% completed
5 | TS 24.501 – NAS Protocol for 5GS | Option 3- No Option 4, 7 – Yes | Option 2 – Yes Option 5 – Yes | Specs to be created after Oct 2017
6 | TS 24.502 – 5GS via non-3GPP access networks | NA | NA | Specs to be created after Oct 2017

## Slide 9: CT6 Core Specs
Item No. | Core Specification and Short Description | Applicable to 5G NR NSA (Option 3, 7 and 4) | Applicable to SA 5G NR (Option 2, 5) | Notes
1. | TS 31.101- UICC( R99) | Option – Yes Option 4,7 - TBD | Option 2 – TBD Option 5 - TBD | It shall be possible to re-use Rel-99 USIM for NSA Option 3
2. | TR 31.890 – UICC\USAT for 5GS | TBD (UICC and SSP) | TBD (UICC and SSP) | CT6 is only evaluating the list of impacted areas and is likely to start normative work at the beginning of 2018.