## Slide 1: Draft WF on mmWave Demod Testing
Qualcomm, Keysight Technologies, Rohde & Schwarz, Anritsu
3GPP TSG-RAN WG5 Meeting# 78 R5-181693
Athens, Greece, 26 Feb – 2 Mar 2018
Agenda item: 5.3.16.16
Document for: Approval

## Slide 2: Test Procedure for mmWave Demod Testing
Stage1: Selecting the best UE beam during initial call setup.
Stage2: Before the actual test measurement starts, ensure the channel is conducive for UE to start decoding a given MCS as required by the RAN4 requirement.
In order to achieve the above, following 2 metrics have been identified at this point.
  UE reporting of antenna power per Rx port
  RI reporting by the UE during stage2 to ensure the channel is conducive for the UE to decode upto rank2 MCS.
    Further metrics during stage2 is FFS
    For Rank1, a subset of these metrics would be needed
In order to implement the above 2 stages, 2 approaches are considered at this time.
  Approach1: Multiple TRxP
  Approach2: Single TRxP with TRxP/DUT positioning system
Synergy with Demod Baseline System defined in RAN4 for testing the requirements to be considered
Stage 3: Actual test with RAN4 defined test parameters starts
  Details are FFS

## Slide 3: AI for 5G-NR Adhoc#2
For Stage1, come up with test procedure for selecting the best UE beam.
  This part of the test procedure may be leveraged from chap 7 UE RF test case.
One of the metric identified for stage2 is the UE reporting of antenna power per Rx port.
  RAN4 will be sending an LS to RAN1 regarding definition of RSRP per branch and requesting RAN5 to come up with the signaling for the test function.
  RAN5 group can start the work in coming up with the signaling requirements for the test function.