## Slide 1: RAN5#79 21 – 25 May 2018
R5-183219
Test Frequencies in 38.508-1
For discussion

## Slide 2: Example - Inter-band
DL UL
DC_25A_n41A / DC_25A_n41A 38.101-3 f10
  1 LTE carrier (B25) + 1 NR carrier (n41) (both DL&UL)
  LTE carriers allowed: 5, 10, 15 or 20 MHz
  LTE is in MCG, NR is in SCG
  NR SCS & carriers allowed:
    𝛍 = 0 (SCS=15): 10, 15, 20, 40, 50
    𝛍 = 1 (SCS=30): 10, 15, 20, 40, 50, 60, 80, 100
    𝛍 = 2 (SCS=60): 10, 15, 20, 40, 50, 60, 80, 100
Inter-band enables reuse of 36.508 LTE test frequencies

## Slide 3: Example - Inter-band
DC_25A_n41A / DC_25A_n41A
  Example arrangements in frequency domain (for constant 𝛍)
NR
B41
LTE
B25UL
B25DL
LTE

## Slide 4: Example - Inter-band
Master Node: LTE As today. Reuse test frequencies from 36.508 clause 4.3.1.1.25
Table 4.3.1.1.25-1: Test frequencies for E-UTRA channel bandwidth for operating band 25
Test Frequency ID | Bandwidth [MHz] | NUL | Frequency of Uplink [MHz] | NDL | Frequency of Downlink [MHz]
Low Range | 1.4 | 26047 | 1850.7 | 8047 | 1930.7
 | 3 | 26055 | 1851.5 | 8055 | 1931.5
 | 5 | 26065 | 1852.5 | 8065 | 1932.5
 | 10 | 26090 | 1855 | 8090 | 1935
 | 15 [1] | 26115 | 1857.5 | 8115 | 1937.5
 | 20 [1] | 26140 | 1860 | 8140 | 1940
Mid Range | 1.4/3/5/10 15 [1]/20 [1] | 26365 | 1882,5 | 8365 | 1962.5
High Range | 1.4 | 26683 | 1914.3 | 8683 | 1994.3
 | 3 | 26675 | 1913.5 | 8675 | 1993.5
 | 5 | 26665 | 1912.5 | 8665 | 1992.5
 | 10 | 26640 | 1910 | 8640 | 1990
 | 15 [1] | 26615 | 1907.5 | 8615 | 1987.5
 | 20 [1] | 26590 | 1905 | 8590 | 1985
NOTE 1: Bandwidth for which a relaxation of the specified UE receiver sensitivity requirement (TS 36.101 [27] Clause 7.3) is allowed. |  |  |  |  | 

## Slide 5: Example - Inter-band
Secondary Node: NR SA. Reuse test frequencies from 38.508-1 4.3.1.1 Test frequencies for NR operating bands in FR1
Separate table for each SCS
Table 4.3.1.1.1.41-1: Test frequencies for NR operating band n41
Test Frequency ID | Bandwidth [MHz] | ARFCN | Frequency (UL and DL) [MHz]
Low Range | 10 |  | 
 | 15 |  | 
 | 20 |  | 
 | 40 |  | 
 | 50 |  | 
Mid Range | 10/15/20/ 40/50/ |  | 
High Range | 10 |  | 
 | 15 |  | 
 | 20 |  | 
 | 40 |  | 
 | 50 |  | 

## Slide 6: Example - Inter-band
Previously discussed specify using
FrequencyInfoDL (38.331)
absoluteFrequencySSB NR-AFRCN
ssb-SubcarrierOffset (optional– not needed)
frequencyBandList (only in SI, not direct signaling)
absoluteFrequencyPointA NR-AFRCN
However, this message specifies location of SSB+PBCH
Need further research to specify PUSCH

## Slide 7: Example - Intra-band non-contiguous
DL UL
DC_41A_n41A / DC_41A_n41A 38.101-3 f10
    1 LTE carrier + 1 NR carrier (both DL and UL)
    LTE carriers allowed: 5, 10, 15 or 20 MHz
    LTE is PCC, NR is SCC
    NR carriers allowed:
        𝛍 = 0 (SCS=15): 10, 15, 20, 40, 50
        𝛍 = 1 (SCS=30): 10, 15, 20, 40, 50, 60, 80, 100
        𝛍 = 2 (SCS=60): 10, 15, 20, 40, 50, 60, 80, 100
      Intra-band makes reuse of 36.508 LTE test frequencies difficult

## Slide 8
DC_41A_n41A / DC_41A_n41A
  Example arrangements in frequency domain (for constant 𝛍)
LTE
NR
LTE
NR
Example - Intra-band non-contiguous

## Slide 9: Example - Intra-band
Master Node: Intra-band is difficult to reuse LTE test frequencies from 36.508
Secondary Node: Intra-band is difficult to reuse test frequencies from 38.508-1
Intra-band allows use of BCS, don’t have to account for all possible LTE channel BWs nor all possible NR channel BWs

## Slide 10: Example - Intra-band
Previously discussed specify using
FrequencyInfoDL (38.331)
absoluteFrequencySSB NR-AFRCN
ssb-SubcarrierOffset (optional– not needed)
frequencyBandList (only in SI, not direct signaling)
absoluteFrequencyPointA NR-AFRCN
However, this message specifies location of SSB+PBCH
Need further research to specify PUSCH

## Slide 11: Example - Intra-band contiguous
DL UL
DC_(n)41AA / DC_(n)41AA R4-1807824, 25, 27
    1 LTE carrier + 1 NR carrier (both DL and UL)
    LTE carriers allowed: 5, 10, 15 or 20 MHz
    LTE is PCC, NR is SCC
    NR carriers allowed:
        𝛍 = 0 (SCS=15): 10, 15, 20, 40, 50
        𝛍 = 1 (SCS=30): 10, 15, 20, 40, 50, 60, 80, 100
        𝛍 = 2 (SCS=60): 10, 15, 20, 40, 50, 60, 80, 100
      Intra-band makes reuse of 36.508 LTE test frequencies difficult

## Slide 12
DC_(n)41AA / DC_(n)41AA
  Example arrangements in frequency domain (for constant 𝛍)
LTE
NR
NR
LTE
Example - Intra-band contiguous

## Slide 13: Example - Intra-band
Master Node: Intra-band is difficult to reuse LTE test frequencies from 36.508
Secondary Node: Intra-band is difficult to reuse test frequencies from 38.508-1
Intra-band allows use of BCS, don’t have to account for all possible LTE channel BWs nor all possible NR channel BWs

## Slide 14: Example - Intra-band
Previously discussed specify using
FrequencyInfoDL (38.331)
absoluteFrequencySSB NR-AFRCN
ssb-SubcarrierOffset (optional– not needed)
frequencyBandList (only in SI, not direct signaling)
absoluteFrequencyPointA NR-AFRCN
However, this message specifies location of SSB+PBCH
Need further research to specify PUSCH

## Slide 15: Example – Inter&Intra-band
FrequencyInfoDL
absoluteFrequencySSB ARFCS of SSB (mid point)
ssb-SubcarrierOffset 0
frequencyBandList NA
absoluteFrequencyPointA required
scs-SpecificCarrierList required
FrequencyInfoUL
frequencyBandList NA
absoluteFrequencyPointA required
scs-SpecificCarriers required
additionalSpectrumEmission [TBD]NA
p-Max [TBD]test case specific
frequencyShift7p5khz [TBD]

## Slide 16: Example – Inter&Intra-band
SCS-SpecificCarrier
offsetToCarrier INT (0..2199)
pointA to lowest useable subcarrier
subcarrierSpacing SubcarrierSpacing
15, 30 (<6GHz), or 60, 120 (>6GHz)
k0 -6, 0, 6
carrierBandwidth INT (1..max#PRBs)

## Slide 17: Summary – necessary data points
FOR TEST FREQUENCIES 38-508-1 §4.1.3
point A ARFCN of CRB0, lowest subcarrier
subcarrierSpacing 15, 30, 60, …
k0 ∈ (-6, 0 +6)
carrierBandwidth number of PRBs (defined in 38.101-X)
              FR1 38.101-1 Table 5.3.2-1
              FR2 38.101-2 Table 5.3.2-1
offsetToCarrier point A to lowest usable subcarrier in
            number of PRBs

## Slide 18: Example – n41
Frequency range: 2496 MHz <-> 2690 MHz (194 MHz) (38.101-1 §5.2)
supported channel BW (38.101-1 §5.3.5)
point A & CRBs (38.211 §4.4.4.3)
SCS | 𝛍 | 10 | 15 | 20 | 40 | 50 | 60 | 80 | 100
15 | 0 | X | X | X | X | X |  |  | 
30 | 1 | X | X | X | X | X | X | X | X
60 | 2 | X | X | X | X | X | X | X | X
SCS | point A (frequency) | Point A (ARFCN | CRBs
15 | 2 496 015 000 | 499203 | 0 ~ 1076
30 | 2 496 030 000 | 499206 | 0 ~ 537
60 | 2 496 060 000 | 499212 | 0 ~ 368

## Slide 19: Example – n41
Bandwidth Part (38.211 §4.4.5)
  Starting position N
  Number of RBs N
BWP,i
BWP,i
start
size
SCS | N (start) | N(size)
15 | 0 | 1076
30 | 0 | 537
60 | 0 | 268