## Slide 1: Discussion on SIG testcase optimization of 5GC
R5-184805
CATT

## Slide 2: Introduction
Testcase optimization has been doing since later LTE period.
Testcase optimization has been doing by drafting 5G WPs imperceptibly.
  For EN-DC:
    RAN5#77: 155 TCs
    RAN5#78: 132 TCs
    RAN5#79: 101 TCs
It is obvious that the Testcase optimization is the sooner the better
No clear guidance for testcase optimization in RAN5

## Slide 3: Introduction
In current version of WP for 5GC, 101 testcases are planned
more optimization could be done.
FYI: 133 testcases for LTE EPC.

## Slide 4: Discussion
Could testcases with different success/fail cases be merged?
9.1.1.3 | 5G AKA based primary authentication and key agreement / Success / Authentication response by the UE
9.1.1.5 | 5G AKA based primary authentication and key agreement / Authentication not accepted by the UE
9.1.1.6 | 5G AKA based primary authentication and key agreement / Abnormal cases / Network failing the authentication check
Advantage:
Possible saving on common procedures (preamble, postamble…) / test time
Less number of testcases on total
Disadvantage:
Different cases may require different configurations of the UE, USIM and the network
Multi-TPs raises the difficulty of debugging

## Slide 5: Discussion
Could different procedures be combined?
9.1.3 | Identification | New sub-clause
9.1.3.1 | Identification procedure | **** TP1: [TS 24.501:5.4.3] WITH: the UE is in 5GMM-CONNECTED mode WHEN: The AMF initiates the identification procedure by sending an IDENTITY REQUEST message to the UE THEN: the UE shall send an IDENTITY RESPONSE message contain the identification parameters as requested by the network, e.g. the SUPI or the PEI.
Advantage:
Saving on common procedures (preamble, postamble…) / test time
Less number of testcases on total
Disadvantage:
The Paragraphing of the test spec will be messed up
Multi-TPs raises the difficulty of debugging

## Slide 6: Discussion
Could basic procedures covered by other testcases be removed?
9.1.6 | De-registration
9.1.6.1 | UE-initiated de-registration
9.1.6.1.1 | UE-initiated de-registration / switch off
Advantage:
Saving on test time
Less number of testcases on total
Disadvantage:
The Paragraphing of the test spec will be messed up
The definition of features being covered are not clear to the certification groups

## Slide 7: Proposals
A balance between “Saving certification time” and “Saving debugging time”; between “less and tidy testcase numbers” and “clear coverage on features” should be defined into a clear and consistent guidance for testcase optimization