## Slide 1: Proposal of noise impact for FR2 Transmitter Test Case
Anritsu, Keysight, ROHDE & SCHWARZ
RAN5#85, Reno, Nevada,
18 Nov – 23 Nov 2019
R5-199497

## Slide 2: Proposal for influence of noise
Test Case | Proposal for “Influence of noise”
EIRP Spherical Coverage | DSNR=0.3dB for FR2a DSNR=0.9 dB for FR2b
Transmitter Spurious | DSNR=0.41dB for 6Ghz <= f <= 60GHz
As a consequence of offline discussion during RAN5#85[1]-[3], it is proposed to apply the
following values for MTSU definition.
For Transmitter OFF Power, it is recommended not to test in conformance test for band n260 due to its low achievable SNR at test system.
Proposal 1 : For PC3 EIRP Spherical Coverage, DSNR=0.3dB for FR2a and DSNR=0.9dB for FR2b
Proposal 2: For PC3 Transmitter Spurious, DSNR=0.41dB for 6GHz <= f <= 60GHz
Recommendation 1 : Not to test PC3 transmit OFF Power for n260

## Slide 3: WF for ACLR test
Following options are possible to cater for testability issue for ACLR test
  Option 1 : Change the test metric from TRP to EIRP
  Option 2 : Test with TRP, but change the antenna directivity assumption
  (Worst case(baseline) assumption 2x8 array -> Reduce it to e.g. 1x4, 2x4 )
  Option 3 : Test only lower MPR (e.g. 0)
  Option 4 : Test only lower channel Bandwidth
  Option 5 : Combinations of some of the options above
Proposal 3 : RAN5 to investigate options 1 to 5 above in order to improve FR2 ACLR testability. As part of this investigation, make action item for e.g. OEM/Chipset vendors to call for input on :
i) Equivalence of TRP ACLR and EIRP ACLR test(for Option 1)
ii) Antenna directivity assumption applicable for ACLR test(for Option 2)

## Slide 4: References
[1] R5-198450, “Proposal for influence of noise”, Anritsu, RAN5#85
[2] R5-198733, “On the SNR for FR2 TRx test cases”, ROHDE & SCHWARZ, RAN5#85
[3] R5-197499, “On noise impact”, Keysight, RAN5#84