## Slide 1: WF on Band n259
NTT DOCOMO, INC.
3GPP TSG-RAN5 Meeting #85 R5-198071
Reno, Nevada, United States, 18th Nov 2019 - 22nd Nov 2019
Agenda Item : 5.3.18.10
Document for : Information

## Slide 2: Summary
Objective
  The objective of this WF is to define milestone to complete P1 and P2 test cases.
  This WF is based on the contributions [1], [2], [3], [4] during RAN5#85 (Nov-2019).
[Appendix] Terminology in this document
  Priority
    P1 : MOP (EIRP, TRP), REFSENS
    P2 : OFF power, Frequency error, OBW, SEM, ACLR, Tx Spurious (General, co-existence), Rx Spurious
    P3 : Other than P1 and P2
  MU for “Upper limit of TT” calculation
    MU value used only for “Upper limit of TT” calculation. (Not MTSU)
  Test requirement (= Minimum requirement + TT + Relaxation)
    TT : General Test Tolerance based on MTSU
    Relaxation : Relaxation value to improve testability (Low UL, High DL power) issue.

## Slide 3: Time plan
Time plan of RAN5#87, #88 will be updated according to the progress after RAN5#86.
Meetings | RAN5 Time plan
RAN5#85 (Nov-2019) | To define WF Time plan / Milestone Working assumption of frequency range for Band n259 MU analysis (#4) To define TT WF (v1) (#5) To define TT as zero for regulatory items based on the core requirement. P2 (OBW, Tx Spurious, Rx Spurious), P3 (ACS, Blocking)
RAN5#86 (Feb-2020) | To define TT WF (v2) (#6) To define upper limit of MU for TT calculation and ratio based on the analysis from MU contributors. P1 (MOP, REFSENS), P2 (Frequency error, SEM, [ACLR]) The list of TCs will be updated based on the progress during RAN4#94.
RAN5#87 (May-2020) | To define Relaxation WF (v1) To define upper limit of Relaxation for testability issue TCs P2 (OFF power, Rx Spurious, [ACLR]) To complete TT (v1) P1 (MOP, REFSENS), P2 (Frequency error)
RAN5#88 (Aug-2020) | To complete TT (v2) P2 (SEM, [ACLR])

## Slide 4: Frequency range
Working assumption
  MU analysis for Band n259 will be conducted with FR2c (40.8 GHz  f  44.3 GHz).
Action point
  These MU value will be used only for TT discussions.
  It is not intention to finalize MTSU value during RAN5#86 (Feb-2020).
FR2a
FR2b
n260
n259
40.8 GHz
23.45 GHz
32.125 GHz
40.0 GHz
37.0 GHz
43.5 GHz
39.5 GHz
44.3 GHz
FR2c
44.3 GHz
Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status
AP#85.xx | RF | FR2c MU analysis for prioritized TCs (MOP_TRP, EIRP, REFSENS, Freq error, SEM) | MU contributors | R5-198071 | RAN5#86 (Feb-2020) | Open

## Slide 5: TT WF (v1, RAN5#85)
V1 (RAN5#85)
  To define TT as zero for regulatory items based on the core requirement.
    P2 (OBW, Tx Spurious, Rx Spurious), P3 (ACS, Blocking)
    Reference from TS 38.101-2.
TC | TTLTE | TTFR1 | TTFR2a | TTFR2b | TTFR2c
OBW | 0 kHz | 0 kHz | 0 kHz | 0 kHz | 0 kHz
TRx Spurious | 0 dB | 0 dB | 0 dB | 0 dB | 0 dB
ACS, Blocking | 0 dB | 0 dB | 0 dB | 0 dB | 0 dB

## Slide 6: TT WF (v2, RAN5#86)
V2 (RAN5#86)
  To define upper limit of MU for TT calculation and ratio based on the analysis from MU contributors.
    P1 (MOP, REFSENS), P2 (Frequency error, SEM, [ACLR])
Action point
  Same approach as FR2a and FR2b (reference is [5]).
 | FR2a, FR2b |  | FR2c | 
TC | Upper limit (MU for TT calculation) | Upper limit (Ratio) | Upper limit (MU for TT calculation) | Upper limit (Ratio)
MOP (TRP) |  5.5 dBm | 0.65 | TBD | TBD
MOP (EIRP) |  5.5 dBm | 0.65 | TBD | TBD
REFSENS |  5.5 dBm | 0.65 | TBD | TBD
Frequency error |  0.01 PPM | 0.50 | TBD | TBD
SEM | - | - | TBD | TBD
Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status
AP#85.xx | RF | To define Upper limit of MU for TT calculation and Ratio based on the MU analysis. | RAN5 | R5-198071 | RAN5#86 (Feb-2020) | Open

## Slide 7: References
[1] R5-197731 : “Band n259 core requirement”, NTT DOCOMO, INC., RAN5#85 (Nov-2019)
[2] R5-197732 : “Handling of Band n259 in RAN5”, NTT DOCOMO, INC., RAN5#85 (Nov-2019)
[3] R5-197733 : “Frequency range of Band n259”, NTT DOCOMO, INC., RAN5#85 (Nov-2019)
[4] R5-197734 : “Test tolerance of Band n259”, NTT DOCOMO, INC., RAN5#85 (Nov-2019)
[5] R5-1987568 : “Discussion on FR2 Test Tolerance values”, Qualcomm Inc, Verizon Wireless, RAN5#81 (Nov-2018)