## Slide 1: WF on TT FR2 for min Peak EIRP Max TRP and RefSens
Orange, Telecom Italia, Vodafone, Apple, Qualcomm, Ericsson, NTT DOCOMO, AT&T,
China Unicom, China telecom, CMCC, Verizon, T-Mobile US, KDDI, Samsung, Huawei
3GPP TSG-RAN WG5 Meeting #85 R5-199353 Reno. USA. 18th - 22nd Nov 2019

## Slide 2: TT FR2 for proposal for Min Peak EIRP, RefSens, Max TRP for Power class 3
FR2 Min Peak EIRP | FR2 Ref Sens | FR2 Max TRP
TT=0.6MU | TT=0.45MU | TT=0.6MU
Sub clause | TT=X*MU | Maximum Test System Uncertainty | Derivation of MTSU
6.2.1.1 UE maximum output power (EIRP) | PC3 Minimum peak EIRP. Max EIRP Quiet Zone size ≤ 30 cm 3.18 dB (FR2a) 2,9dB 3.31 dB (FR2b) 2.9dB | PC3 Minimum peak EIRP. Max EIRP Quiet Zone size ≤ 30 cm ±4.79 dB (FR2a) ±4.79 dB (FR2b) | MTSU = 1.00 x MU (from Table B.3-2-2. B.3-2-3 in TR 38.903)
6.2.1.1 UE maximum output power (TRP) | PC3 Minimum peak EIRP. Max EIRP Quiet Zone size ≤ 30 cm 2.87dB (FR2a) 2.65dB 3 dB (FR2b) 2.77dB | PC3 Max TRP Quiet Zone size ≤ 30 cm 4.42 dB (FR2a) 4.62 dB (FR2b) | MTSU = 1.00 x MU (from Table B.3-2-2. B.3-2-3 in TR 38.903)
7.3.2 Reference sensitivity power level | (Quiet Zone size ≤ 30 cm. FR2a. FR2b) 3.37 dB -> 2,34dB | ±5.19 dB (Quiet Zone size ≤ 30 cm. FR2a. FR2b) | MTSU = 1.00 x MU (from Table B.19-2-2. B.19-2-3 in TR 38.903)
Note: This TT way forward is applicable for NTC only

## Slide 3: TT FR2 for proposal for EIS and EIRP Spherical Coverage for Power class 3
FR2 Spherical Coverage EIRP | FR2 Spherical Coverage EIS
TT=[0.6]*MU | TT=[0.45]*MU
Sub clause | TT=X*MU | Maximum Test System Uncertainty | Derivation of MTSU
6.2.1.2 UE maximum output power (Spherical coverage) | [2.62 ]dB (FR2a) [2.62 ]dB (FR2b) | PC3 Spherical coverage Quiet Zone size ≤ 30 cm [±4.67+0.3 ]dB (FR2a) [±5.27+0.9 ]dB (FR2b) | 
7.3.4 EIS spherical coverage | [2.232] | [±4.96] dB (Quiet Zone size ≤ 30 cm, FR2a, FR2b) | MTSU = 1.00 x MU (from Table B.19-2-2, B.19-2-3 in TR 38.903)
bracket for TT will be removed after MU is finalized
Note: This TT way forward is applicable for NTC only