3GPP TSG-WG5 Meeting # 89-e	<R5-XYZZYX>

# Electronic Meeting, 9th Nov 2020 - 20th Nov 2020

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 38.523-2 | CR | <CR#> | rev | - | Current version: | 16.5.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Applicability for ethernet header compression and decompression for NR |
| --- | --- |
| Source to WG: | Nokia, Nokia Shanghai Bell |
| Source to TSG: | R5 |
| Work item code: | NR_IioT-UEConTest |  | Date: | 2020-11-06 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | Ethernet header compression functionality is defined in the core specification. This applicability declaration covers testcases defined for EHC functionality. |
| Summary of change: | Applicability for EHC functionality is added to conformance specifications. |
| Consequences if not approved: | EHC testcase applicability is not valid. |
| Clauses affected: | 4.1, 4.2 |
|  | Y | N |  |  |
| Other specs |  | x | Other core specifications | TS/TR ... CR ... |
| affected: | x |  | Test specifications | TS/TR 38.523-1, 38.508-2 CR 4986, XXXX |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

< Start of modifications >

## 4.1	Protocol conformance test cases applicability

< Skipped tables >

Table 4.1-2a: Applicability of Protocol conformance Layer 2 test cases, ref. TS 38.523-1 [2]

| Clause | TC Title | Release | Applicability |
| --- | --- | --- | --- |
|  |  |  | Condition | Comment |
| 7.1.1 | MAC |  |  |  |
| 7.1.1.1 | Random Access Procedures |  |  |  |
| 7.1.1.1.1 | Correct selection of RACH parameters / Random access preamble and PRACH resource explicitly signalled to the UE by RRC / contention free random access procedure | Rel-15 | R | UEs supporting 5GS |

< Skipped table entries >

| 7.1.3.6 | PDCP Ethernet header compression and decompression |  |  |  |
| --- | --- | --- | --- | --- |
| 7.1.3.6.1 | Ethernet header compression and decompression / Correct functionality of ethernet header compression and decompression | Rel-16 | CXYZ |  |

< Skipped tables >

## 4.2	Protocol conformance test cases Applicability Condition

Table 4.2-1: Applicability of Protocol conformance test cases Conditions

| Condition | Test case Selection Expression | Comment |
| --- | --- | --- |
| C01 | IF A.4.1-3/2 THEN R ELSE N/A | UEs supporting EN-DC |
| C02 | IF (A.4.3.4-1/2 OR A.4.3.4-1/3) THEN R ELSE N/A | UEs supporting 5GS and RLC UM Mode |

< Skipped table entries >

| CXYZ | IF (A.4.1-3/1 OR A.4.1-3/2) AND A.4.3.3/XYZ THEN R ELSE N/A | UEs supporting NG-RAN NR or EN-DC and supporting ethernet header compression |
| --- | --- | --- |

< End of modifications >