## RF:

## Action Points at RAN5#90-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#90e.21 | RF | Group To provide feedback on which antenna aperture declaration to incorporate in TS38.508-2 for DFF methodology: --- Option 1: UE vendor declares the exact maximum radiation aperture of any of the panels integrated in the UE --- Option 2: UE vendor declares whether the maximum radiation aperture of any of the panels integrated in the UE is ≤5cm or not --- Other options are not precluded | ?? | R5-210839 R5-211194 | RAN5#91e | Open |

## Action Points at RAN5#89-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#89e.21 | RF | TE vendors to provide preliminary QoQZ and XPD MU and MTSU estimates, using MOP and REFSENS as reference, for QZ sizes of 35 and 40cm (others not precluded) assessed on existing IFF test systems originally designed for 30cm QZ. | KS, R&S, Anritsu | R5-205713 R5-206068 R5-206130 R5-211235 R5-211186 R5-210617 | RAN5#90e | Open |
| AP#89e.22 | RF | RF TE vendors to provide full QoQZ evaluation results for a 20cm QZ in order to keep the 20cm QZ in TS38.521-2 and TS38.508-1 | R&S, KS, Anritsu | R5-206069 R5-206070 R5-206071 R5-211232 | RAN5#90e | Open |
| AP#89e.23 | RF | RF Provide input on acceptable clipping frequency due to fading and/or acceptable fading crest factor margin for FR2 Demod performance and CSI test cases | Qualcomm | R5-206168, R5-205702 R5-211083 | RAN5#90e | Open |
| AP#89e.24 | RF | On/Off time mask MU/ requirement relaxation open items a) Achievable power window PW for FR2 relative power control. b) Wherther there will be a degradation of TE noise floor if the maximum UE power can be as high as 22.4 + 2*PW in the test. c) What is the maximum allowed UE ON power which will not degrade the current specified TE noise floor for OFF power measurement. Assess if this ON power is high enough to identify failing transient periods as shown in section 2.6. | KS, R&S, Anritsu, E///, Huawei, OPPO. | R5-205991r2 R5-211105 R5-211268 | RAN5#90e | Open |

## Action Points at RAN5#88-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#88e.21 | RF | For FR2 absolute power control test cases analyze to determine if we can test both upper and lower limits with a very large span when the aggregated BW is smaller than or equal to 400 MHz. | , E///, Anritsu, Keysight, R&S, Huawei | R5-204022 | RAN5#91e | Open |

## Action Points at RAN5#87-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#87e.21 | RF | Review the existing test point analysis of NR (FR1, FR2) RF tests for optimization | DCM, E///, Huawei, Qualcomm, Oppo, DISH, China Unicom, TMO, CAICT, CMCC, Sporton | R5-201818 R5-202375 R5-204136 | RAN5#91e | Open |
| AP#87e.23 | RF | OEM vendors and Operators to provide feedback on how to handle test coverage for large devices in case 100% coverage cannot be ensured. Any TP allowance, MU relaxations allowed for meeting the requirements | OEMs and Operators | R5-202082 R5-202083 R5-202084 R5-202085 R5-198262 R5-198262 R5-204191 R5-204200 R5-205713 AP#89e.21 | RAN5#90e | Open |
| AP#87e.24 | RF | OEM vendors and operators to provide data on max antenna separation distances and device size for NR FR2 devices that can currently not be tested with the largest QZ size of 30cm in diameter | OEMs and Operators | R5-202082 R5-202083 R5-202084 R5-202085 R5-198262 R5-204191 R5-204200 R5-205713 R5-206068 R5-210617 | RAN5#90e | Open |

## Action Points at RAN5#84 Ljubljana

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#84.21 | RF | Alignment of MPR/ACLR/SEM test points for NR and come with a combined TP analysis (separate analysis required for FR1, FR2 and Interworking) to TR38.905, and associated CRs | Ericsson, KEYS, CAICT | R5-197586 R5-201930 R5-201936/7 R5-201931 R5-201946 R5-201947/8 R5-201786 R5-201919 R5-205572 R5-210546 R5-210547 | RAN5#90e | Open |

## Action Points at RAN5#83 Reno

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#83.22 | RF | To provide feedback on the maximum difference in direction between the beam peak at NTC when compared to ETC to determine the Test procedure and framework for peak EIRP and peak EIS test cases | RAN5 | R5-194596 R5-196361 R5-204189 R5-210557 R5-211184 R5-211264 R5-211185 R5-211276 | RAN5#90e | Open |