## Slide 1: Discussion on handling of CA related test cases among WIs
CMCC, Huawei, Hisilicon, Ericsson
3GPP TSG-RAN5 Meeting #95-e R5-223338
Electronic Meeting, May 9 – May 20, 2022

## Slide 2: Background
Observation 1: The requirements for different types of CA configurations have been defined in different RAN4 WIs, which leads to complex RAN5 WIs’ scopes differentiation.
Req. for different types of config. in TS 38.101-1 | CC number in 38101-1 Rel-15 [1] | CC number in 38101-1 Rel-16 [2] | CC number in 38101-1 Rel-17 [3]
intra-band contiguous CA | 2DL/1UL | 2DL/2UL, 3DL/1UL, 4DL/1UL, 5DL/1UL | 
intra-band non-contiguous CA | / | 2DL/1UL, 2DL/2UL, 3DL/1UL, 4DL/1UL | 3DL/2UL
inter-band CA, intra-band contiguous + inter-band, intra-band non-contiguous + inter-band | 2DL/1UL, 2DL/2UL | 3DL/1UL, 3DL/2UL, 4DL/1UL, 4DL/2UL, 5DL/1UL | 3DL/3UL, 4DL/3UL, 5DL/2UL, 5DL/3UL, 6DL/1UL, 6DL/2UL, 6DL/3UL, 7DL/1UL, 7DL/2UL, 7DL/3UL, 8DL/1UL, 8DL/2UL, 8DL/3UL, 9DL/1UL, 9DL/2UL, 9DL/3UL, 10DL/1UL, 10DL/2UL, 10DL/3UL, 11DL/1UL, 11DL/2UL, 12DL/1UL, 12DL/2UL

## Slide 3: Proposal
Proposal 1: To adopt the following WIs’ scopes dividing solution to handle CA related test cases in RAN5. Rapporteurs to update the corresponding WPs accordingly. Contributions to be submitted under the corresponding WIC.
Test cases for different types of configurations in TS 38.521-1 | Rel-15 WI “TEI15_test, 5GS_NR_LTE-UEConTest” (UIC=760087) | Rel-16 WI “NR_RF_FR1-UEConTest” (UIC=870061) | Rel-16 WI “NR_CADC_NR_LTE_DC_R16-UEConTest” (UIC=830083) | Rel-17 WI “NR_CADC_NR_LTE_DC_R17-UEConTest” (UIC=900056)
intra-band contigs CA test cases | 2DL/1UL with BW Class C (completed) | 2DL/1UL with BW Class B (completed), 2DL/2UL with BW Class B and C | 3DL/1UL, 4DL/1UL, 5DL/1UL | 
intra-band non-contigs CA test cases | / | 2DL/1UL (completed), 2DL/2UL | 3DL/1UL, 4DL/1UL | 3DL/2UL3
inter-band CA, intra-band contigs + inter-band, intra-band non-contigs + inter-band test cases | 2DL/1UL (completed), 2DL/2UL (completed) | 3DL/1UL1 (completed) | 3DL/2UL, 4DL/1UL, 4DL/2UL, 5DL/1UL | 3DL/3UL Tx2, 4DL/3UL Tx2, 5DL/2UL, 5DL/3UL Tx2, 6DL/1UL, 6DL/2UL, 6DL/3UL Tx2, 7DL/1UL, 7DL/2UL, 7DL/3UL Tx2, 8DL/1UL, 8DL/2UL, 8DL/3UL Tx2
NOTE 1: 3DL/1UL TCs should be in the scope of Rel-16 WI “NR_CADC_NR_LTE_DC_R16-UEConTest” (UIC=830083). However, 3DL/1UL TCs have already been completed under Rel-16 WI “NR_RF_FR1-UEConTest” (UIC=870061). No need to remove 3DL/1UL TCs into Rel-16 WI “NR_CADC_NR_LTE_DC_R16-UEConTest” (UIC=830083). NOTE 2: Only Tx TCs need to be completed for xDL/3UL since the Rx TCs for xDL/2UL also apply to xDL/3UL. NOTE 3: For intra-band non-contigs CA TCs, Rel-16 3DL/1UL Rx TCs apply to 3DL/2UL and Rel-16 2DL/2UL Tx TCs apply to 3DL/2UL. So no further TCs are needed for 3DL/2UL in Rel-17. |  |  |  | 

## Slide 4: Reference
[1] 3GPP TS 38.101-1 V15.17.0 (2022-03).
[2] 3GPP TS 38.101-1 V16.11.0 (2022-03).
[3] 3GPP TS 38.101-1 V17.5.0 (2022-03)
Notes: (2022-3)

## Slide 5: Thank you!