## Slide 1: Discussion on handling of R18 NB-IoT/eMTC NTN RF/Performance/RRM WI
CMCC, MTK, BV
3GPP TSG-RAN5 Meeting #98 R5-230413
Athens, Greece, Feb 27th - Mar 3rd, 2023

## Slide 2: The Impacts to TS 36.508 and the Creation of TS 36.521-4
Proposal 1: To update Common test environment for NB-IoT/eMTC NTN in TS 36.508.
  eMTC NTN: to update the existing E-UTRA sections, including Section 2(References), Section 4(Common test environment), Section 5(Test environment for RF test), Section 6(Test environment for Signalling test), Section 7(Test environment for RRM tests).
  NB-IoT NTN: to update the existing NB-IoT Section 8 (NB-IoT test environment).
Proposal 2: For TS 36.521-4,
  To introduce test cases with suffix A for UE category M1
  To introduce test cases with suffix B for UE category NB1 and NB2
  To introduce RF Tx test cases for UE category M1 and NB1/NB2 in Section 6
  To introduce RF Rx test cases for UE category M1 and NB1/NB2 in Section 7
  To introduce Performance test cases for UE category M1 and NB1/NB2 in Section 8

## Slide 3: Option 1 to TS 36.521-2
Option 1: No new sections to be added.
  To add new “Table 4.1-8: Applicability of RF and Performance conformance test cases for NB-IoT/eMTC NTN, ref. TS 36.521-4 [20]”, “Table 4.1-8a: Applicability of RF and Performance conformance test cases Conditions” and “Table 4.1-8b: Tested Bands Selection Criteria of RF and Performance conformance test cases for NB-IoT/eMTC NTN”.
  To introduce applicabilities for NB-IoT/eMTC NTN RRM test cases in existing “4.2 RRM conformance test cases/Table 4.2-1: Applicability of RRM conformance test cases, ref. TS 36.521-3 [2]” in TS 36.521-2, and to add the corresponding conditions and Tested Bands Selection Criteria into the existing “Table 4.2-1a: Applicability of RRM conformance test cases Conditions”.

## Slide 4: Option 2 to TS 36.521-2
Option 2: New separate sections to be added for RF/Performance conformance test cases and RRM conformance test cases for NB-IoT/eMTC NTN, respectively.
  To add new section “4.1A RF and Performance conformance test cases for NB-IoT/eMTC NTN” with sub-sections for “4.1A.1 RF conformance test cases for NB-IoT/eMTC NTN” and “4.1A.2 Performance conformance test cases for NB-IoT/eMTC NTN”, respectively.
  To add the corresponding applicability of RF and Performance test cases and conditions into new tables under new sub-sections 4.1A.1 and 4.1A.2, respectively.
  To add new section “4.2A RRM conformance test cases for NB-IoT/eMTC NTN”. To add the corresponding applicability of RRM test cases and conditions into new tables under new section 4.2A.

## Slide 5: Option 3 to TS 36.521-2
Option 3: A new separate section to be added for RF/Performance/RRM conformance test cases for NB-IoT/eMTC NTN only.
  To add new section “4.3 RF and RRM conformance test cases for NB-IoT/eMTC NTN”
  To add new sub-sections “4.3.1 RF conformance test cases for NB-IoT/eMTC NTN”
  To add new sub-sections “4.3.2 Performance conformance test cases for NB-IoT/eMTC NTN”
  To add new sub-sections “4.3.3 RRM conformance test cases for NB-IoT/eMTC NTN”
Proposal 3: To endorse Option 3 to introduce applicabilities for NB-IoT/eMTC NTN RF/Performance test cases into TS 36.521-2.

## Slide 6: Thank you!