## Slide 1: Discussion on spurious emission for UE co-existence for CA in E-UTRA
ZTE Corporation
3GPP TSG-RAN5 Meeting #98 R5-231277 Athens, Greece, February 27th– March 3rd, 2023

## Slide 2: Spurious emissions for UE co-existence in NR
Background:
In RAN5#96-e meeting, to optimize the test requirement tables for UE co-existence in NR, the following agreements have been achieved for inter-band EN-DC and inter-band CA configurations (R5-225651).
Agreement 1: It is proposed to merge the tables of test conformance requirements for EN-DC configurations for UE co-existence with protected bands with all the releases in one table and add a column “Release” in the table to indicate from which release the configuration supports.
  If the requirements for a specified configuration have not changed since an early release, the column of “Release” should be noted as all the supported releases in one row. Otherwise, a new row in the table for the later release with new requirements for the specified configuration should be added.
  If the Note number in the table is different among releases, an additional information for release should be applied, such as NOTE X_R15, NOTE X_R16, etc.
Agreement 2: It is proposed to merge the tables of test requirements for inter-band CA configurations for UE co-existence with protected bands in TS 38.521-1 respectively. A new column of “Release” in the merged table to indicate all the supported releases is suggested. If the requirements for a certain combo are different among releases, the combo should be added in the table separately.
Agreement 3: It is proposed to merge the tables of test requirements for the specified single NR band for UE co-existence with protected bands in TS 38.521-1. A new column of “Release” in the merged table to indicate all the supported releases is suggested.

## Slide 3: Spurious emissions for UE co-existence in NR
Examples for UE co-existence for inter-band EN-DC configurations:

## Slide 4: Spurious emissions for UE co-existence in E-UTRA
Observation 1: For spurious emissions for UE co-existence in E-UTRA, the test requirements for the UE are release specific. If the UE supports a CA configuration, which is not defined in the table corresponding to UE’s release, the requirements for this CA configuration are taken from the table of earliest release where requirements for this CA configuration are defined.
Observation 2: Similar to the cases in NR, the test requirements for inter-band CA for UE co-existence with protected bands in E-UTRA are specified in different tables in accordance with different releases respectively. For most of the inter-band CA configurations in the earlier releases, the test requirements are the same and are redundant in the later releases.

## Slide 5: Spurious emissions for UE co-existence in E-UTRA
Observation 3: Follow the same guidelines in NR, the test requirements for spurious emissions for UE co-existence for dual-uplink inter-band CA in E-UTRA can be optimized such as blow.
Proposal 1: Follow the same guidelines in NR, it is proposed to merge the tables of test requirements for spurious emissions for UE co-existence for dual-uplink E-UTRA inter-band CA configurations in TS 36.521-1 respectively. A new column of “Release” in the merged table to indicate all the supported releases is suggested. If the requirements for a certain combo are different among releases, the combo should be added in the table separately.
    If the Note number in the table is different among releases, an additional information for release should be applied, such as NOTE X_R15, NOTE X_R16, etc.

## Slide 6: Thank you!