## Slide 1: Way Forward on QoQZ Procedure for Spurious Emissions
3GPP TSG-RAN WG5 5G NR AH #4
Singapore, Singapore, 21st – 25th January 2019
R5-190942
Keysight Technologies, Rohde&Schwarz, Anritsu

## Slide 2: Background
Three contributions on the QoQZ for Spurious Emissions procedure have been submitted by TE vendors [R5-190386, R5-190567, R5-190343] to this meeting
The following slides outline agreements reached during offline discussions on topics related to proposals made in the respective contributions

## Slide 3: Test Frequencies
It was agreed to use the following list of test frequencies [GHz]: [6], [12.75], 23.45, 40.8, 66, and 80
Another test frequency of [TBD] GHz will be added as soon as FR2 bands >40GHz are introduced

## Slide 4: Re-Use of In-band QoQZ Measurement Results
It was agreed that the subsets of the QoQZ measurements from the 23.45 and 40.8GHz tests can be re-used under the condition that the reference antenna position and orientation as well as the measurement frequency and measurement antenna are identical in both cases

## Slide 5: Measurement Distance
The antenna used to form the beam towards the beam peak direction shall be in FF
Interested parties to provide proposals for
  MU for measuring TRP in NF with measurement distance ≥ 0.62*sqrt(DSE3/l)
  definition of radiating aperture DSE for spurious emissions
  NF system for Spurious Emissions TCs

## Slide 6: Re-Positioning during QoQZ Validation for Spurious Emissions
The beam peak direction of the spur does not have to be in the same hemisphere as the in-band beam peak
Whether the repositioning concept used for in-band measurements can be applied to spurious emissions measurements (QoQZ validation and test cases) by measuring two hemispheres twice is FFS

## Slide 7: Reference Antenna Orientations for QoQZ Procedure
If the device repositioning concept is accepted, a single reference antenna orientation (forward facing) and two orthogonal antenna polarizations shall be used
If the device repositioning concept is not accepted, two reference antenna orientations (forward and backward facing) and two antenna polarizations shall be used
Forward Facing Orientation
Backward Facing Orientation

## Slide 8: Other Agreements
The metric for the MU evaluation is TRP/efficiency
The QoQZ evaluations are performed for the same QZ sizes as in-band QoQZ procedure, i.e., 15cm and 30cm
The measurement grid for the QoQZ evaluation for spurious emissions is the same as for in-band MOP TRP test cases.
The QoQZ evaluation for spurious emissions is performed at the same 7 reference positions as for in-band QoQZ evaluation
The reference antennas used for the QoQZ validations in the spurious emissions domain shall have a HPBW of ≥ 20o in E-Plane and H-Plane.