## Slide 1: NR TT Way Forward update
3GPP TSG-RAN WG5 5G NR AH #4
Singapore, Singapore, 21st – 25th January 2019
R5-190257
Telecom Italia

## Slide 2: Background FR1
At RAN5#79 the Maximum Test System Uncertainty for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952
At RAN5#79 a Way Forward on FR1 TTs for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952 (Except the FFS items)
At RAN5#80 New FR1 MU values introduced in R5-184484 for the following TCs: 6.3.4.2, 6.3.4.3, 6.3.4.4, 6.4.2.1, 6.4.2.2, 6.4.2.3, 6.4.2.4. New TT values agreed based on the WF assumption in R5-185564
At RAN5#80 RAN5 also agreed to maintain the document until the TT for FR1 and FR2 are finalized
At RAN5 5G-AH#3 a WF for FR1 NSA in TS 38.521-3 has been agreed in R5-185657
At RAN5#81 an update has been presented in R5-187813

## Slide 3: Background FR2
At RAN5 5G-AH#3 New FR2 MU values for IFF method introduced in R5-186344
At RAN5#81 the following contribution regarding TT are presented:
  R5-186888: proposing TT = 0 and highlight Network coverage impact
  R5-187576: defining upper bound for TTs (TT = 2.1 dB)
  R5-187568: proposing basically TT = 0.65xMU
  R5-187235: proposing basically TT = 0.82xMU
At RAN5 RAN5#81 a WF for FR2 in TS 38.521-2 is agreed in R5-188058
MU update in R5-188224 and R5-188225

## Slide 4: Agreed FR1 Way Forward: TT < MU
At RAN5#79 TT WF agreed in R5-183952
WF: Except the FFS Items, the proposed FR1 TT Values are included in the spreadsheet file, based on the following assumption:
  The SA FR1 TT values should not exceed the value adopted in pure LTE (TS 36.521-1 BW ≤ 20 MHz f ≤ 4.2 GHz). It is assumed that the amount of uncertainty exceeding the E-UTRAN shall not be considered.

## Slide 5: Agreed FR1 NSA WF TS 38.521-3
At 5G-AH#3 RAN5 agreed NSA MU in R5-185641
At 5G-AH#3 RAN5 agreed WF in R5-185657 for TS 38.521-3 FR1 EN-DC as follow:
  In case TTLTE, TTSA = 0, TTNSA to be defined as zero.
  In case MUNSA = MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.
  In case MUNSA > MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.

## Slide 6: Agreed FR2 WF TS 38.521-2
Except the FFS and empty items, the proposed FR2 TT Values are included in the spreadsheet file, based on the following assumption:
TTs shall be defined case by case
TT = 0.65 * MU (the upper bound of MU value used for TT calculation is 5.5 dB, 0.65 upper bound TT/MU ratio)
  Applies to following Test Cases:
    Min Peak EIRP
    Max TRP
    Reference Sensitivity
TT = 0.50 * MU (the upper bound of MU value used for TT calculation is 0.01ppm , 0.5 upper bound TT/MU ratio)
  Applies to following Test Cases:
    Frequency error
TT = MU for ACLR and SEM it will be updated when the related MU will be finalized
since TT have dependency from MU, no TT value can be defined if the corresponding MU is not finalized (business as usual).
TT values may decrease based on the experience on the field and when all parties will have more confidence in device performance
The TT values and the method to derive the TT defined until RAN5#85 (November 2019) for execution in any possible certification. At RAN5#85 the TT values shall be re-evaluated
  Required actions are specified in editor’s note in Annex F

## Slide 7: Attached Spreadsheets update
TS 38.521-1 SA FR1 TT
  Introduces the still missing UL-MIMO Test cases and minor few TC alignment.
TS 38.521-2 SA FR2 TT
  MU values from R5-188224 and R5-188225.
  TT values from R5-188058 (WF), R5-187576 (low PSD) and R5-186335 (OBW).
TS 38.521-3 NSA FR1 TT
  Added missing Test Cases