## Slide 1: WF MU Threshold
[Qualcomm, Ericsson, Orange, Verizon, Dish, AT&T, Huawei, CMCC, Vodafone]

## Slide 2: Background
In the interest of 5G NR to evolve and become better going ahead, its important to evolve in every aspect.
The understanding to set in stone the MU values and not change them going forward for a long time is detrimental to the 5G NR industry.
RAN5 would like to thank the TE vendors to bring in great contributions towards MU elements for various areas, but would also like to pave a way forward for these values to evolve and become better.
Two Contributions were presented in this meeting: R5-190532r1 & R5-190614, that raises this very concern of not keeping the current large MU values unchanged, but rather working towards to make them smaller and better.

## Slide 3: Problem Understanding
These large MU values will be applied towards OEM and UE validation.
Large MU will result
  Large variance in measurements
  Inaccurate link budget and coverage stats
  Incorrect probability-of-failure tolerance
  Difficult to distinguish bad DUT’s from good DUT’s, will lead bad DUT’s to Pass
Impact is long-term, and cannot “fix” the above problems later once a test laboratory makes the investment and gets certified with “compliant” TE’s.
R5-190614 gives an example of how the large MU value makes the EIRP range so high
RAN4 PC3 UE in specs (GHz) | Minimum spherical EIRP in dBm from 38.101-2 | Standard uncertainty (σ) [dB] from Table B.3.2-2 in 38.903 | Agreed TT Value | Possible range of outcome EIRP measurement
N260 (39GHz) | 8.00 | 4.78 | 0.65*MU | 4.893~11.107
N261 (28GHz) | 11.5 | 4.41 | 0.65*MU | 8.634~14.366

## Slide 4: Way Forward
Define MU Threshold for various Tx & Rx tests, that’s lower than the current MU values of 38.903
As an example, R5-190614 suggests the following for EIRP (using 0.7 as scaling factor):
Frequency | MBW | Power | Aperture size | MU threshold
23.45GHz <= f <= 32.125GHz | BW <= 400MHz | P = Max Output Power | D <= 5cm | 3.10
 |  |  | 5cm < D <= 15cm | FFS
32.125GHz < f <= 40.8GHz |  |  | D <= 5cm | 3.40
 |  |  | 5cm < D <= 15cm | FFS

## Slide 5: Way Forward - Agreements
Observation 1: RAN5 agrees current FR2 MU values are very large, and for reasons explained earlier, work towards reducing them to make 5G NR eco-system better.
Proposal 1:RAN5 defines all FFS MU Thresholds in TR 38.903 Annex B.x for each test to be lesser than current derived MU values. Include MU threshold table with FFS values in TS38.521-2 Annex F.1.2 & F.1.3.
Proposal 2: Use the current MU derived values to determine test requirements in TS38.521-2 for an interim period of [xx] meetings until the MU derived values meet the MU threshold values.

## Slide 6: References
TR 38.903
TS 38.521-2
R5-190614
R5-190532r1