## Slide 1: Test frequency calculation tool
Implemented in Python
R5-250637r1
3GPP TSG-RAN5 Meeting #106
Athens, February 17 – 21 2025

## Slide 2: Supported Functionality of the Tool
Python tool
User input (GUI)
( Configuration, Band, SCS, UL/DL -> Table )
3GPP Tables
(38.101, 38.213, 38.508)
3GPP parameters, hard coded in python.
(38.101, 38.213, 38.508)
3GPP Tables, coded in python.
(38.101, 38.508)
Manual insertion
Input parameters in CSV format, as a reference.
Single Freq
TDD, FDD, FR1, FR2
Intra CA Contiguous
TDD, FR1, FR2
Intra CA Noncontiguous UL, TDD, FR1
More Types
DL
DL&UL
Possibly in JSON format, outside python.
More Types
Test frequencies and Coreset#0 in CSV format.
SSB and Coreset#0 Calculation

## Slide 3: Added configuration types since Ran5#105 meeting.
C.2.2: Determination of test frequencies for asymmetric NR bands and symmetric uplink and downlink channel bandwidth combinations.
C.2.3: Determination of test frequencies for asymmetric uplink and downlink channel bandwidth combinations.
C.2.1.1: Determination of test frequencies for Low-, Mid- and High-Range, for UL testfrequencies (FDD Bands)

## Slide 4: Added 3GPP tables in JSON format.
38.101-1, table 5.3.5-1

## Slide 5: What configuration types does the tool support at this stage? (38.508-1, Annex C)
C.3: Determination of SSB and CORESET#0
C.2.1.1: Determination of test frequencies for Low-, Mid- and High-Range, (FR1, FR2, FDD, TDD).
C.2.4.2.2: Determination of test frequencies for Low-, Mid- and High-Range, for NR Intra-band Contiguous CA, FR1 and FR2, for 2 carriers only.
C.2.4.3: Determination of test frequencies for NR Intra-band Non-Contiguous CA , only FR1, only 2 carriers.
C.2.2: Determination of test frequencies for asymmetric NR bands and symmetric uplink and downlink channel bandwidth combinations.
C.2.3: Determination of test frequencies for asymmetric uplink and downlink channel bandwidth combinations.

## Slide 6: What is not supported in 38.508-1, at this stage?
Potentially all clauses above are possible to implement.
Further studies are required.
C.2.1.2: Determination test frequencies for Mid-Low and Mid-High-Range for signalling tests.
C.2.4.2A: Determination of test frequencies for FR1 NR Intra-band Contiguous CA without UL CA for bands with uplink bandwidth less than downlink bandwidth.
C.2.5: Frequency determination for supplemental uplink.
C.2.6: Frequency determination for EN-DC configurations.
C.4: Determination of SSB and CORESET#0 for RRM testing with SSB SCS 120 kHz and 240 kHz.

## Slide 7: What is next?
RAN4 are developing a tool to verify CRs related to CA configurations. A part of that work is to represent needed tables in 38.101 in a machine readable format. The format used is JSON.
See related doc: RP-242483
To make the “Test Frequency Calculation Tool” generic for any band/configuration without updating the python tool for every band/configuration, there is a need of access to a number of machine readable tables.
Some of the needed tables will be implemented by RAN4 and some tables, that is needed for the “Test Frequency Calculation Tool” might not be in the plan to be implemented to support the RAN4 tool.
The next step for the “Test Frequency Calculation Tool” is to modify the tool to use the RAN4 database, containing machine readable tables and also, if needed, add the tables that is missing for the “Test Frequency Calculation Tool”, into the database.
If there is a need of additional tables, it needs to be discussed with the RAN4 group!
Note! This future improvement does not prevent RAN5 from introducing the tool at this point.

## Slide 8: What is next?
Since the “Test Frequency Calculation Tool” also can be used for generating tables to be added into 38.508-1 and the bands/configurations that are implemented for that purpose also will be supported of the tool, there is a need to make it clear for the user which CA band combinations are allowed to be used for calculating missing BW combinations in 38.508-1.
Two options to solve it is:
Two different tools depending on usage.
One tool with initial choice:
  Calculate missing BW combinations in 38.508. (According to Note in table)
  Calculate BW combinations for CR.
Suggestion for solution to be prepared for RAN#107

## Slide 9: How to make the tool a part of the standard?
The tool will be made a part of the standard by adding a note to the tables that have an intentional reduction of BW combinations. See suggested note below:
NoteX: This table does not include all possible BWdth combinations for this configuration. A python tool to calculate missing BW combinations can be found in the following repository of 3GPP Forge:
https://forge.3gpp.org/rep/ran5/xxxxx

## Slide 10: Proposal 1
Make this python tool a part of the standard to support calculations of test frequencies that is not added in test frequency tables due to too many bandwidth combinations.