## Slide 1: Discussion on TT denotation for EN-DC Refsens test requirements
ZTE Corporation
3GPP TSG-RAN5 Meeting #107 R5-252835
St Julian’s, Malta, May 19 – 23, 2025

## Slide 2: Overview on test requirements for EN-DC Refsens
In last RAN5 meeting, a discussion paper on EN-DC Refsens test requirements handling was raised in [1]. The formats of “xx+TT” or “xx” in test requirement table were discussed. For EN-DC Refsens test requirements in Table 7.3B.2.3.5-0 and Table 7.3B.2.3.5-4, it is observed that for dual uplink operation the Refsens values are using different formats , some of which with “xx” while some others with “xx+TT”.
Observation 1 For EN-DC Refsens test requirements, the NR band part uses “xx+TT” format where TT is defined in Table 7.3B.2.3.5-1a; the E-UTRA band part uses “xx” format where TT is implicitly included in “xx”.
Table 7.3B.2.3.5-1a: Test Tolerance (TT) for RX sensitivity level
NR or E-UTRA Band / Channel bandwidth |  |  |  |  |  |  |  |  | 
EN-DC Configuration | EUTRA or NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | IMD order | Duplex mode
… | … | … | … | … | … | … | … | … | …
DC_3A_n7A | 3 | N/A | REFSENS | - | - | - | - | - | 
 | n7 | 15 | - | -84.6 +TT5 | - | - | - | - | 
DC_3A_n8A | 3 | N/A | - | REFSENS | - | - | - | N/A | FDD
 | n8 | 15 | -88.3 | - | - | - | - | IMD43 | FDD
 | 3 | N/A | - | -86.9 | - | - | - | IMD5 | FDD
 | n8 | 15 | REFSENS | - | - | - | - | N/A | FDD
Table 7.3B.2.3.5-4: Reference sensitivity exceptions due to dual uplink operation for PC3 EN-DC in NR FR1 (two bands)
“xx+TT” where TT is defined in Table 7.3B.2.3.5-1a for NR part
References
[1] R5-251699, Further discussion on EN-DC Refsens test requirements handling, ZTE, RAN5#106
“xx” where TT is not explicitly denoted for E-UTRA part due to TT already included in Table 7.3.5-1 of TS 36.521-1
TT for E-UTRA band Refsens implicitly included in the test requirements for single band
f ≤ 3.0GHz | 3.0GHz < f ≤ 6.0 GHz
0.7 dB | 1.0 dB

## Slide 3: Test requirements for EN-DC Refsens for NR part
However, in the following examples for dual uplink operation for two bands and three bands EN-DC configurations have different formats for NR part, some in “xx” and the others in “xx+TT”. Some values for EN-DC Refsens test requirements are not correct and it makes people confusion whether TT is missing by accident or already included in “xx” due to different TT denotation used.
Observation 2 For EN-DC Refsens test requirements, different formats of “xx” and “xx+TT” have been used for NR band part.
Observation 3 The TT defined in Table 7.3B.2.3.5-1a for some NR bands has not been referenced by EN-DC Refsens test requirements. It makes people confusion whether TT is missing by accident or already included in “xx”
f ≤ 3.0GHz | 3.0GHz < f ≤ 6.0 GHz
0.7 dB | 1.0 dB
Table 7.3B.2.3.5-1a: Test Tolerance (TT) for RX sensitivity level
NR or E-UTRA Band / Channel bandwidth |  |  |  |  |  |  |  |  | 
EN-DC Configuration | EUTRA or NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | IMD order | Duplex mode
… | … | … | … | … | … | … | … | … | …
DC_3A_n7A | 3 | N/A | REFSENS | - | - | - | - | - | 
 | n7 | 15 | - | -84.6 +TT5 | - | - | - | - | 
DC_3A_n8A | 3 | N/A | - | REFSENS | - | - | - | N/A | FDD
 | n8 | 15 | -88.3 | - | - | - | - | IMD43 | FDD
 | 3 | N/A | - | -86.9 | - | - | - | IMD5 | FDD
 | n8 | 15 | REFSENS | - | - | - | - | N/A | FDD
Table 7.3B.2.3.5-4: Reference sensitivity exceptions due to dual uplink operation for PC3 EN-DC in NR FR1 (two bands)
“xx+TT” where
xx = -94.8+10.2(MSD)
= -84.6 dBm
“xx” where
xx = -97.0+8.0(MSD)+0.7(TT) = -88.3 dBm
EN-DC Configuration | Test ID | EUTRA/ NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | Duplex mode | IMD order | Single UL allowed
… |  |  |  |  |  |  |  |  |  | 
DC_1A_n28A-n78A | 1 | 1 | N/A | REFSENS | - | - | - | FDD | N/A | 
 |  | n28 | 15 | REFSENS | - | - | - | FDD | N/A | 
 |  | n78 | 15 | - | -79.1 | - | - | TDD | IMD3 | 
 | 2 | 1 | N/A | REFSENS | - | - | - | FDD | N/A | 
 |  | n78 | 15 | - | REFSENS | - | - | TDD | N/A | 
 |  | n28 | 15 | -94.5 | - | - | - | FDD | IMD5 | 
… |  |  |  |  |  |  |  |  |  | 
Table 7.3B.2.3_1.1.5-1: Reference sensitivity exceptions for Scell due to dual uplink operation for PC3 EN-DC in NR FR1 (three bands)
“xx” where
xx = -95.8+15.7(MSD)+1.0(TT) = -79.1 dBm
“xx” where
xx = -98.5+4.2(MSD)+0.7(TT)
= -93.6 dBm, which is incorrect!

## Slide 4: Rules for TT denotation in EN-DC Refsens test requirements
To avoiding the above mentioned confusion on TT denotation in EN-DC Refsens test requirements, it is suggested to have the following rules on TT denotation for E-UTRA band and NR band respectively.
Proposal 1 For E-UTRA band Refsens test requirements in EN-DC configuration, it is suggested to use “xx” format, where xx is the direct value in which TT implicitly included in Table 7.3.5-1 in TS 36.521-1.
Proposal 2 For NR band Refsens test requirements in EN-DC configuration, it is suggested to use “xx+TT” format, where TT is referenced to Table 7.3B.2.3.5-1a explicitly.
Proposal 3 Check the current NR band Refsens test requirements in EN-DC configuration, if “xx” format is used, change it to “xx+TT” format. If the values in “xx” and “xx+TT” are different, change it in separate CR case by case.
f ≤ 3.0GHz | 3.0GHz < f ≤ 6.0 GHz
0.7 dB | 1.0 dB
Table 7.3B.2.3.5-1a: Test Tolerance (TT) for RX sensitivity level
NR or E-UTRA Band / Channel bandwidth |  |  |  |  |  |  |  |  | 
EN-DC Configuration | EUTRA or NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | IMD order | Duplex mode
… | … | … | … | … | … | … | … | … | …
DC_3A_n7A | 3 | N/A | REFSENS | - | - | - | - | - | 
 | n7 | 15 | - | -84.6 +TT5 | - | - | - | - | 
DC_3A_n8A | 3 | N/A | - | REFSENS | - | - | - | N/A | FDD
 | n8 | 15 | -88.3 | - | - | - | - | IMD43 | FDD
 | 3 | N/A | - | -86.9 | - | - | - | IMD5 | FDD
 | n8 | 15 | REFSENS | - | - | - | - | N/A | FDD
Table 7.3B.2.3.5-4: Reference sensitivity exceptions due to dual uplink operation for PC3 EN-DC in NR FR1 (two bands)
Change to “xx+TT” format as
“-89.0+TT”
EN-DC Configuration | Test ID | EUTRA/ NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | Duplex mode | IMD order | Single UL allowed
… |  |  |  |  |  |  |  |  |  | 
DC_1A_n28A-n78A | 1 | 1 | N/A | REFSENS | - | - | - | FDD | N/A | 
 |  | n28 | 15 | REFSENS | - | - | - | FDD | N/A | 
 |  | n78 | 15 | - | -79.1 | - | - | TDD | IMD3 | 
 | 2 | 1 | N/A | REFSENS | - | - | - | FDD | N/A | 
 |  | n78 | 15 | - | REFSENS | - | - | TDD | N/A | 
 |  | n28 | 15 | -94.5 | - | - | - | FDD | IMD5 | 
… |  |  |  |  |  |  |  |  |  | 
Table 7.3B.2.3_1.1.5-1: Reference sensitivity exceptions for Scell due to dual uplink operation for PC3 EN-DC in NR FR1 (three bands)
Wrong value in “xx” format should be corrected by using “xx+TT” format!
Change to “xx+TT” format as
“-80.1+TT”

## Slide 5: Thank you!