## Slide 1: D2D ProSe: Test Model and ASPs updates
3GPP RAN5 – TF160 & SS Vendors Workshop #32 21st Jan 2016
R5w160002r1 MCC TF160

## Slide 2: ASP changes since workshop#31
  ASPs used to report SLSS for Discovery and SLSS/MIB-SL for Communication have been updated to use the Start/Stop method. This will avoid overloading SS-UE and TTCN with too many messages
    SS-UE reports an indication every time when SLSS/MIB-SL reception from UE has toggled in the subframes configured for SLSS/MIB-SL reception:
      No SLSS/MIB-SL reception -> SLSS/MIB-SL reception or
      SLSS/MIB-SL reception -> No SLSS/MIB-SL reception
RRC asn.1 types were used to configure SS-UE (noted with FFS), new asn.1 types have been created to provide to SS-UE with only the necessary fields
SS-UE is initially configured as ON as it is not transmitting
Other editorial

## Slide 3: DISCOVERY ASP changes since workshop#31
Discovery configuration ASPs have been reorganised so that SyncRef are provided together with Tx or Rx parameters
New index type SL_TF_IndexPairList_r12b (added in 36.331vc70) added for type 2B
Simplify EnquireTiming with UTC ASP, the following sequence can be applied
  UTC time to be retrieved by TTCN using fx_GetSystemTime, then
  EnquireTiming to be used to retrieve SFN/Subframe
  The tolerance will be in an acceptable range for DISCOVERY transmission
SL_DATA_REQ: to facilitate the retransmission calculations for SS it is proposed to provide:
  N_PSDCH (resource index)
  The number of discovery periods to transmit
  The SFN/Subframe of the first discovery period
  This is also nearer from procedures defined in 36.321 and 36.213
All ASP changes have been delivered in the draft mini test suite except SL_DATA_REQ

## Slide 4: DISCOVERY - UL data clashes 1/2
The prose is still under discussion but it seems that we could have the requirement for SS-UE to transmit continuously, including during UE signalling procedures. There will be discussion at RAN5#70
So we could have possible clashes between Uu and PC5 transmissions on PSDCH and PUSCH/PRACH/PUCCH
In addition in case of failure, UE may transmit signalling while SS-UE transmits PC5_DISCOVERY on the same UL resource.
  In SIB19, 24 PRBs are allocated in 2 subframes per discovery period of 320ms => the probability for it to happen is low
It can only happen in monitoring test cases

## Slide 5: DISCOVERY - UL data clashes 2/2
  The default configured UL grant is I_MCS = 9 and N_PRB = 25
It is proposed to change the UL grant:
  To I_MCS = 9 and N_PRB=19 => TB=2984
  Keep the 4 PRB index from 19 to 22 for PC5
  CR required on 36.508 to modify SIB19 Rx pool. The subframe bitmap could be extended.
Transmission of PC5_DISCOVERY message may also be affected. The continuous transmission can be handled in the sidelink PTC

## Slide 6: COMMUNICATION - UL data clashes
Clashes between PSCCH/PSSCH/PSBCH and PRACH/PUCCH/PUSCH may also occur in failure cases
It can happen only in test cases in which SS-UE transmits
In the prose, there is currently no requirement for SS-UE transmission during UE signalling

## Slide 7: COMMUNICATION- Type 1 - DCI format 5
According to 36.213, SL-RNTI can be on common or UE specific search space for PDCCH and UE specific for ePDCCH
  It is proposed to use the UE specific search space
For FDD, 2 candidates are defined in 36.523-3 cl 7.1.1 for DL C-RNTI and UL C-RNTI
For TDD, UE-specific search space aggregation L=8 results in 2 PDCCH candidates.
So there isn’t enough candidates for UL/DL C-RNTI and SL-RNTI in the same subframe in UE-specific search space.
It is proposed to set a limitation: UL scheduled transmissions on C-RNTI and SL-RNTI is not considered for default CCE management

## Slide 8: COMMUNICATION - PDCP test model
The PDCP Data PDU for SLRB, defined in 36.323 cl 6.2.10, is using an SN field of size 16bits. This value shall be added in PDCP_SNLength_Type
type enumerated PDCP_SNLength_Type {
// PDCP Sequence Number
PDCP_SNLength5, // TS 36.323 clause 6.2.2
PDCP_SNLength7, // TS 36.323 clause 6.2.3
PDCP_SNLength12, // TS 36.323 clause 6.2.4
PDCP_SNLength16 // TS 36.323 clause 6.2.10
};
The security type SL_CipheringStartRestart_Type is clarified:
  Group Member ID and Group ID are already provided when configuring SL-DCH and STCH. There is no need to duplicate the information.
  Initialisation in the security test cases can be done using the generic procedure or using a USIM. To allow both methods we shall provide the PGK/PGK Id instead of PMK/PMK Id