## Slide 1: RRC Connection Resume Procedure test cases in NB-IoT
RAN5 TTCN Workshop #40 Rohde & Schwarz
R5w180010

## Slide 2: RRC Connection Resume Procedure in NB-IoT
RRC Connection Resume procedure is used in NB-IoT test cases 22.3.3.5, 22.4.15, 22.4.16
There are discussion ongoing in core group to clarify the support of early contention resolution.
RRCConnectionResume-NB message is a DL DCCH message and therefore cannot be sent on SRB0.
Depending on the agreement reached, if early contention resolution is not supported for NB-IoT, then TTCN needs to ensure that RRCConnectionResume-NB is provided to the SS as part of the “ContentionResolution_ContainedRlcPdu_Type”.
In order to facilitate SS implementation we would like to request for a test model change to identify if the RlcPdu provided is a CCCH or DCCH message.

## Slide 3: Current ASP definition for ContentionResolution_ContainedRlcPdu_Type
type union ContentionResolution_ContainedRlcPdu_Type {
octetstring RlcPdu, /* octetstring of an RLC PDU containing e.g. the RRC Connection Setup;
* to be sent in the same MAC PDU as the MAC Contention Resolution Control Element */
Null_Type None /* MAC PDU containing the MAC Contention Resolution Control Element does not contain an RLC PDU * (i.e. RRC Connection Setup is sent in another PDU) */
};
In order to facilitate SS implementation we would like to request for a test model change to identify if the RlcPdu provided is a CCCH or DCCH message.