## Slide 1: Upper Tester Issues
On the reproducibility of test results …
3GPP RAN5 TTCN Workshop #40 08 Feb. 2018 (R5w180011)

## Slide 2: Overview
There are 3 scenarios with UT commands which currently create problems :
  Race conditions with signalling
  Sequencing of UT commands
  UT commands triggering actions potentially taking significant amount of time
Test results … possibly not systematically reproducible
  failures
  inconsistent behaviours
These problems are explained using placeholder examples, and remedies/countermeasures are proposed
Problems and proposed remedies should be discussed

## Slide 3: Race conditions with signalling
36.523-3 Annex E.2: "TTCN needs an immediate response as a trigger to continue e.g. with DL signalling or starting a timer. In general there is no signalling in between UT_COMMON_CMD and UT_COMMON_CNF.“
In TC 9.2.2.1.2

## Slide 4: Race conditions with signalling
A UE presenting signalling before the UT response will fail the test ! Such UE signalling behaviour is conformant and therefore needs tobe accounted for!
In this simple case it will be sufficient not to wait for the UT response in order to avoid the race condition [UT command to be changed] ”In the TTCN, a confirmation shall only be requested in cases when there is no signalling from the UE being triggered by the MMI/AT command” (36.523-3 cl. 5.2)”
Alternatively interleaving could be introduced which handles UT response and signalling [interleave to be added]

## Slide 5: Sequencing of UT commands
36.523-3 Annex E.2. assumes the UT functionality to be stateless
UT command sequences may cause ambiguous results
In TC 22.5.17

## Slide 6: Sequencing of UT commands
As the UT functionality is stateless the UE response upon Switching On may be handled and passed as response upon configuring PSM if this command were confirmed
All UT commands in a sequence except the last one should be confirmed !
Unclear what happens if a UT command in a sequence is unconfirmed.
  Would it help to apply a delay ?
  Should a “Confirmed” variant be created ?

## Slide 7: UT commands triggering actions taking significant amount of time
In TC 6.1.2.9a

## Slide 8: UT commands triggering actions taking significant amount of time
The sequence may work fine … but if the Automatic PLMN selection is not "completed" when the power level change happens, then the search process will be (re)started. While traversing the cells in question other cells will not be "seen" and SystemInformation will be missed.
Automatic PLMN selection is the default and therefore the test case prose is redundant …
Automatic PLMN selection could be activated in a similar way as shown in the example taken from 22.5.17. See also 6.1.1.4 as an example …
Note: This will impact quite a number of test cases … 6.1.1.4a, 6.1.2.9, 6.1.2.9a, 22.2.6, 22.2.7, ….

## Slide 9: Proposed way forward
Discuss the described issues / conclude as far as possible i.e. define action points as needed
Add text / examples to Annex E.2 resp. coding conventions
Identify changes to be done to the TC prose
Assign analysis of remaining open issues
Establish CRs as required