## Slide 1: NR ASPs: Clarification of Rlc Bearer Routing Info
ETSI / SS Vendors TTCN workshop#44 R5w190114
16/04/2019
Shaun Harry

## Slide 2: RlcBearerRouting field
The field RlcBearerRouting is present in the common part of NR REQ/IND ASPs and optionally present in the common part of EUTRA REQ/IND ASPs (type DC_RlcBearerRouting) with choices “EUTRA”, “NR” and “None”.
The semantics are currently defined as:
    type union DC_RlcBearerRouting_Type { /* data routing e.g. in case of split bearer (split DRB or split SRB);
    applicable for multi-RAT Dual Connectivity (MR-DC) as well as single-RAT Dual Connectivity */
    EUTRA_CellId_Type EUTRA,
    NR_CellId_Type NR,
    Null_Type None /* normal case: PDCP and RLC are configured at the same cell */
    };
  Indicates data transfer on a non-split bearer should use “None” option.
  This is currently not used consistently across TTCN test cases and test suites, leading to difficulties with SS implementation.

## Slide 3: Examples of current TTCN usage
 | REQ ASP | IND ASP
NR SCG DRB data (EN-DC test suite) | “None” (8.2.2.4.1) “NR” (8.2.2.7.1) “NR” (L2 test cases) | “None” (8.2.2.4.1) “NR” (8.2.2.7.1) “NR” (L2 test cases)
EUTRA MCG DRB Data (EN-DC test suite) | “EUTRA” (8.2.2.7.1) | “EUTRA” (8.2.2.7.1)
EUTRA SRB (EN-DC and legacy test suites) | omit | *
NR SRB (NR5GC test suite) | “None” | “None”
NR DRB (NR5GC test suite) | “None” | “None”

## Slide 4: Current usage of RlcBearerRouting field in TTCN (19wk12)
EN-DC test suite
  Inconsistent usage e.g.:
  Test case 8.2.2.4.1 uses “None” in NR_DRB_DATA_REQ and NR_DRB_DATA_IND
  Test case 8.2.2.7.1 uses “NR” and “EUTRA” in all data check steps, including those where the bearer is non-split (e.g. steps 6 and 12)
  7-series test cases use “NR” when sending and receiving on SCG
  For EUTRA signalling on non-split SRB (SRB_COMMON_REQ/_IND) “omit” and “*” are used
NR5GC test suite uses “None” for all SRB and DRB transfer.

## Slide 5: Proposals
Clarify semantics and align TTCN usage / expectation for RlcBearerRouingField
  Option 1
    “NR” and “EUTRA” choices are only used in split bearer configurations
    “None” is used for non-split bearer data and non-data related ASPs
    As per current description in type definition
  Option 2
    “NR” and “EUTRA” choices always used for data-related ASPs to indicate the used RLC type and cell ID (irrespective of split / non-split bearer)
    For backwards compatibility in EUTRA ASPs, “omit” and “*” could also be used for non-split bearers
    “None” to be used only for non-data related ASPs (e.g. NR_SYSTEM_CTRL_REQ)
  Option 3
    Clarify that both options are allowed (e.g. for non-split NR bearer TTCN can specify “NR” or “None” and will accept either value from SS)
  Keysight preference is for option 2 to allow for slightly simpler SS implementation.