## Slide 1: 5G NR Test Model: Selection criteria for LRBs / IMCS with given Uplink TBS
3GPP RAN5 TTCN Workshop #45
16 April 2019, ETSI
R5w190116

## Slide 2: Problem statement
For creation of Uplink TBS tables, TS 38.523-3 Annex B.2 currently refers to the criteria specified in subclause 7.1.2.2.4.2 for selection of an LRBs / IMCS pair in Downlink:
R5w190108 describes in Observation 1…4 those cases, which leave more than one LRBs / IMCS candidate pair after having applied [Rule A]. These are exactly the cornercases when switching to a higher modulation order.

## Slide 3: Discussion
TF160‘s view, that option „max. IMCS“ was preferable as [RuleB] because it would lead to a lower coding rate and thus provides more redundancy of data bits onto the physical channel symbols, is not shared by our PHY experts.
Reason: see Matlab simulation  A higher modulation order requires a higher SNR for reliable symbol decoding after FEC. This nullifies (if not exceeds) the apparent advantage mentioned above. Especially in OTA environment (=FR2) with its high MU, a large SNR cannot be guaranteed for TC designs with tight decision margins (e.g. meas. reporting). This may cause instability of test results.

## Slide 4: Discussion: SNR vs. BER relationship shown in IQ constellation diagram
Conclusion: at the same SNR, a higher modulation depth is related to higher BER red dot = ideal constellation, black dots = statistical location of data points with noise

## Slide 5: Conclusion
R&S prefer to use minimum IMCS as selection criteria for the second stage [RuleB]. TS 38.523-3 Annex B.2 would read: