## Slide 1: 5G AKA Procedure
ETSI / SS Vendors TTCN workshop#44 R5w190117
16/04/2019
Shaun Harry

## Slide 2: 5G AKA procedure
TTCN / SS ME USIM
-------AUTHENTICATION REQUEST (RAND, AUTN)-------------
Calculate XRES and XRES* -----RAND, AUTN
Calculate RES
----RES-------------
RES ->RES*
--AUTHENTICATION RESPONSE (RES*)---------------------------
Check XRES* = RES*

## Slide 3: 5G AKA procedure
24.501 9.11.3.17 -> 24.301 9.9.3.4 :
    “In an EPS authentication challenge, the response calculated in the USIM (RES) is minimum 4 octets and may be up to 16 octets in length.
    In a 5G AKA authentication challenge, the response calculated in the ME (RES*) is 16 octets in length.”
RES (variable length) is calculated by USIM and mapped to RES* (fixed length) by ME
  33.501 6.1.3.20 :
    “the USIM computes a response RES…. The ME then shall compute RES* from RES according to Annex A.4”
  33.501 A.4:
    “L2 = length RES or XRES (i.e. variable length between 0x00 0x04 and 0x00 0x10).”
  33.102 6.3.7:
    The authentication response (RES) shall have a variable length of 4‑16 octets.

## Slide 4: 5G AKA failures
  USIM returns RES value which is variable length (4-16 octets) but only RES* is signalled back to the TTCN which is fixed length (16 octets)
  So TTCN cannot know the length of RES produced by the USIM (unlike for EPC authentication)
  TTCN currently assume XRES length 16 octets when calculating XRES*
  Authentication will fail if the USIM produces a shorter RES value.
  Length of RES is not currently mandated although 34.108 8.1.2.1. has “NOTE:Suggested length for RES is 128 bits (i.e. n = 127).”

## Slide 5: Proposals
  Option 1
    Update prose to mandate 128-bit RES for test USIM
    Restricts test USIM implementation
  Option 2
    Introduction of new PIXIT parameter for XRES length
  Option 3
    TTCN derives XRES* for all possible lengths of RES (4 octets -> 16 octets) and matches each against received RES*