## Slide 1: ASP proposal for Delta Values (FR2)
Ram Thiruvathirai
TTCN Workshop#47
R5w190312

## Slide 2: Current Implementation
For FR2 testing, test operator needs to provide the ∆(f) (defined in TS 38.508-1 [5] subclause 6.1.3.4) values of each NR frequency.
Current implementation uses pixits px_NR_PrimaryBandDeltaNRfx / px_NR_SecondaryBandDeltaNRfx (see TS 38.523-3 Table 9.2-1) to derive this information and the threshold values are updated accordingly.
The delta values will be different for each primary / secondary frequency band associated with the test and therefore will hold different values depending on band under test.
FR2 work is still under progress and there are several open issues ( multi cell / 2 or more LTE cells / CA ) and the current implementation will require more and more pixit updates.
The document proposes an alternate solution for providing the delta ∆(f) values to TTCN.

## Slide 3: Proposal
delta ∆(f) values needs to be provided at the start of test cases so that TTCN can update the threshold values accordingly.
It is proposed to use ASPs to request for the delta ∆(f) values for the band under test.
Proposal can be extended for other RATs if required.
It is left up to SS implementation as to how the calibrated delta ∆(f) values are provided to the ASP.
Please see attached document for ASP changes.
NR_BandforDelta_Type and UE_NR_DeltaValues_Type can further be extended based on new requirements.

## Slide 4: TTCN ASP sequence