## Slide 1: NR ASPs: Proposed Updates
ETSI / SS Vendors TTCN workshop#47 R5w190314
17/10/2019
Shaun Harry

## Slide 2: SDAP test mode configuration
When configuring SDAP for transparent mode, the SS needs to know if the UE is configured to include SDAP UL header in order to be able to decode received uplink SDAP PDUs
Propose adding SDAP_Header_Type (present, absent) in SDAP transparent mode configuration.
  type enumerated SDAP_Header_Type {
  Present,
  Absent
  };
  …….
  type union SdapConfigInfo_Type {
  SdapConfig_Type SdapConfig, /* SDAP configuration parameters for the DRB */
  Null_Type TransparentMode
  SDAP_Header_Type TransparentMode /* SDAP configuration for transparent (test) mode, used for SDAP tests:
  * SS does not add any SDAP headers in DL and does not remove any SDAP headers in UL */
  };

## Slide 3: NR_SYSTEM_IND for MAC Control Element
When the SS is configured to forward MAC UL Control Elements to the TTCN, currently the NR_SYSTEM_IND type only allows the control element contents to be included in the ASP. The associated MAC subheader (including LCID and length) should also be included to allow the contents to be decoded.
This is needed especially for variable-length Control Elements e.g. Multiple Entry PHR (7.1.1.3.7 EN-DC)
Proposed to include NR_MAC_CE_SubPDU_UL_Type (including sub-header) in place of NR_MAC_ControlElementUL_Type
  type union NR_SystemIndication_Type {
  charstring Error, /* indicates an error situation in SS;
  * is not explicitly handled in TTCN but causes an INCONC due to default behaviour;
  * an additional error code can be signalled in the common part of the ASP;
  * SS shall raise an error when in TS 38.523-3 or in any other ASP definitions */
  NR_RlcDiscardInd_Type RlcDiscardInd, /* indicates discarded PDUs */
  NR_MAC_ControlElementUL_Type MAC,
  NR_MAC_CE_SubPDU_UL_Type MAC /* indicates MAC control element being receive from the UE */
  NR_RachPreamble_Type RachPreamble, /* RACH preamble being sent by the UE */
  Null_Type SchedReq, /* indication for scheduling request sent by the UE */
  HARQ_Type UL_HARQ, /* to report the UL HARQ as received on PUCCH or PUSCH for corresponding DL transmission */
  NR_HarqError_Type HarqError /* indicates detection of HARQ error:
  * 1. HARQ CRC error for UL data
  * 2. HARQ NACK from the UE unless SS is configured to report HARQ ACK/NACK */
  };