## Slide 1: Proposal on slice priority and slice group
SA#95 emeeting
China Mobile, ZTE, Nokia

## Slide 2
Background
  RAN2 defines Slice list and priority information for cell reselection in Rel-17 and send LS to SA2 to complete the E2E solution(S2-2107039).
  The latest LS sent from RAN2(R2-2203807) indicate:
    RAN2 understands whether per TA or per PLMN granularity has no major RAN2 impacts. However, RAN2 assumes (based on majority views in RAN2) that the mapping of slice to the slice groups for cell reselection is per TA.
    RAN2 also assumes that the NAS layer in the UE is able to provide slice group priorities to AS layer in the UE.
    RAN2 has achieved the following agreements:
      A slice is not associated with multiple slice groups for the same purpose within a slice to slice group mapping “granularity”. A slice can be associated at most with one slice group for RACH and with one slice group for reselection, within the same granularity.
      Both for RACH and for cell reselection, the UE NAS needs to provide the slice information to the UE AS. The UE AS is aware of the slice group ID (s) based on such slice information provided by the UE NAS.

## Slide 3: Proposal on network slice priority
Two sets of solutions are proposed in SA#95emeeting for network slice priority.
Option1) SP-220301 (Nokia, CMCC, NEC, Verizon UK ltd.,ZTE, InterDigital, Xiaomi)
  When the UE performs Network Slice based cell reselection and there is a need to prioritize the S-NSSAIs the UE may(if possible) prioritize the S-NSSAIs in a way outside the scope of 3GPP specification. The UE may trigger reselection when it changes set of network slices. The RAN provides network based Cell reselection priorities as usual and potentially per slice group(as per RAN2 CRs). RAN control of the cell reselection priorities is still there.
Option2) SP-220319(Ericsson)
  The NG-RAN may send network based NSAG priorities to the UE e.g. at RRC release. The NG-RAN determines the NSAG priorities based on e.g. Allowed NSSAI, RFSP and other available information at the NG-RAN. The UE uses the network based NSAG priorities for Network Slice based cell reselection until the UE NAS changes the priorities i.e. when suitable due to either of the following cases:
    A new Network Slice is to be registered in a Requested NSSAI;
    A PDU Session is to be established; or
    UL data is to be sent i.e. UP is to be activated for a PDU Session.
    Observation: Option2 about slice priority is a new proposal and seems not aligned with RAN2 CRs.
    Proposal : SoH about the two options above
  Option 1: support SP-220301
  Option 2: support SP-220319

## Slide 4: Proposal on Network Slice Access Stratum groups(NSASG or NSAG)
Two sets of solutions are proposed in SA#95emeeting for network slice access stratum groups.
1) SP-220302/220303/220312(Nokia, CMCC, NEC, Verizon UK ltd.,ZTE, InterDigital, Xiaomi)
  Per TA level to send the information to UE:
  The RAN provides the AMF with the values of the NSAG(s) an S-NSSAI is associated with, in a TA at NG Set Up and RAN Configuration Update procedures. The AMF in turn provides the supported NSAG per TAI to the NSSF.
  the AMF may configure a UE for some S-NSSAIs in the Configured NSSAI, with Network Slice Access Stratum (AS) Group (NSAG) Information
  The AMF shall indicate in the NSAG Information it provides to the UE in which TA a specific NSAG association to S-NSSAI(s) is valid if the same NSAG value is used in different TAs with a different association with NSSAIs.
  A S-NSSAI can be associated with one or more NSAG values.
2) SP-220317/220318/220316(Ericsson)
  Per PLMN level to send the information to UE:
  A UE supporting NSASG may store NSASG values corresponding to some S-NSSAIs in the Configured NSSAI of the Registered PLMN.
  If the UE supports NSASG and at least one S-NSSAI in the Configured NSSAI of the registered PLMN is associated with a NSASG, the NSSF may provide the NSASG. The association between S-NSSAI and NSASG is unique in the PLMN.
  NOTE:An S-NSSAI can be associated with multiple NSASGs.
Proposal : SoH about the two options above
  Option 1: The UE get the NSASG information per TA level. (SP-220302/220303)
  Option 2: The UE get the NSASG information per PLMN level.(SP-220317/220318)
  Option 3: Both per TA level and PLMN level are optional and can be supported.

## Slide 5: SA plenary CRs on slice priority/group
SP-220301 | CR | Approval | 23.501 CR3317R3 (Rel-17, 'B'): Enabling slice priority and slice groups for RRM purposes | Nokia, Nokia Shanghai Bell, CMCC, NEC, Verizon UK ltd.,ZTE, InterDigital, Xiaomi | Rel-17 | Revision of (Postponed) S2-2200508
SP-220302 | CR | Approval | 23.502 CR3300R2 (Rel-17, 'B'): Enabling configuration of Network Slice AS Groups | Nokia, Nokia Shanghai Bell, CMCC, NEC, Verizon UK ltd.,ZTE, InterDigital, Xiaomi | Rel-17 | Revision of (Postponed) S2-2200918
SP-220303 | CR | Approval | 23.501 CR3539R1 (Rel-17, 'B'): Enabling configuration of Network Slice AS Groups | Nokia, Nokia Shanghai Bell, CMCC, NEC, Verizon UK ltd, ZTE, InterDigital, Xiaomi | Rel-17 | Revision of (Postponed) S2-2200847
SP-220312 | DISCUSSION | Discussion | Discussion on Slice list and priority information for cell reselection | Nokia, Nokia Shanghai Bell, InterDigital | Rel-17 | 
SP-220316 | DISCUSSION | Approval | Discussion on Slice list and priority information for cell reselection | Nanjing Ericsson Panda Com Ltd | Rel-17 | 
SP-220317 | CR | Approval | 23.501 CR3482R1 (Rel-17, 'F'): Enabling Network Slice Access Stratum groups | Ericsson | Rel-17 | Revision of (Postponed) S2-2200280
SP-220318 | CR | Approval | 23.502 CR3334R1 (Rel-17, 'F'): Enabling Network Slice Acess stratum group | Ericsson | Rel-17 | Revision of (Postponed) S2-2200281
SP-220319 | CR | Approval | 23.501 CR3317R4 (Rel-17, 'B'): Enabling slice priority and slice groups for RRM purposes | Ericsson | Rel-17 | Revision of (Postponed) S2-2200508