3GPP TSG SA Meeting # 101 	SP-231016

Bengaluru, India, 11 -15 Sept 2023

# Source:	SA1 (from S1-232652)

# Title:	New WID on Ambient power-enabled Internet of Things

# Document for:	Approval

# Agenda Item:	6.3.1

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: Ambient power-enabled Internet of Things

## Acronym: AmbientIoT

## Unique identifier:	1010024

Potential target Release: Rel-19

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X | X | X |  |
| No |  |  |  |  |  |
| Don't know | X |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

### This work item is a …

|  | Study |
| --- | --- |
| X | Normative – Stage 1 |
|  | Normative – Stage 2 |
|  | Normative – Stage 3 |
|  | Normative – Other* |

* Other = e.g. testing

### 2.2	Parent Work Item

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| FS_AmbientIoT | SA1 | 950004 | Study on Ambient power-enabled Internet of Things |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

## 3	Justification

This work item is to specify service requirements for Ambient power-enabled Internet of Things.

Ambient power-enabled Internet of Things (Ambient power-enabled IoT) device is an IoT device powered by energy harvesting,  with limited battery or energy storage capability (e.g. using a capacitor) and the energy is provided through light, motion, heat, or any other power source that could be seen suitable. An Ambient IoT device may have low complexity, small size and lower capabilities and lower power consumption than previously defined 3GPP IoT devices (e.g. NB-IoT/eMTC devices). Ambient IoT devices can be maintenance free and can have long life span (e.g. more than 10 years).

The related study FS_AmbientIoT (TR22.840) has been carried out in SA1 addressing the service requirements from the following 4 use case groups:

- Inventory

- Sensors

- Positioning

- Actuators (e.g. switch)

As a new type of service provided by 5G, Ambient power-enabled IoT leads to new functional and performance requirements to the 5GS.

Specifically, the study shows that Ambient IoT use cases require new functional requirements, e.g. communication aspects of Ambient IoT devices/network, positioning of Ambient IoT devices, management of Ambient IoT devices, exposure of related network capabilities, of data collected by Ambient IoT devices and of information about Ambient IoT devices, charging and security and privacy.

The study also suggests new performance requirements in order to support Ambient IoT services, e.g. max. allowed end-to-end latency, communication service availability, user-experienced data rate, message size, device density, communication range and positioning accuracy.

## 4	Objective

The objective is to specify 5G system requirements and KPIs in order to support ambient power enabled IoT services. The service requirements include the following aspects related to Ambient power-enabled IoT:

- Communication,

- Positioning,

- Management,

- Exposure,

- Charging,

- Security and privacy.

Note 1: Specifics of how the device performs energy harvesting are not in the scope of this work.

Note 2: KPIs should be further evaluated, including RAN feedback.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Rapporteur |
| TS | 22.XXX | Service requirements for Ambient power-enabled IoT | SA#101 | SA#102 | Xu, weijie, OPPO, xuweijie@oppo.com |

| Impacted existing TS/TR |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 22.261 | Adding of new section pointing out to new TS | SA#102 |  |

## 6	Work item Rapporteur(s)

Xu, Weijie, OPPO, xuweijie@oppo.com

## 7	Work item leadership

SA1

## 8	Aspects that involve other WGs

## 9	Supporting Individual Members

Supporting IM name

OPPO

China Telecom

Xiaomi

Tencent

ZTE

China Unicom

CATT

Alibaba Group

CMCC

vivo

KPN

Convida Wireless

InterDigital

Lenovo

Futurewei

Orange

Huawei

Sharp

Vodafone

Nokia

Nokia, shanghai Bell

WilIoT

Philips International B.V.

AT&T

FirstNet