TSG SA Meeting #SP-90E	SP-201096rev3

08 - 14 December 2020, Electronic meeting

# Source:	CATT, OPPO

# Title:	New WID on System enhancement for Proximity based Services in 5GS

# Document for:	Approval

Agenda Item:	6.4

3GPP TSG SA2 Meeting #142E (e-meeting) 	S2-2009232

Nov 16 – Nov 20, 2020, Elbonia

# Source:	CATT, OPPO

# Title:	New WID on  Proximity based Services in 5GS

# Document for:	Approval

Agenda Item:	9.1

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	Proximity based Services in 5GS

## Acronym: 5G_ProSe

## Unique identifier: 	900007

Potential target Release: {Rel-17}.

Note that this field above indicates the proposed Release at the time of submission of the WID to TSG approval. It can later be changed without a need to revise the WID. The updated target Release is indicated in the Work Plan.

## 1	Impacts 	{ For Normative work, identify the anticipated impacts. For a Study, identify the scope of the study.}

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes | X | X | X | X |  |
| No |  |  |  |  |  |
| Don't know |  |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a …

| X | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| FS_5G_ProSe | SA2 | 830033 | Study on System enhancement for Proximity based Services in 5GS |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |
| 320022 | Requirements for evolution of the 3GPP system architecture | SA1 work item to define requirements for LTE/EPS, which contains proximity services requirements. |
| 790001 | New Services and Markets Technology Enablers – Phase 2 | SA1 work item to define requirements for 5GS, which contains proximity services requirements. |
| 780002 | Removal of 'over LTE' limitation from Mission Critical Specifications | The requirements specified in 3GPP stage 1. |
| 800023 | Study on Mission Critical services support over 5G System | SA6 study item to support mission critical services over 5GS. |
| 800015 | Study on Network Controlled Interactive Service in 5GS | SA1 study item, which studies new services requirements related to proximity services. |
| 840030 | WID on Network Controlled Interactive Service(NCIS) Requirements | SA1 work item, which specifies the requirements for interactive service. |
| 860042 | WID on NR Sidelink enhancement | RAN work item, which specifies enhancements of NR Sidelink. |
| 860038 | Study on NR Sidelink relay | RAN study item, which studies NR Sidelink Relay. |
| 880005 | Study on Security Aspects of Enhancement for Proximity Based Services in 5GS | SA3 study item, which studies ProSe security aspects |
| 890018 | Study on charging aspects of Enhanced Proximity-based Services in 5GC | SA5 study item, which studies ProSe charging aspects |

## 3	Justification

Proximity Services has been developed in EPS from Rel-12 to support both commercial and public safety services. In Rel-14, the Proximity Services (specifically the direct communication) has been enhanced to support V2X services over LTE.

For 5GS, the Proximity Services are expected to be an important system wide enabler to support various applications and services. In Rel-16 the PC5 based architecture and communications are developed to support advanced V2X services. However, there are more proximity related service requirements than service requirements covered by the existing Rel-16 SA2 work, e.g. eV2XARC. For example, the SA WG6 identified that the direct mode, D2D, communication mechanisms, including UE-to-Network Relay, are lacking in 5GS, creating a significant gap to enable Mission Critical services over 5GS (details please refer to S6-190280, LS out to RAN and SA). There are other upcoming applications that rely on the Proximity Services.

The SA1 Study on Network Controlled Interactive Service in 5GS (i.e. FS_NCIS) studies the new proximity related use cases and potential services requirements for interactive services, which could be found in TR 22.842 to explore PC5 communication to maximise the spectrum utilization of frequency resource.

As such, the 5G System needs to be enhanced to support the proximity based services with one common architecture to take advantage of economy of scale, i.e. such architecture can be used for both public safety and commercial related proximity services, where applicable.

The SA2 study has been progressed to identify and evaluate potential architecture enhancements of 5G System design needed to support proximity based services based on SA WG1 requirements defined in TS 22.278, TS 22.261 and TS 22.115 and determine which of the solutions can proceed to normative specifications.

## 4	Objective

The objective of this work item is to specify architecture enhancements of 5G System to support Proximity Services as per conclusions reached within TR 23.752 (clause 8).

The detailed objectives are as follows:

1.	5G System architecture reference models for Proximity Services.

2.	Support of PC5 Direct Discovery (including in-coverage and out-of-coverage cases).

3.	Support of PC5 unicast, groupcast and broadcast modes communication (including in-coverage and out-of-coverage cases).

4.	Support of PC5 Service Authorization and Policy/Parameter Provisioning.

5.	Support of direct communication path selection between PC5 and Uu.

6.	Support of Charging for PC5.

NOTE 1:	The decision to support Control Plane based UE usage reporting or User Plane based UE usage reporting will be determined taking into account feedback from SA5.

7.	Support of UE-to-Network Relay (including QoS and service continuity aspects).

NOTE 2:	The decision to support Layer 3-based UE-to-Network Relay solution, Layer 2-based UE-to-Network Relay solution, or both will be determined taking into account feedback from RAN2 and SA3.

8.	Support of UE-to-UE Relay.

NOTE 3:	The decision to support Layer 3-based UE-to-UE Relay solution, Layer 2-based UE-to-UE Relay solution, or both will be determined taking into account feedback from RAN2 and SA3.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Rapporteur |
| TS | 23.xyz | Proximity based Services (ProSe) in the 5G System (5GS) | SA#91E (March 2021) | SA#92E (June 2021) | Jianhua Liu, OPPO (liujianhua@oppo.com) |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |

## 6	Work item Rapporteur(s)

Qiang Deng, CATT, dengqiang1@catt.cn

## 7	Work item leadership

SA2

## 8	Aspects that involve other WGs

SA3 for the Security aspects, SA5 for the Charging aspects, RAN for the RAN related issues.

## 9	Supporting Individual Members

Supporting IM name

CATT

OPPO

China Telecom

Telecom Italia

CAICT

Tencent

ZTE

China Unicom

TD Tech Ltd

KPN

Convida Wireless

Huawei

HiSilicon

ITRI

Xiaomi

Qualcomm Incorporated

China Mobile

Vivo

NEC

AT&T

Verizon UK Ltd

Interdigital

Motorola Mobility

Lenovo

Telstra

Samsung

Ericsson

Intel

SES S.A.

MediaTek Inc.

LG Electronics

Spreadtrum

Apple

Orange

Philips

FirstNet

Matrixx

Nokia

Nokia Shanghai Bell