## Slide 1
China Telecom
Proposal for 6G Use Cases and Considerations on SID Approach
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR

## Slide 2
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
General Perspectives
Open topics on SA1 6G Use cases：
6G need to emphasize development and continuity. Meaningful use cases should be focused. Gap with 5G-A should be considered.
Emphasis on network simplification, capabilities enhancements , convergence of TN and NTN during network evolution.
New features such as distributed network, multi-parties network should be considered.
Less options of 5G to 6G migration, e.g. standalone is preferred in 6G from our view.
We firstly to submit contributions on SA1 6G SID in SA1#105, Athens (S1-240111). Based on the discussion in stage 1 May Workshop, few aspects are updated and we re-submit it on this meeting.

## Slide 3: Key R20 6G Day-1 features
The study should focus on: 6G use cases, in the center of the 6G portrait, targeting 6G day-1 features and requirements, etc.
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
NEW User Experience
Ubiquitous connectivity
Satellite
Low altitude economy
Multi-parties Network
…
NEW Operation
Migration to 6G
Energy efficiency
Distributed network
Trust
…
NEW Services
Native AI
Immersive communication
ISAC
Data service
…

## Slide 4
New Operation – Migration to 6G
Motivation：network architecture and topology are both very complex. 5G：40+NF，80+interfaces
The 6G system will support most of the existing 5G services, in addition to many new services. New or changed services should be prioritized.
Scenario：Potential migration trend from 5G to 6G
Requirements：
Use cases related to migration to 6G new core design should be studied.
Use cases related to backward compatible between 6G & 5G
Achieving significant improvement for reliability and simplification compared to 5G.
Reducing signaling interactions and simplify the network procedures. Reduce energy consumption.
AI for network operation.
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
AMF
SMF
UDM
UDR
UDSF
AUSF
PCF
NEF
NWDAF
UE
RAN
UPF
NRF
Control Plan
User Plan
SBI
SBI
DCI
SBI: Service Based Interface
DCI: Data Channel Interface
Data Plane
Intelligence Plane
Others
RAN

## Slide 5: New Operation – Distributed Network
Use case 2：Inter-network disaster recovery collaboration
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
Requirements：
Support flexible, on-demand customization and configuration of network capabilities based on user requirements.
Support autonomous operation in one network, i.e., capable of providing limited service when losing connection to other networks.
Support flexible, on-demand collaboration with other networks (e.g., seamless user experience when UE is connected to a different network in disaster condition or requesting a service not provided by the subscribed network.)
Motivation:
Verticals* expect 6G network operation to be
Easy of use: support tailor-made functionality,
Highly flexible: support different and fast-changing usage scenarios from factories to factories and from production lines to production lines,
Extremely resilient: support 24/7 operation, and several logically independent communication domains in one network.
*from 5G-ACIA presentation in 3GPP Stage 1 Workshop on IMT2030 Use Cases
Use case 1：Customized network based on user requirements
Gap：
5G network slice or NPN has to be a complete logical network, comprising of all network functions and NF services.
Isolation (e.g., for local processing and high resilience) and collaboration (e.g., for efficient service delivery) are simultaneously required for 6G network operation, and the level of isolation/collaboration dynamically changes with user requests.
However, 5G only supports a fixed level of isolation/collaboration once the network is deployed with PNI-NPN or SNPN.

## Slide 6: New User Experience - Satellite
Motivation:
Scarcity of orbit and frequency resources: 57,000 low-earth orbit satellites will be deployed in 2029, leaving little available space in the low orbit orbital slots.
Low coverage and high deployment cost: the satellite cannot cover the operator all the time. The operator need to increase the number of satellites.
Requirements:
New use case for new design/new frequency/new connect/new terminal (e.g. vehicles) for NTN
Use case and scenarios to support satellite network sharing between MNOs.
  Inter-satellite networking: Inter-satellite collaboration across multiple orbits.
  Smooth interworking between TN and NTN on service and management level.
  Collaboration on GEO, MEO and LEO should be considered for 6G.
  Small constellations (e.g. hundreds of satellite) should be considered to provide new service
Gap:
The current studies of 3GPP network sharing has not yet been extended to satellite network sharing.
Compared to 5G networks, 6G network NTN sharing are further extended to new service (new call)
Roaming and interworking are not yet fully supported
Remote areas
Ocean
Desert
Sky
Specific locations
Vertical industry
……
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR

## Slide 7: New User Experience – Multi-parties Network
Use case：
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
Requirements：
Flexible reconstruction of the multi-parties network considering network storage and computing capatilities provided by various type of devices and nodes.
Coordination of devices in proximity network and the MNO network for coverage enhancement, data exchanging and processing supporting user-centric services.
Corresponding security and charging aspect.
Gap:
Need service-enabling and coordinated resource orchestration within proximity network and in between the proximity network and the MNO networks, considering connection, storage and computing capatilities.
Need service-enabling multi-parties coordinated operations between proximity network and the MNO network.
Motivation:
The boosting number of user devices and the services emerging in proximity networks are negligible
The merging of proximity network connecting user devices with the various MNO networks provides a new chance and new potential breakthrough for MNO to enhance coverage, and to enable exlusive and compatitive services with low CAPEX.
Extended Hi-Freq and NTN coverage provided by MNO to more users by proximity networks with low CAPEX and/or in emergency.
User-centric AI: data sharing and processing are provided/assisted by coordination between proximity service and cloud service for lower cost, lower latency and higher privacy and security.
Smart Home: contents are exchanged and processed with compatible and MNO certified resource from both Proximity Network and the MNO network.
O2
Notes: Security and charging aspect: authentication and authorization and charging for different parties.

## Slide 8
New Services - Native AI
Motivation:
New feature drivers: ultra-high performance, distributed computing power, complex algorithm models, big data.
New business drivers: ToC (XR, V2X), ToB (intelligent industry, healthcare), intelligent operation (intention driven, digital twin).
AI technologies: federated learning, transfer learning, Large models
Potential trend of 6G AI:
Multi elements collaboration
"Add-on/External" to "Native"
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
Cases:
Multi-agent distributed training and inference
(Network for AI)
Network optimization and automation
(AI for Network)
Cloud
AI
5GC
NWDAF
AI
Cloud
AI
AI
6GC
AI
AI
AI
AI
AI
UE
RAN
Core
O&M
Connection
Data
Computing
Algorithms
Requirements：
New KPIs e.g. latency/accuracy/data rate; New use cases for 6G air and network should be studied.
Support AI capabilities natively, including data management, model training, model transfer, etc.
Multi-node collaboration and distributed algorithms, including federated learning, multi-agents learning, transfer learning.

## Slide 9: New Services - Immersive Communication
Use case：Service awareness and differentiated forwarding
UPF
Service A
Service B
Service C
underlay
GTP-U tunnel
The underlay is not aware of the SLA requirements of service and cannot provide refined and differentiated QoS；
Imperceptible
real-time
Medicine
Immersive
XR
Strong interactive
game
Motivation:
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
Requirements：
Use cases to meet high performance of data forwarding, high data rate, end to end latency related to immersive communication.
Use cases to support service awareness to meet the multi-dimensional service requirements.
Use cases on network protocol enhancement brought by immersive communication.
Gap:
5G networks and applications are deeply decoupled, only providing connectivity function.
New services in 6G networks have differentiated service requirements. Service awareness and end-to-end high-performance data forwarding should be supported.

## Slide 10: Considerations on SID Approach
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR
Preferred Option 1: “One self-contained study item ”, one 6G TR with new logo
Option 2: Multiple 6G SIDs in parallel. Our interest is on network operation (simplification, migration, TN & NTN.)
3GPP stage 1 workshop for IMT-2030 use cases hosts on May, and 6G use cases are not yet clear at this stage. To explore and consolidate the potential use cases, opinions from various companies should be collected and comprehensively considered.
Lessons from 5G indicate that “one umbrella SID” is good.

## Slide 11
Thank you
S1-241022, 3GPP TSG SA1#106, 27 May - 31 May 2024, Jeju, KR