## Slide 1: Discussion on Rel-18 VMR requirements for satellite access
Huawei
S1-241098

## Slide 2: Background
  This document discusses how to clean up the Rel-18 service requirements related to satellite access for the VMR captured in TS 22.261 following SA1 Chair/MCC guidance, and proposes a way forward.

## Slide 3: Discussion
SA1
Rel-18 VMR requirements
SA2
Rel-18 WID
TS 22.261
SA1 Terminology: mobile base station relay
  The related study for Rel-18 VMR in stage 2 is listed in the following:
5.35 Support for Integrated access and backhaul (IAB)
5.35.1 IAB architecture and functional entities
Integrated access and backhaul (IAB) enables wireless in-band and out-of-band relaying of NR Uu access traffic via NR Uu backhaul links. In this Release of the specification, NR satellite access is not applicable. The serving PLMN may provide the mobility restriction for NR satellite access as specified in clause 5.3.4.1
TS 23.501 System architecture for the 5G System
5.35A Support for Mobile Base Station Relay (MBSR)
5.35A.1 General
The MBSR uses the IAB architecture as defined in clause 5.35, and operates as an IAB node (with an IAB-UE and gNB-DU) with mobility when integrated with the serving PLMN. The architecture described in clause 5.35 applies unless specific handling is specified in clause 5.35A.
Observation: satellite access is not applicable for VMR in the Rel-18 stage-2.

## Slide 4: Proposal and way forward
  It is proposed to remove the following Rel-18 VMR requirements for satellite access in TS 22.261, in order to align with Stage 2 specification.
The 5G system shall be able to support mobile base station relays using 3GPP satellite NG-RAN (NR satellite access).
The 5G system shall be able to support mobile base station relays accessing to 5GC via NR satellite access and NR terrestrial access simultaneously.
The 5G system shall be able to support service continuity for mobile base station relays using at least one 3GPP satellite NG-RAN.
NOTE 7: This requirement applies to scenarios where there is a transition between two 3GPP NG-RAN, operated by the same MNO, involving at least one 3GPP satellite NG-RAN.

## Slide 5
Thank you