## Slide 1
Discussion paper of computing services
China Mobile，ZTE
3GPP TSG-SA WG1 Meeting #111
© 3GPP 2025
S1-253140

## Slide 2: Progress of computing services
In Fukuoka meeting, the following 6G computing services are drafted below:
One remaining issue is, what’s the form of computing services that providing to users?
  Option 1: Physical computing resources
  Option 2: Virtualized resources
  Option 3: model
  Option 4: Service oriented
6G Computing Service: A service provided by 6G network utilizing computing resources in Service Hosting Environment, which can be used by a subscriber (via UE)/3rd party.

## Slide 3: Option 1: Physical computing resources
Computing requirements description:
{ "request_type":
"raw_compute", "operation": "matrix_multiply", //computing task type
"compute_unit": "FP16", // computing accuracy:FP32, FP16, INT8, BF16
"total_flops": 1e15, // total computing
"max_latency": "10s", // maximum latency
"data_format": "NCHW" // data format}
6G core network
NOTE: The above term does not imply any architectural assumption, e.g. whether 6G CN is a new or evolved CN (compared to 5G).
"compute_unit": "FP16", // computing accuracy:
FP32, FP16, INT8, BF16
"total_flops": 1e15, // total computing
Real computing
Notes: NCHW: Batch-Channel-Height-Width

## Slide 4: Option 2: Virtualized resource
6G core network
NOTE: The above term does not imply any architectural assumption, e.g. whether 6G CN is a new or evolved CN (compared to 5G).
{ "request_type":
"virtual_resource",
"vm_spec":
{ "cpu_cores": 8, // number of CPU
"ram_gb": 32, // RAM
"gpu_spec":
{ "type": "NVIDIA_A100", // GPU type (A100/H100/L4)
“count”: 4 // number of GPU },
"storage":
{ "type": "SSD", // Storage (SSD/HDD) "size_gb": 512 // Size (GB) }, "network_bandwidth": "10Gbps" // bandwidth
},
"duration": "2h" // occupied time}
Computing requirements description:
"type": "NVIDIA_A100", // GPU type (A100/H100/L4)
“count”: 4 // number of GPU
Virtualized resource
VM
PoD
vGPU

## Slide 5: Option 3: Model
6G core network
NOTE: The above term does not imply any architectural assumption, e.g. whether 6G CN is a new or evolved CN (compared to 5G).
{ // ===== model id===== "model":
{ "name": "stable_diffusion_3", // model ID)
"version": "xl_1.0", // version
"type": "image_generation", // model type: image_generation | llm | nerf | physics_sim
"custom_model_uri": "s3://my-models/v1.pt", // address },
// ===== input parameters=====
"inputs":
{ "prompt": "cyberpunk city with holograms, 8K", // Text Input (Generative Model)
"image_data": "base64_encoded_string", // Image input (image-to-image / segmentation)
"params": { // parameters
"steps": 30, // Number of iterations
"sampler": "euler_a", // sampler
"height": 1024, // output height
"width": 1024 // Output width} },
Computing requirements description:
{ "name": "stable_diffusion_3", // model ID)
"version": "xl_1.0", // version
"type": "image_generation", // model type: image_generation | llm | nerf | physics_sim
"custom_model_uri": "s3://my-models/v1.pt", // address },
Related services
​GPT-5
Stable Diffusion 3.5
Multi-View Rendering, MVR

## Slide 6: Option 4: Service oriented
6G core network
NOTE: The above term does not imply any architectural assumption, e.g. whether 6G CN is a new or evolved CN (compared to 5G).
{ // ===== basic task configuration=====
"task_id": "xr_render_20250812001",
"task_priority": "normal", // low | normal | high | realtime
// ===== case description=====
"scene": {
"type": "6dof_vr", // 360_panorama | 6dof_vr | ar_fusion | nerf_volume
"resolution": [7680, 4320], // [Width, Height] in pixels
"target_fps": 90, // Target frame rate
“hdr_enabled”: true, // HDR support
"latency_tolerance": 20, // maximum latency
// --- NeRF/ Specialized for point cloud case ---
"nerf_config":
{ "voxel_size": 0.01, // voxel size
"ray_samples": 1024, // number of samples per ray
"encode_type": "hashgrid" // coding scheme: hashgrid | triplane } },
Computing requirements description:
"type": "6dof_vr", // 360_panorama | 6dof_vr | ar_fusion | nerf_volume
"resolution": [7680, 4320], // [Width, Height] in pixels
"target_fps": 90, // Target frame rate
Related services
​6dof_vr
cloudxr
Dynamic diffuse global illumination

## Slide 7: Evaluation of four options
Option 1: not recommended
  It is difficult for users to measure the specific amount of computation required for the requested business. 3GPP has great difficulty in standardization.
Option 2: recommended
  Mature in technology (e.g.: K8S), and operators should control and manage the computing resources to further satisfy the requirements.
Option 3: recommended
  Requested model has high dependence to computing, and operator can provide the computing resources according to the requested model.
Option 4: recommended
  Friendly to users and users do not need to care about the real computing resources, and users can just provide the service related requirements to network (e.g.: details of rendering description)
Notes: Option 3改为算法？

## Slide 8
Thank you