## Slide 1: Summary of CEPT Report 52 regarding BDA2GC (for information only)
Terng-Yin Hsu tyhsu@cs.nctu.edu.tw
Jian-Ya Chu skyfeeling.cs96@g2.nctu.edu.tw
Yuan-Te Liao hsnudaniel.cs97g@g2.nctu.edu.tw
Ying-Liang Chen mono.chen@gmail.com
Yi-Hsueh Tsai lucas@iii.org.tw
3GPP TSG-SA WG1 #72 S1-154010
Anaheim, US, 16-20, November, 2015
Agenda Item: 8.1 FS_Smarter: New Services and Markets Technology Enablers Source: Institute for Information Industry (III)

## Slide 2: Outline
Background
Harmonisation possibilities- Broadband DA2GC
Broadband Direct Air To Ground Communications
  DA2GCS (2x10 MHz for FDD operation)
  DA2GCS (20 MHz for TDD operation)
Compatibility/sharing scenarios for DA2GC
  Definitions for Broadband DA2GC (ECC Report 214)
  BDA2GC RL/FL in the frequency band 1900-1920 MHz
  BDA2GC RL/FL in the frequency band 2010-2025 MHz
Conclusion

## Slide 3: Background
The European Commission considered that there is no viable harmonisation option for mobile broadband services using the unpaired terrestrial 2 GHz spectrum that would avoid an unacceptable impact on current licences. An alternative harmonisation option outside the current framework of licence conditions would have to be pursued, which would be likely to imply change or revocation of existing authorisations. Therefore, CEPT was mandated to undertake the following tasks:
  Assess and identify suitable uses other than mobile electronic communications services delivered through terrestrial cellular networks and define the common minimal (least restrictive) technical conditions that would apply to them in these bands. These conditions should be sufficient to avoid interference with services or radio applications in adjacent bands, ensure coexistence with other services or radio applications in the same band, and facilitate cross-border coordination, also at the EU outer borders;
  In performing task (1), consider the following non-ECS uses in line with the priorities of the RSPP: broadband PPDR, PMSE, short-range devices and DECT. This is without prejudice to the consideration of alternative uses for electronic communications services in line with EU spectrum policy objectives, such as Broadband Direct-Air-To-Ground Communications.
  In performing task (1) as specified by task (2) and given the limited temporal or geographical scope of one or more of the radio applications under consideration, assess and justify the possibility of spectrum sharing amongst the radio applications under consideration and, if necessary, develop common technical sharing conditions which may include inter alia spectrum access rules, channelling arrangements or power emission limits that are sufficiently precise for the development of EU-wide equipment.

## Slide 4: Harmonisation possibilities- Broadband DA2GC
A Broadband DA2GC system constitutes what is effectively a backhaul application to support various types of telecommunications services on board aircraft, such as internet access and mobile multimedia services (described in section 3.1). It aims to provide access to broadband communication services during continental flights on a Europe-wide basis. Currently, there is no spectrum designated for Broadband DA2GC in Europe. To allow European citizens and airlines to profit from the social and economic benefits of the implementation of such a radio application (intended to provide broadband connectivity between the aircraft and a terrestrial based network), a harmonised spectrum designation within CEPT would be necessary. In order for the system to be commercially viable, it would need to have the potential to provide a solution across Europe.

## Slide 5: Broadband Direct Air To Ground Communications
Several ECC Reports were under development within CEPT/ECC describing frequency management related and compatibility/sharing issues:
  ECC Report 214 on Broadband Direct-Air-to-Ground Communications (DA2GC),
  ECC Report 209 on compatibility/sharing studies related to Broadband Direct-Air-to-Ground Communications (DA2GC) in the frequency bands 1900-1920 MHz / 2010-2025 MHz and services/applications in the adjacent bands,
  ECC Report 220 on the compatibility and sharing studies of DA2GC, PMSE video links, SRD and DECT in the 2 GHz unpaired bands.
Additionally, as other frequency bands - especially 5855-5875 MHz - have also been studied for Broadband DA2GC, ECC Report 210 on Compatibility/sharing studies related to Broadband Direct-Air-to-Ground Communications (DA2GC) in the frequency bands 5855-5875 MHz, 2400-2483.5 MHz and 3400-3600 MHz was developed.

## Slide 6: Broadband Direct Air To Ground Communications
The outcome of the evaluation of other frequency bands below 6 GHz, which were considered as less suitable than the unpaired 2 GHz bands or than the band 5855-5875 MHz, is also provided in ECC Report 214. In addition, ECC Report 214 also came to the conclusion that a short term solution for Broadband DA2GC (by end of 2017) could not be realised in a frequency band above 6 GHz.
Based on the calculations, which have been carried out and accepted within ECC, paired spectrum of up to 2x10 MHz for FDD operation or 20 MHz for TDD operation is agreed to be necessary to cope with short- to medium-term demand. The amount of spectrum released could be done on a step-by-step process, e.g. by allocating the spectrum in smaller blocks on a national basis. This could be a methodology for facilitating a time plan for a common European harmonisation.

## Slide 7: DA2GCS (2x10 MHz for FDD operation)
Upper Band
Reverse Link
Lower Band
Forward Link

## Slide 8: DA2GCS (20 MHz for TDD operation)
Lower Band

## Slide 9: Compatibility/sharing scenarios for DA2GC
A number of different compatibility/sharing scenarios with other radio services/applications were considered for the implementation of Broadband DA2GC within the 2 GHz unpaired bands. In addition, the possibility to put the DA2GC FL as well as the DA2GC RL within either band was also subject for the studies.
The following three options were considered as the preferred ones as a result of the compatibility studies between Broadband DA2GC and existing services adjacent to the unpaired 2 GHz bands:
  For an FDD system according to ETSI TR 103 054, frequency bands: 1900-1910 MHz (FL) and 2010-2020 MHz (RL);
  For a TDD system according to ETSI TR 101 599, frequency band: 1900-1920 MHz;
  For a TDD system according to ETSI TR 103 108, frequency band: 1900-1920 MHz.

## Slide 10: Definitions for Broadband DA2GC (ECC Report 214)
Term | Definition
Aircraft Station (AS) | Equipment which is installed on-board aircraft providing the radio, control and telecommunication functionalities for broadband DA2G communication
Broadband | “Broadband” in this context refers to a service providing data rates between several hundred kbit/s up to several Mbit/s per end-user, depending on the traffic load within a communication cell
Direct-Air-to-Ground Communications | Direct radio link between an Aircraft Station (AS) and a Ground Station (GS)
Forward Link (FL) | Within the DA2GC system the link from the Ground Station (GS) to the Aircraft Station (AS)
Ground Station (GS) | Equipment which is installed on the ground providing the radio, control and telecommunication functionalities for DA2GC
Reverse Link (RL) | Within the DA2GC system the link from the Aircraft Station (AS) to the Ground Station (GS)

## Slide 11: BDA2GC RL in the frequency band 1900-1920 MHz

## Slide 12: BDA2GC FL in the frequency band 1900-1920 MHz

## Slide 13: BDA2GC RL in the frequency band 2010-2025 MHz

## Slide 14: BDA2GC FL in the frequency band 2010-2025 MHz

## Slide 15: Typical performance expectations for Broadband DA2GC
Metric | 
Broadband DA2GC | “Broadband” in this context refers to a service providing data rates between several hundred kbit/s up to several Mbit/s per end-user, depending on the traffic load within a communication cell
Availability of the service (average target) | 99%
Latency | Less than 100 ms (compared to e.g. geostationary satellite solutions which are typically in the area of 500 ms)
Data rate for one aircraft link | Typically 15 Mbit/s in either direction
Operational system efficiency | Typically between 1.5 and 3 bit/s/Hz

## Slide 16: Conclusion
The Commission services have identified the following shortlist of potential harmonised uses of the 1900-1920 MHz and 2010-2025 MHz frequency bands to be given priority (the order is chosen arbitrarily) in this Mandate:
  PPDR, most likely with preference to ad-hoc (non-permanent) PPDR networks.
  PMSE, preferably for use by wireless cameras.
  Short-range devices (SRD), preferably for improving energy saving and/or energy efficiency.
  DECT19, preferably in the 1900-1920 MHz band.
  Broadband Direct Air-to-Ground Communications (BDA2GC), preferably in a paired spectrum arrangement.