## Slide 1
NTT DOCOMO
Handover Failure Handling
for SRVCC

## Slide 2: Handover Failure for SRVCC
SRVCC PS to CS Cancel Notification
SRVCC PS to CS Cancel Notification Ack
UE
eNB
MME
IMS
MSC
VoLTE
MeasurementReport
HO Required
SRVCC PS to CS Req
SRVCC PS to CS Resp
HO Command
MobilityfromEUTRACommand
Case2: HO fails→
LTE re-connecting
RRC Con Re-est Req
HO Cancel
Notification
HO Cancel Ack
RRC Con Re-est
Comes back to LTE
RRC Con Re-est Cmp
RRC Con Reconf Cmp
RRC Con Reconf
2
re-INVITE (failure to transition to CS domain)
【IMS 】
・After sending back 200K for first re-INVITE, it would also send back to 200 OK for second re-INVITE.
・ Before sending back 200K for first re-INVITE, it would send back to SIP 500 for second re-INVITE
Case-2: re-INVITE (handover cancelled)
Problem
Case 1: UE does not receive HO Command

## Slide 3: Two Cases of handover Failure
Case-1: The UE never receives the handover command.
  There is Radio Link Failure and the HO Command is never received by UE.
  RF gets better. UE comes back to old eNB.
  But UE does not know that it was asked to go to LTE, hence the UE will not send SIP Re-invite(handover failure)
  On receiving the Session Re-establishment trigger from MME, the UE will send SIP re-invite(failure to transition to CS domain)
Case-2: UE receives the handover command. Goes over to 2G/3G. SRVCC fails there. UE comes back to LTE
  In this case on coming back to LTE, the UE will send a SIP re-invite (handover cancel).
  On receiving the “session re-establishment notification” trigger from the MME the UE will again send the SIR re-invite to MME.
Ideal behavior of MME: MME should differentiate between these two cases and not send Session Re-establishment trigger for Case-2.
Can eNB provide info to MME, so MME differentiate Case-1 from Case-2?
  ANS: YES, See next slide

## Slide 4: RRC behavior for IRAT HO failure (TS 36.331)
In both the cases the UE will try to setup the RRC Connection.
From TS 36.331, Section 5.3.7.4:
1> set the reestablishmentCause as follows:
2> if the re-establishment procedure was initiated due to reconfiguration failure as specified in 5.3.5.5 (the UE is unable to comply with the reconfiguration):
3> set the reestablishmentCause to the value reconfigurationFailure;
2> else if the re-establishment procedure was initiated due to handover failure as specified in 5.3.5.6 (intra-LTE handover failure) or 5.4.3.5 (inter-RAT mobility from EUTRA failure):
3> set the reestablishmentCause to the value handoverFailure;
2> else:
3> set the reestablishmentCause to the value otherFailure;
The eNB echoes the RRC failure code on S1AP in the HO Cancel message.
Based on cause MME know if it is case -1: (Cause = otherFailure), or case-2(Cause = handoverFailure)

## Slide 5: Proposal in the CR
For handover failure, MME/SGSN does not send Session Re-establishment message if the handover cancel message from the eNB/RNC indicates that the UE received the handover command but could not handover to the target RAT.