## Slide 1: Way forward on CIoT architecture design

## Slide 2: Contents
Potential Agreements
Show of hands on small data solution
  blue text indicates undiscussed changes
  In this tdoc:
  FeMTC UE means a UE built to the “Rel-13 WI on Further LTE Physical Layer Enhancements for MTC”.
  LC-FeMTC means the Low Complexity part of FeMTC.
  EC-FeMTC means the Extended Coverage part of FeMTC.
  FeMTC uses 1.4 MHz.
  NB-IoT uses 180kHz. NB-IoT is not part of FeMTC.

## Slide 3: Potential Agreements (1)
R13 should support a non-IP service (c.f. “non-IP PDP context”) for NB-IoT (and also for LC-FeMTC ) (and also for Normal Complexity LTE?)
SMS needs to be supported in battery efficient manner on NB-IoT [Vodafone S2-153394] - avoid establishment of DRBs when sending/receiving SMS - move to 2 radio interface messages (rather than 4) per SMS. -> this is a form of “small data over NAS”
In “initial” NB-IoT signalling from UE to RAN, UE should indicate whether the type of ‘access’ is e.g. for MM&SM signalling or SMS or “Data” or Paging Response. [Samsung S2-153303] -> this is similar to GSM-CS and UMTS (Rel 8 LTE does not differentiate SMS and signalling)

## Slide 4: Potential Agreements (2)
The specifications shall support that the NB-IoT control plane node CAN be physically separate to the legacy MME. - this does NOT preclude that they are co-located. - because the NB-IoT UEs access the RAN on different physical resources to other UEs, this does not require DECOR functionality.
In Extended Coverage mode, “R13 FeMTC” UEs are believed to access the RAN on different physical resources to Rel 8 UEs. - EC mode can be supported by both “R-13 Low Complexity” UEs and “Normal Complexity” UEs. -> RAN functionality (e.g. DECOR or extra RRC establishment information) is needed to route to ‘device type specific’ MMEs  having a common RRC protocol for R-13 LC and Normal Complexity mobiles is probably useful

## Slide 5: Potential Agreements (3)
For Smart Phones (i.e. Normal Complexity UEs), caching of the UE context in last used eNB (and UE) seems helpful [Ericsson , S2-153177] - for Smart Phones, the need for the UE context to keep the ROHC context is FFS
 TSG RAN can choose (or not) to specify UE context caching for R-13 NC UEs
    If UE context caching is used for NC devices, a common RRC for LC-FeMTC and NC implies UE context caching for LC-FeMTC UEs
    this does NOT imply any decision on NB-IoT UEs.

## Slide 6: Potential Agreement (4)
Attach without Bearer Service is permitted - e.g. EMM only attach without any ESM signalling (as possible in 2G and 3G). - i.e. Attach without allocating any PDN/Serving GW - i.e. different to Rel 8 LTE (where PDN/bearer activation is mandatory) - this permits SMS-only devices (as possible in 2G). - at least for NB-IoT - also for LC-Fe MTC? - also for Normal Complexity devices? (For NC devices this may add complexity to the network, e.g. with regard to existing inter-RAT mobility specifications.)

## Slide 7: Show of hands on infrequent small data solutions
Who would support to move forward with only solution 2 for NB-IOT.
Who would object to moving forward with only solution 2 for NB-IOT.
Who would support to move forward with only a 5/6/13 solution for NB-IOT.
Who would object to moving forward with only a 5/6/13 solution for NB-IOT.
Who would support to move forward with only solution 2 for LC-FeMTC.
Who would object to moving forward with only solution 2 for LC-FeMTC.
Who would support to move forward with only a 5/6/13 solution for LC-FeMTC.
Who would object to moving forward with only a 5/6/13 solution for LC-FeMTC.
Who would support to apply any assumptions taken on LC-FeMTC also for NC-FeMTC.
Who would object to applying any assumptions taken on LC-FeMTC also for NC-FeMTC.