## Slide 1: CIOT Drafting
Rapporteur: Puneet Jain
11/16/2015, 6:00 – 7:30 PM PST
S2-154275

## Slide 2: CIoT Open Issues
Attach
Documentation Approach
Switch between CP and UP mode
Do agreements apply to eMTC and/or LTE UE

## Slide 3: Attach
  Option 1: Attach without DRB but with IP address allocation for IP data - HW (4076), QC (3987)
  Option 2: MM only attach (without DRB, without any IP address allocation) - VF (4111)
  Option 3: At attach UE provides indication - Ericsson (3869), ALU (4060)
  “No PDN connection” then attach w/o EPS bearer context (inc no DRBs)
  “CP optimization” then attach without DRB
  “UP optimization” then attach with DRB

## Slide 4: Way forward on Attach Procedure for NB-IoT UE
  UE and MME exchange capabilities and their preferences (e.g. CP/UP optimization preference), Data Type (IP or non-IP data).
  UE Indication in attach
    UE Capability (support for UP optimization)
    Preference (CP optimization, UP optimization)
    Optional SM container (e.g. PDN connectivity request) with PDN Type (IP version/unstructured data).
      For unstructured data (e.g. Non-IP data) MME/C-SGN decide to use SGi or T6a path based on operator configuration/SLA agreement.
    If serving MME cannot decode any UE indication then attach shall be rejected.
  Based on UE capabilities and possibly subscription information, MME will decide how to complete the attach based on indication from UE
  “No PDN connection” then attach without PDN connection establishment (inc no DRBs)
    PDN connection can be established later based on UE preferences (e.g. CP/UP optimization preference) already exchanged as part of attach.
  “CP optimization” then attach without DRB but with PDN connection
  “UP optimization” then attach with DRB and PDN connection
  For NB-IoT only UE, stored information on SIM (e.g. GUTI mapping rules) need not be used.

## Slide 5: Way forward on Documentation Approach
No need for new TS
Whether to use Separate clause in TS 23.401 for CIoT will be assessed on case by case basis.
Standalone CN implementation optimized for CIoT should be documented in separate clause/Annex.
For this meeting we can agree on the content (e.g. technically endorse the CRs) and leave room for structuring for the next meeting

## Slide 6: Applicability of solutions to eMTC and/or LTE UE
Solution 2 is mandatory, Solution 18 is optional for NB-IoT. Probably same may not be true for other UEs.
Proposal
  Try to finalize the CRs for NB-IoT
  Revisit this aspects at Jan meeting

## Slide 7: Switch between CP and UP mode
LG (3925), Orange (3792)
Agreement: NB-IoT during the attach procedure the UE and MME exchange their capability and their preference to use UP mode and optimized UP mode.
For switching between CP and UP mode can we further agree that its based on operator’s configuration at MME (e.g. depending on data volume/frequency).