## Slide 1: Handling of signalling conflicts with “data via MME”
Vodafone
S2-161079
3GPP TSG SA WG2 #113 ad hoc
ETSI, Sophia Antipolis, France 23-26 Feb 2016
Agenda item 5.6

## Slide 2: Clash of signalling and data
VPLMN re-runs authentication once per week? - re-authentication policy can be time based rather than (solely) data-volume driven
PSM set to 24 hours?
Software downloads triggered at PSM wake up, imply a reasonable chance of clash with security procedures. - SMS msg waiting flag in MME triggers alert to HSS upon S1 establishment. - Then downlink data arrives before Authentication Response received/Security Mode Command sent to UE. - many software downloads >> GERAN TR model of 2000 bytes.
If security procedures fail, then software download will be interrupted.
Next software download attempt may again clash with VPLMN security procedures…

## Slide 3: NB-IoT data rates
Minimum about 300 bit/s -> 40 secs for 1500 byte packet
Maximum about 120 kbit/s -> 0.1 seconds for 1500 bytes
Large unknown range does not interact well with MME timers

## Slide 4: SCEF Data Service?
Providing indication to the SCEF that data has been delivered to the UE would be a useful service.
Need to avoid power consumption by UE sending application level acks.
Get eNB to tell the MME when a (RLC acknowledged mode) packet has been successfully delivered to the UE
MME can relay this ‘success’ to the SCEF.
SCEF trusts that UE software stack provides RLC packet’s payload to upper layers.

## Slide 5: Potential Way Forward as of Telco, 16/2/16
Buffer data in MME - submit max 2 data/signalling packets to eNB - eNB (but NOT UE) sends S1AP ack to MME when each packet from MME delivered to UE - wait for eNB to confirm delivery of 1st packet before pushing 3rd downlink packet to eNB
MME can prioritise between signalling and data
Allows more predictable start of MME NAS timers
Useful SCEF service

## Slide 6: Alternative

## Slide 7: EPS Signalling Procedures
What procedures are there? - Attach - ID request (IMSI or IMEI) - Authentication - NAS Security Mode control - EMM info - GUTI reallocation - PDN establishment (inc. request for APN name) & release - movement based TAU - periodic TAU - SMS (NAS transport) - Location Services (generic NAS transport)
Most likely clash will be during periodic TAU that triggers both data delivery AND security procedures.
Need care during Authentication and Security Mode Command procedures to be sure which key set is being used to encrypt/decrypt data/signalling on Uplink and Downlink

## Slide 8: Complete Security Procedures before Data Transfer?
Delay HSS/MSC SMS msg waiting alert if re-authentication scheduled by MME. - works at (Periodic) TAU and Attach to same MME. - inter-MME Attach/TAU? Probably natural that MME completes TAU before data transfer - UE could still do MO Service Request with big uplink data and then be slow to respond to Authentication challenge -> but could mandate internal UE behaviour to not submit too much data to AS. - need to extend MME behaviour also at Page Response, and be careful that UE ‘service request response timer does not expire’ – but the timer is for CT 1 - what happens with HL-Com? Probably OK -> don’t alert the SGW until security completed.

## Slide 9: New Proposed Way Forward:
Complete security procedures before data transfer
Improve with eNB indication of coverage level to MME in S1-AP initial UE message? (This enables MME to adjust its internal timers: aligns with EC-GPRS?) Also in draft CR.
On Uplink, UE internal behaviour avoids too big data submission to AS. Above documented in “draft” CR in S2-161083. Downlink buffering of signalling and data remains in eNB
Keep “verified delivery” SCEF data service for Rel 14

## Slide 10: Background information

## Slide 11: Data and Signalling buffering
Currently buffering of downlink data and signalling is in eNB.
However:
In rel 8, only EMM, ESM and SMS are multiplexed downlink on S1-AP. - SMS is ‘state driven’ and only 1 MO and 1 MT SMS can occur at one time - EMM is state driven: no overlapping procedures - ESM can invoke multiple parallel bearer establishments during Attach. And MME is aware of these procedures and TS 23.401 has specified mechanisms to cope with eNB NAS message dropping at X2 and S1 mobility.
Rel 9 added Location Services (LPP 36.355 &48.080 Supplementary Services) - was LCS design analyzed by SA 2 ? (e.g. for emergency calls, interaction of large LCS packets with GBR bearer establishment) - not clear how big the LCS messages are, but clearly CT 1 was concerned that they could be >255 bytes and hence they created the Generic NAS transport (with size limited by PDCP’s [8188] bytes).
EPS location services architecture will probably get (re)used for NB-IoT.