## Slide 1: Discussion on DCN selection parameters for eDECOR
Apr. 1, 2016
NTT DOCOMO
S2-161778
TSG SA WG2 #114
11-15 April 2016, Sophia Antipolis, FR

## Slide 2: Objective
Key decision vectors
Requirement for Selected DCN_ID
Comparison of UE Usage Type and DCN ID from the following aspects;
  Support of fine-grained DCNs
  Inter-operation with Rel-13 DECOR
Conclusion

## Slide 3: Key Highlights of the different Solutions
Solution Title/Section | SIM Parameter | Parameter provided by Network | Storage of parameter in UE | Parameter provided by UE in RRC | Parameter provided by UE in NAS
Solution #1: Per PLMN DCN ID, SIM info, NAS Type | Default DCN ID (maybe per PLMN) | DCN ID | PLMN1: DCN ID1, PLMN2: DCN ID2, … | DCN ID +NAS Type | DCN ID
Solution #5: Per PLMN DCN ID + SIM | (Default) UE Usage Type | DCN ID | PLMN1: DCN ID1, PLMN2: DCN ID2, … | DCN ID, else Default UE Usage Type | DCN ID
Solution #3: UE Usage Type + SIM | (Default) UE Usage Type (maybe per PLMN) | None (Decor MMEGI based solution is used) | None (MMEGI as part of GUTI is used) | UE Usage Type | None (RAN forwards UE Usage type to MME)
Solution #7: UE Usage Type, No SIM | None | UE Usage Type | UE Usage Type | UE Usage Type | UE Usage Type

## Slide 4: Key Decision Vectors (decreasing order of priority)
Should the network provide “Selected DCN” ID (SDCN_ID) to the UE?
  YES.
  In Rel-13, we used MMEGI as the SDCN_ID and we needed to have MMEGI coordination across the network for NNSF. This is a big NNSF configuration issue, (reason: In Rel-13 we did not want to impact UE). With Rel-14, we should have a cleaner solution: network provides SDCN-ID to UE which UE echoes back to network in initial NAS message. Hence, we have a single SDCN_ID in the NNSF for DCN selection.
Should there be “default” parameter (in SIM or device)?
  It is nice to have this; but not a must.
  Having such a parameter in SIM reduces probability of redirection in a “first Attach” to network in HPLMN.
Should the SDCN_ID be per-PLMN or not?
  Preferable.
  Having this per-PLMN helps in roaming scenarios. This is not such a big deal. However, if UE stores this per PLMN, preferable and makes this work also with roaming considerations.
Solution #1, #3 and #5 are better
Solution #1 and #5 are better
Solution #1, #5 and #7 are better

## Slide 5: Requirement for SDCN_ID
The SDCN_ID should clearly be a separate parameter from the subscription parameter “UE Usage Type”.
  Each MME has this function:
    SDCN_ID = f(UE Usage Type, UE Capabilities, …);
  The MME should be able to distinguish between UE Usage Type or SDCN_ID; i.e. whether it needs to do a mapping of not.

## Slide 6: Comparison of UE Usage Type and DCN_ID - Support of fine-grained DCNs -
RAN
DCN for IoT
(default)
DCN for IoT
(Company A)
DCN for IoT
(Company B)
DCN for IoT
(Company C)
Fine-grained DCNs for IoT
Main DCN for IoT
UE Usage Type | DCN_ID
#10 (standardized value for IoT) | UE Usage Type: #10 DCN_ID: any (except #1-#3)
#201 (operator-specific value for IoT of company A) | UE Usage Type: #10 DCN_ID: #1 (value for IoT of company A)
#202 (operator-specific value for IoT of company B) | UE Usage Type: #10 DCN_ID: #2 (value for IoT of company B)
#203 (operator-specific value for IoT of company B) | UE Usage Type: #10 DCN_ID: #3 (value for IoT of company C)
DCN_ID is more extensible for using fine-grained DCNs w/o changing UE Usage Type (no roaming impact).
These UEs cannot camp on DCNs of VPLMN

## Slide 7: Comparison of UE Usage Type and DCN_ID - Inter-operation with Rel-13 DECOR -
Impacts to DNS
  DCN_ID can be used with Rel-13 Decor with DCN_ID used as “mapped UE Usage Type” (C4-161364):
    The UE usage type used during DNS procedure shall be the one mapped from the UE Usage Type received from the HSS as part of the subscription, based on the serving network operator configured policies and the UE related context information available at the serving network, e.g. information about roaming.
  Hence no impacts to DNS with not only UE Usage Type but also DCN_ID.

## Slide 8: Comparison of UE Usage Type and DCN_ID - Inter-operation with Rel-13 DECOR -
Impacts to Reroute/Attach/TAU/RAU procedures
No problems with Rel-13 DECOR.
Obtain UE Usage Type (by existing procedure)
DCN_ID = f(UE Usage Type, UE Capabliities, …)
(MMEGI/Null-NRI/SGSN Group ID, UE Usage Type)
(MMEGI/Null-NRI/SGSN Group ID, UE Usage Type)
“Reroute parameters” = MMEGI … can be replaced by DCN_ID.
Old MME/SGSN
Identification Request/ Context Request
Response(UE Usage Type)
DCN_ID = f(UE Usage Type, UE Capabilities, …)
DCN_ID can also be provided here as a new parameter (DCN_ID).
DNS based on “mapped UE Usage Type” or DCN_ID
Can be based on DCN_ID, e.g. DNS.

## Slide 9: Comparison of UE Usage Type and DCN_ID - Inter-operation with Rel-13 DECOR -
Impacts to Handover procedure
No problems with Rel-13 DECOR.
Old MME
New MME
Forward Relocation Request (UE Usage Type)
DCN_ID = f(UE Usage Type, UE Capabilities, …)
DNS based on “mapped UE Usage Type” or DCN_ID
DCN_ID can also be provided here as a new parameter (DCN_ID).

## Slide 10: Conclusion
DCM supports the introduction of DCN_ID.
  Agree to at least Solution #1 without the NAS Type parameter.
Solution Title/Section | Provision of SDCN_ID | Default SDCN_ID | SDCN_ID per PLMN | Support of fine-grained DCNs | Inter-operation with Rel-13 DECOR | DCM evaluation
Solution #1: Per PLMN DCN ID, SIM info, NAS Type | X | X (DCN_ID) | X | X | X | 
Solution #5: Per PLMN DCN ID + SIM | X | X (Default UE Usage Type) | X | X | X | 
Solution #3: UE Usage Type + SIM |  | X (Default UE Usage Type) | X(?) |  | X | 
Solution #7: UE Usage Type, No SIM | X (mapped UE Usage Type) |  | X | X | Confusion between subscribed UE Usage Type and mapped UE Usage Type | 
< Evaluation >