## Slide 1
Options for the Multi-homed IPv6 PDU Session
Intel
S2-172265
3GPP SA2#120, Busan, Korea 27-31 March

## Slide 2: Summary
The multi-homed IPv6 PDU Session is one of the main Session Management features in the 5G System
The current assumptions are:
  It is based on so-called “Scenario 1” in IETF RFC 7157
  It relies on IETF RFC 4191 to influence the selection of the source address in the UE
  Each IPv6 prefix in the multihomed PDU Session is associated with an SSC mode. However, only the SSC mode for the first IPv6 prefix is signalled, whereas all IPv6 prefixes that are assigned subsequently are assumed to have SSC mode 3
This contribution proposes to investigate
  The actual support in existing IETF RFCs
  The consequences on the 5G system in terms of signalling and the limitations in use
Proposal

## Slide 3: Use cases for Multi-homed IPv6 PDU Sessions
Concurrent access to remote and local DN
  PDU Session associated with multiple IPv6 prefixes
  A "common" UPF referred to as "branching point“ that steers the UL traffic towards one or the other IP anchor based on the Source Prefix of the uplink packet
  RFC 4191 is used to configure rules into UE to influence the selection of the source address. This corresponds to Scenario 1 defined in IETF RFC 7157 "IPv6 Multihoming without Network Address Translation“
  Can be used to support concurrent access to a local service (e.g. local MEC server) and the Internet
  A branching point for a given PDU Session may be inserted or removed by the SMF on the fly
Service continuity
  Same as left-hand side, except that it is used to support make-before-break session and service continuity mode 3 (SSC mode 3)

## Slide 4: Relationship to IETF RFC 7157 Scenario 1
Current assumption: based on RFC 7157 Scenario 1
  “rtr1” and “rtr2” reside in the UPFs serving as PDU Session Anchors
  Route Information Option (RIO) defined in RFC 4191 is used by each “rtr” to advertise destination prefixes, associated with Route Lifetime and a route preference (Prf) that can take one of three possible values (High, Medium (Default), or Low)

## Slide 5: How to use RIO in Scenario 1? (1/2)
1a. Concurrent access to local and remote Data Network:
    1) the PDU Session Anchor providing access to the local DN advertises the route(s) to the local network with a higher preference than the other router (e.g. the Prf parameter set to ”Medium (default)“).
    2) the PDU Session Anchor providing access to the remote DN advertises the route(s) (or a single ”default“ route) to the remote network with the Prf parameter set to “Low” preference.
    Based on this information, for all traffic destined to the local DN (as identified by the advertised route(s)) the UE will choose the router in the ”local“ PDU Session Anchor. Choosing the router automatically determines the source IPv6 prefix that the UE must use with this traffic.
1b. Service Continuity:
    When the SMF configures the new PDU Session Anchor 2, the SMF requests the two PDU Session Anchors to send a Router Advertisement to the UE as follows:
    1) PDU Session Anchor 2 sends a RA including the same route information as the one that was previously advertised by PDU Session Anchor 1, however, with a route preference that is raised by one degree (e.g. ”High“ if the previous one was ”Medium (default)“).
    2) At the same time, PDU Session Anchor 1 is configured to send a new RA message advertising the same route(s) as previously with the same (”Medium (default)“) preference, but this time with a Route Lifetime parameter set to a value that corresponds to the time duration the network is willing to keep the old prefix alive.
    Once PDU Session Anchor 1 is released, the SMF configures the remaining PDU Session Anchor 2 to send a new RA message that is identical to the previous, except that the preference is decreased by one degree (i.e. set to ”Medium (default)“ instead of “High“). The reason for this is that the route preference parameter (Prf in RFC 4191) supports only three values (Low, Medium (default), and High). In order to cope with future relocation of the PDU Session Anchor, the SMF needs to lower the preference of the advertised ”local“ route(s).

## Slide 6: How to use RIO in Scenario 1? (2/2)
1c. Concurrent access and Service Continuity combo:
    When the SMF configures the new ”local“ PDU Session Anchor ”L2“, the SMF requests the two ”local“ PDU Session Anchors to send a Router Advertisement to the UE as follows:
    1) PDU Session Anchor ”L2“ sends a RA message including the same route information as the one that was previously provided by ”local“ PDU Session Anchor “L1“, however, with a route preference that is raised by one degree (e.g. Prf is set to ”High“ if the previous one was ”Medium (default)“).
    2) At the same time, the ”local“ PDU Session Anchor ”L1“ is configured to send a new RA message advertising the same route(s) as previously with the same (”Medium (default)“) preference, but this time with a Route Lifetime parameter set to a value that corresponds to the time during which the network is willing to keep the old prefix alive.
    Once the ”local“ PDU Session Anchor “L1” is released, the SMF configures the remaining ”local“ PDU Session Anchor “L2” to send a new RA message that is identical to the previous, except that the preference for the ”local“ route(s) is decreased by one degree (i.e. set to ”Medium (default)“ instead of “High“). The reason for this is that the route preference parameter (Prf in RFC 4191) supports only three values (Low, Medium (default), and High). In order to cope with future relocation of the ”local“ PDU Session Anchor, the SMF needs to lower the preference of the advertised ”local“ route(s). In contrast, the “remote” routes are invariably advertised with Prf set to “Low”.

## Slide 7: Comments related to RFC 7157 Scenario 1
While Scenario 1 can be supported with RFC 4191 in its current form, there are some limitations to be considered:
  Requires close control of route preferences (i.e. lowering the preference value after each service continuity event).
  No possibility to explicitly signal the SSC mode associated with an IP prefix (e.g. in the combo scenario (1c) each time a new prefix is assigned, it is assumed to be of SSC mode 3, whereas in some cases it would be beneficial to have it as SSC mode 2).
  No explicit linkage between the new and old prefix in the service continuity scenario (i.e. UE supposed to make the linkage based on the fact that the same route(s) are being advertised on both prefixes).
  The link between the UE and the network is not point-to-point anymore.

## Slide 8: How about IETF RFC 7157 Scenario 2?
Scenario 2 in RFC 7157
  A single gateway router (“GW rtr”) connects the host to two or more upstream networks
  This is not the current assumption in the 5G system
To support it in the 3GPP 5G system architecture:
  The “GW rtr” would need to reside in the UPF serving as the “branching point”
  Requires new option in the RA message (see below)

## Slide 9: How to use a new RA option in Scenario 2?
2a. Concurrent access to local and remote Data Network:
    When the network decides to add a local PDU Session Anchor “L”, the SMF controlling the PDU Session inserts a “branching function” with “GTW rtr” functionality in the multi-homed PDU Session and configures the “GTW rtr” function to advertise the following information using a new RA option:
      The “local” route(s) and the associated source IPv6 prefix that the UE needs to use for the “local” route.
      The “remote” route(s) and the associated source IPv6 prefix that the UE needs to use for the “remote” route.
      The SSC mode associated with each source IPv6 prefix.
2b. Service Continuity:
    When the network decides to assign another PDU Session Anchor 2 that is geographically closer to the current UE location, the SMF controlling the PDU Session inserts a “branching function” with “GTW rtr” functionality in the multi-homed PDU Session and configures the “GTW rtr” function to advertise the following information using a new RA option:
      The new prefix associated with the same route(s) as the old prefix, with an indication that UE should start diverting traffic from an old source prefix to the new source prefix.
      The old prefix that is “linked” to the new prefix (“linked” in the sense that it indicates which one of the old prefixes is being replaced by the new prefix), associated with a timer value indicating how long the network is willing to keep the old prefix.
      The SSC mode associated with the new source IPv6 prefix.
2c. Concurrent access and Service Continuity combo:
    This case is the addition of the previous two cases. Given that the UE is always explicitly indicated to which old prefix the new prefix relates, there is no need for handling route preferences (contrary to the solution relying on RFC 7157 Scenario 1 described earlier).

## Slide 10: Comments related to IETF RFC 7157 Scenario 2
No need for use of route preferences (Prf).
Explicit signaling of “linked” prefixes for the service continuity and combo scenarios.
Centralized source of RA signaling (i.e. from the “GW rtr” function), which implies lower volume of RA messages, as well as of C-plane configuration messages from the SMF.
Preservation of the point-to-point link between the UE and the network.
The only drawback of this option is that it requires a new option in the RA message.

## Slide 11: Proposal
Define a new RA option for vendor specific content in the IETF that can be used by 3GPP
  It is noted that the Vendor Specific Option (VSO) in IKEv2 is used in several occasions in TS 23.502
Consider adding RFC 7157 Scenario 2 mode of operation for the multi-homed IPv6 PDU Session in the 5G system
    If this is agreeable, the authors will provide corresponding pCR in the next meeting