## Slide 1: Service Based Architecture Status and Suggested Future Work
China Mobile

## Slide 2: Goal
  The 5G system is defined with a single architecture (i.e., service-based architecture).
    The architectures with P2P reference points are the representations of SBA which illustrated the interactions of the NFs
Single interaction mechanism (either service-based or P2P interface) within CP is the target.
“Network functions within the 5G Core Control Plane unless explicitly stated otherwise, shall exhibit service-based interfaces for services that can be used by other authorized network functions.”
The service-based interfaces (SBI) are the target within the CP NFs.
  All SBIes should apply a same type of interface
  SBIes are not (necessarily) the same as the NB interface(s) for exposure

## Slide 3: Current Status
NF service definition
  Two basic types of NF services are defined
NF Service framework: High level description almost done
  Discovery: Service discovery by using NF discovery via NRF
  Authorization : two steps authorization
  Registration/de-registration: a reference to SA5 WG
NF Services
  23.501: Template tables for NF services
  23.502
    Drafting rules and conventions for NF service description are agreed
    Drafting rules to reflect the NF services in procedure flow are agreed
    Initial NF services are identified (need further evaluation) on AMF, UDM, EIR, PCF, NEF, NRF, SMF, SMSF
The current two TSes already provided good information to proceed on SBA!

## Slide 4: On “Evaluation Criteria”
The current two TSes already provided good and enough information that can be used as the “determine/evaluate” criteria
  Annex B in 23.502
  Definition in Section 7.1.1 in 23.501
Therefore, it is suggested to proceed with what we agreed in SA2#119
Consider the problem from another angle: what is the criteria that makes an interface/reference point can not be defined as a SBI

## Slide 5: Suggested Work to do
NF Service framework
  Some further work may need to discuss e.g.,
    Discovery: the service level of discovery
    Authorization:
    Registration/de-registration: dynamic mechanism on registration/de-registration (beyond SA5 OAM)
  Service framework procedures to be defined in 23.502.
  Relation of discovery/authorization/registration to other parts of the architecture
    For example interacts with NRF or slicing concepts
NF Services
  23.501
    Fill in the Table of section 7.2.
  23.502
    Further description of potential NF services in clause 5
    Incorporate the NF services in the flows (clause 4).
      Modifications of the flows maybe needed in terms of representation (follow A.3.2/3 in 23.502) or modification to fit for NF service description

## Slide 6: Suggested Future Plan
SA2#120 (March)
  Continue derive potential NF services based on E2E flows
  Discuss implication of E2E flows due to the NF services, describe/update flows based on the NF services drafting rule
SA2#121 (May) 23.501 for information
  Complete Service framework (23.501 and 23.502)
  Agree on the identified NF services
  Discuss the exception of non-SBI interfaces in CP if have
SA2#122 (June)
  Update flows/NF services as needed
SA2#122-BIS (Aug) 23.501 for approval; 23.502 for information
  Update flows/NF services as needed
SA2#123 (Oct.)
  Update flows/NF services as needed
SA2#124 (Nov.) 23.502 for approval
  Update flows/NF services as needed