## Slide 1: SA WG2 Meeting #124 Nov 27 – Dec 1, 2017, Reno, NV, USA S2-178422
OI#12 – N3IWF-ePDG selection for 5G capable UEs
Discussion paper
Nokia, Nokia Shanghai Bell
<Change information classification in footer>

## Slide 2: N3IWF vs ePDG
When 5G-UE moves between NR and WLAN in the same PLMN, the same AMF can be used. -> This minimizes the accesses to AUSF and UDM as full authentication is not required (If the UE would have selected an ePDG, authentication would be required for both 5G to/from WLAN and EPS to WLAN mobility)
Services such as SMS over NAS are still supported when accessing Core Network via N3IWF even if no access via 3GPP radio. This is not possible via ePDG, which requires SMS over IMS
Unlike ePDGs, there is no need for 3GPP AAA servers since N3IWF is connected to AMF that handles authentication towards AUSF
Advantages of accessing Core via N3IWF rather than via ePDG

## Slide 3: N3IWF-ePDG selection
  N3IWF selection is already specified in TS 23.501 clause 6.3.6
    The Tracking/Location Area Identifier FQDN shall be constructed by the UE based only on the Tracking Area wherein the UE is located
    The ePDG FQDN format is substituted by with N3IWF FQDN format as specified in TS 23.003
    The ePDG identifier configuration and the ePDG selection information are substituted by the N3IWF identifier configuration and the N3IWF selection information respectively
  Assumption for Rel-15
    In Rel-15, the ePDG selection and the N3IWF selection processes shall be used as they are specified today, i.e. the "N3IWF-ePDG selection" shall use the two algorithms w/o change, and shall not redefine a brand new algorithm. In other words, we just need to define an "pre-selection" algorithm which is intended to select either N3IWF selection process or ePDG selection process
    It might not be the most optimized way, but it may be optimized in Rel-16
Basics and assumptions

## Slide 4: N3IWF-ePDG selection
  TS 23.501 clause 5.16.3.5 (Domain selection for UE originated sessions/calls) states:
    "A UE set to "voice centric" for 5GS shall always try to ensure that Voice service is possible. A voice centric 5GC capable and EPC capable UE unable to obtain voice service in 5GS shall not select a cell connected only to 5GC. By disabling capabilities to access 5GS, the UE re-selects to E‑UTRAN connected to EPC first (if available). A UE set to "data centric" for 5GS does not need to perform any reselection if voice services cannot be obtained."
  This implies that a "voice centric" 5G capable UE that cannot obtain voice services over 5GS behaves as if it is a 5G non-capable UE. When attaching to EPS, the UE will NOT indicate to the MME that it is 5G capable, so the MME will NOT select a PGW that is also SMF/UPF. If the UE moves to N3GPP access and selects a N3IWF, the handover will not be possible.
  Hence, if "VoIMS in 5GS" is not supported, the UE has to select an ePDG.
  This is not linked to any home operator configuration: it is a pre-requisite for all UEs
Pre-selection related to voice/data centric considerations

## Slide 5: N3IWF-ePDG selection
Proposal summary
Collect information about voice/data-centric, 5GS VoIMS support, N3IWF Sel Info, ePDG Sel Info
«SiMPLE DECISION PROCESS
N3IWF selection process
ePDG selection process

## Slide 6: N3IWF-ePDG selection
  Smooth deployment of N3IWF's
    Operators having deployed ePDG's geographically distributed may prefer that an ePDG close to the UE is selected rather than a centralized N3IWF
    On the other hand,
      This would be only for an interim period, as in the long term, N3IWF's will be deployed the same way as ePDG's: after the interim period, the operator will prefer a 5G capable UE to select a N3IWF
      Data centric UEs can be handled by centralized N3IWF's. Voice-centric UEs under a 5GS not supporting VoIMS are already taken into account by the pre-selection algorithm
      So, sub-optimal situation only concerns "voice-centric" UEs under a 5GS supporting VoIMS during interim period
    This may be solved by a specific configuration in the UE (voice-centric preference = ePDG or N3IWF) to be applied by the UE when its status is voice-centric.
      Should only concern the Home PLMN. Not the visited PLMN's. Because the Home Operator should not care about whether a roaming partner supports VoIMS over 5GS or not. In addition, only some parts of a PLMN may support VoIMS over 5GS…
      Is it strongly required or can we skip it?
Issues and proposed way forward

## Slide 7: N3IWF-ePDG selection
  Should the 3GPP attachment be considered?
    In TS 23.402, the 3GPP attachment is considered only for the selection of the PLMN. See clauses 4.5.4.4 and 4.5.4.5. It does not consider the RAT (GERAN, UTRAN, E-UTRAN). It does not either consider the Core Newtrok type (GPRS or EPC)
    As a summary: if the UE is 3GPP-attached to a PLMN, which has roaming agreements with HPLMN for untrusted N3GPP access (configured in ePDG selection information), the UE attempts to select an ePDG in that PLMN. Otherwise, UE attempts to select an ePDG in same country, then in its HPLMN.
    It is proposed to have the same principles for 5G capable UEs, i.e.:
      Do not consider whether the UE is attached to E-UTRAN or NR for selecting N3IWF or ePDG
      Consider the attached PLMN with regards to roaming agreements provided in N3IWF Selection Information and in ePDG Selection Information
Issues and proposed way forward

## Slide 8: N3IWF-ePDG selection
Issues and proposed way forward
  3. Should we consider the use case of a PLMN that has deployed 5GS but not N3IWF?
    If the UE is registered to such a PLMN, the UE will not be able to select a N3IWF in this PLMN, and so will select a N3IWF in a different PLMN (of the same country)
    It will not select an ePDG in the registered PLMN
    Selecting a N3IWF in a different PLMN, would mean that a handover between EPS (rPLMN) and N3GPP (other PLMN) would not work)
  This use case has NOT been considered in the pCR.

## Slide 9: N3IWF-ePDG selection
Proposed way forward
  If the UE is data-centric or is registered for 3GPP access on 5GS, the UE should attempt to perform N3IWF selection process first, and possibly to ePDG selection second
  If the UE has attached to EPS onto a MME without indicating it is “5G capable”, the UE shall perform ePDG selection
  If the UE is neither attached to EPS onto a MME, nor registered for 3GPP access on 5GS, the UE should attempt to perform N3IWF selection first, and possibly to ePDG selection second

## Slide 10: N3IWF selection
If an ePDG has been enhanced to support both N3IWF and ePDG functions, then it should know whether it has to operate as an N3IWF or as an ePDG. This could be done via several ways (to be defined):
  The different (public) IP addresses (there are separate FQDNs, so it is possible)
  After the IKE SA_INIT exchange, the combined ePDG/N3IWF can detect that the UE is 5G by looking in the IKE-AUTH Request message, at:
    Either a specific "Registration Parameter" (there is already the SUPI/GUTI and NSSAI) that is conveyed together with the NAS Registration Request message
    Or to the NAI (another possibility would be to append <5G> to the NAI, used for the ID. But it is not nice to have a NAI that would depend on the access technology.
   It is proposed to use a specific registration parameter
Combined ePDG/N3IWF node