## Slide 1: RACS: Way forward
Nokia, Nokia Shanghai Bell
SA2#136
Reno, Nevada, USA, 18-22 November 2019
Tdoc type: discussion
For: Agreement
Agenda Item: 7.10.3
WI/ Release: RACS/Rel -16
Tdoc # S2-1911939

## Slide 2: PLMNs Modes of operation
Both Tdocs: Imply a PLMN may operate using Manufactured Assigned ID only
This is not expected as this will not allow the operator to benefit from RACS for all UEs that do not support Manufacturer Assigned Mode of operation
There is no certainty any single UE vendor will indeed support Manufacturer Assigned Mode of operation
S2-1911804 | DISCUSSION | Decision | RACS ID types usage. | Ericsson
S2-1911878 | DISCUSSION | Discussion | Way Forward on issue of PLMN and Vendor provided Radio Capability IDs . | T-Mobile USA
From S2-1911804
Observation 3: Operators that don’t want to deal with PLMN supplied ID’s can configure their network to use only Manufacturer supplied IDs
From S2-1911878
Agreement Proposal 1: It is not expected there will exist PLMN deployments supporting Manufacturer Assigned IDs only

## Slide 3: Transition mechanism trigger and Modes of operation
Both Tdocs: Imply a PLMN may operate its own proprietary way to transition: this is not possible (see next slide)
This is not expected as a method is needed to identify those PLMN assigned IDs that need to be removed (next slides to clarify) and this I should be related to the process of creation and deployment of Manufacturer assigned IDs. UCMF vendors and UE manufacturers should have certainty on how things work in multivendor scenarios.
It is questionable why a UE vendor would want to only partly use Manufacturer Assigned IDs: each radio configuration should be tested by the UE vendor before shipping and at that time an ID can be assigned to each such radio configuration – we should not make sure to enable untested radio configurations in devices in the market
It is questionable why a PLMN would go through the capital and operations costs of supporting Manufacturer Assigned IDs without a precise outlook on the benefit as the coverage of UE radio configurations may only be partial.
S2-1911804 | DISCUSSION | Decision | RACS ID types usage. | Ericsson
S2-1911878 | DISCUSSION | Discussion | Way Forward on issue of PLMN and Vendor provided Radio Capability IDs . | T-Mobile USA
From S2-1911804
For the transition from PLMN ID to manufacturer ID – the network needs to trigger the UE to delete the existing PLMN supplied ID – since SA2 cannot agree on the triggering mechanism it is proposed to leave this implementation specific
From S2-1911878
Agreement Proposal 2: A standardised trigger for transitions is required
Agreement Proposal 3: A UE Supporting Manufacturer assigned IDs is expected to have one and correct (i.e. not invalid) for each of its radio configurations, else it is faulty and the UE type can use PLMN assigned IDs
Alternative Agreement Proposal to 2 and 3: Remove the options to use Manufacturer assigned IDs if it is expected to be difficult to assign an ID for each Radio Configuration (assumption: each radio configuration is tested and for each radio configuration test case a Manufacturer assigned ID can be added – so tested devices should naturally be able to have a valid Manufacturer Assigned ID for each radio configuration – 3GPP should not encourage untested configurations to come to market)
If there is a preference from the operator to “force” UEs supporting a newly provisioned M-RACS ID to start using this M-RACS ID, the network can be implemented to request such UEs to delete all P-RACS IDs. The network identification of applicable UEs can be implementation specific and the granularity of such deletion trigger depends on the parameters of the deletion trigger. A working mechanism to use for P-RACS ID deletion in UEs is proposed in 23.501 CR#1592 (S2-1911307).

## Slide 4: Transition mechanism trigger comments
The yellow text implies that each PLMN can identify which PLMN assigned IDs to transition is PLMN or UCMF vendor specific manner: however not a single working example is provided. It needs to be proven this undefined approach is feasible.
The Green text says that the granularity of transition is not specified. How can a UE vendor be sure its granularity is supported? How can a UCMF vendor decide which granularity to support? What is the impact on the Algorithm for assignment of PLMN assigned UE radio capability IDs if the PLMN assigned IDs are assigned in a way that is not compatible with an assumed granularity by certain UE vendors?
The red text says S2-1911307 defines ONLY a deletion algorithm: this is not true as it forces the PLMN assigned IDs to be unique per TAC+SV for this to be able to cope with any granularity of transition. This is against our decision at the last meeting. Also, this method DOES NOT allow sharing of PLMN assigned IDs across different UE models and it has to be unique at the granularity of the transition! This to us cannot be assumed to be a generic assumption for all the PLMN assigned UE Radio Capability IDs assignment algorithms.
From S2-1911804
The network identification of applicable UEs can be implementation specific and the granularity of such deletion trigger depends on the parameters of the deletion trigger. A working mechanism to use for P-RACS ID deletion in UEs is proposed in 23.501 CR#1592 (S2-1911307).
We think that when a UE manufacturer provides to operators a dictionary of UE radio Capabilities IDs, the Manufacturer says to which TACs these apply. As from the last meeting we have agreed we do not support transitions per TAC+SV.
So all we need to do is to STANDARDIZE that there in UCMF an association between PLMN assigned IDs and the TACs of the UEs that got each PLMN assigned ID assigned.
  This allows identification on a TAC granularity basis of WHICH PLMN assigned IDs are associated to the TAC values of the Manufacturer Assigned IDs
  This is only needed for maintenance of PLMN assigned IDs in UCMF
Then the criterion for deletion in AMF is just based on these TACs. There is no need whatsoever to indicate to the AMFs the PLMN assigned IDs for deletion as the command to the UE is to delete ALL the PLMN assigned IDs and not one specific PLMN assigned ID.
  The indication of a specific PLMN assigned ID to the AMF is not needed and would only be needed as also it prevents the sharing of the PLMN assigned IDs across different UE models
Agreement 4: Standardise that the PLMN assigned IDs are associated in UCMF to a TAC value and that the
Manufacturer assigned IDs transition granularity is per TAC

## Slide 5: Transition mechanism trigger unspecified?
PLMN assigned IDs
1
2
3
4
5
6
7
8
9
MANU assigned IDs Vendor ID =10 TAC values x,y | Radio config
a | LTE
b | LTE+NR
c | LTE+NR no mimo
? Which PLMN assigned IDs are no longer needed ?
Without association to a TAC value, decision is not possible: we need to keep in ALL UCMFs
an association of PLMN assigned IDs to TACs

## Slide 6: Transition mechanism specified trigger: delete per TAC in AMF
PLMN assigned IDs | Associated TACs
1 | wz
2 | xyw
3 | xy
4 | wz
5 | z
6 | z
7 | xyzw
8 | w
9 | z
The PLMN assigned IDs only associated to x,y are no longer needed
MANU assigned IDs Vendor ID =10 TAC values x,y | Radio config
a | LTE
b | LTE+NR
c | LTE+NR no mimo

## Slide 7: Transition mechanism specified trigger: delete per TAC in AMF
PLMN assigned IDs | Associated TACs
1 | wz
2 | xyw
3 | xy
4 | wz
5 | z
6 | z
7 | xyzw
8 | w
9 | z
The PLMN assigned IDs to be removed in UCMF after transition
MANU assigned IDs Vendor ID =10 TAC values x,y | Radio config
a | LTE
b | LTE+NR
c | LTE+NR no mimo

## Slide 8: Transition mechanism specified trigger: delete per TAC in AMF
PLMN assigned IDs | Associated TACs
1 | wz
2 | w
4 | wz
5 | z
6 | z
7 | zw
8 | w
9 | z
State after transition
UCMF
MANU assigned IDs transitioned TAC values
x
y
UCMF
AMF
MANU assigned IDs Vendor ID =10 TAC values x,y | Radio config
a | LTE
b | LTE+NR
c | LTE+NR no mimo

## Slide 9: Transition mechanism specified trigger: delete per PLMN assigned ID in AMF and mixed mode allowed
PLMN assigned IDs | TACs | Quar.
1 | w | 
2 | z | 
3 | x | 
4 | y | 
5 | w | 
6 | x | 
7 | y | 
8 | z | 
9 | z | 
The PLMN assigned IDs need to be quarantined but never deleted in UCMF
The PLMN assigned IDs can only be associated to a single TAC (no sharing allowed )
It is not possible to know which PLMN assigned Id corresponds to the no MIMO config. As the operator has no clue on what the missing configurations are: so the UCMF indicates a list including all the P-RACS IDS for TACs X, Y to AMF
PLMN assigned IDs | TACs | Quar.
10 | x | 
11 | y | 
12 | z | 
13 | w | 
14 | w | 
15 | z | 
MANU assigned IDs Vendor ID =10 TAC values x,y | Radio config
a | LTE
b | LTE+NR
NOT ASSIGNED (i.e. not in Manufactures assigned IDs DB): In general there is no notion of which and how many such configs could possibly be either! | LTE+NR no mimo
Problem: the quarantined IDs cannot be reassigned and need to be ported if the UCMF changes (vendor swap) or the assignment algorithm changes
Serving LTE+NR no MIMO Radio config

## Slide 10: Transition mechanism specified trigger: delete per PLMN assigned ID in AMF and mixed mode allowed
PLMN assigned IDs | TACs | Quar.
1 | w | 
2 | z | 
3 | x | 
4 | y | 
5 | w | 
6 | x | 
7 | y | 
8 | z | 
9 | z | 
State kept in the system at regime conditions in AMF and UCMF
PLMN assigned IDs | TACs | Quar.
10 | x | 
11 | y | 
12 | z | 
13 | w | 
14 | w | 
15 | z | 
16 | x | 
17 | y | 
MANU assigned IDs Vendor ID =10 TAC values x,y | Radio config
a | LTE
b | LTE+NR
UCMF
UCMF
UCMF
PLMN assigned IDs for deletion
3
4
6
7
10
11
AMF
Problem: the quarantined IDs cannot be reassigned and need to be ported if the UCMF changes (vendor swap) or the assignment algorithm changes
Serving LTE+NR no MIMO Radio config

## Slide 11: Conclusions
Only PLMNs supporting UEs running in PLMN assigned mode or UE manufacturer assigned mode are expected
No PLMN is expected to solely serve UEs using manufacturer assigned mode
Support of UEs running in Mixed mode is not required unless we want to support untested UE configurations in the market (!!!!)
It has been shown that the association of PLMN assigned IDs to TAC values is required. This should be standardised.
It has been shown the support of indication of deletion of specifc PLMN assigned IDs to AMFs is too complex statewise (more state) and signalling wise (more signalling to delete some IDs) and also madates uniqueness of PLMN assigned ID per TAC. It makes changes of UCMF or UCMF PLMN assigned IDs algorithms complicated (porting of quarantined values creates a hurdle to adoption of new algorithms or new UCMF vendors)

## Slide 12: proposals
Agreement Proposal 1: It is not expected there will exist PLMN deployments supporting Manufacturer Assigned IDs only
Agreement Proposal 2: A standardised trigger for transitions is required
Agreement Proposal 3: A UE Supporting Manufacturer assigned IDs is expected to have one and correct (i.e. not invalid) for each of its radio configurations, else it is faulty and the UE type can use PLMN assigned IDs
Alternative Agreement Proposal to 2 and 3: Remove the options to use Manufacturer assigned IDs if it is expected to be difficult to assign an ID for each Radio Configuration (assumption: each radio configuration is tested and for each radio configuration test case a Manufacturer assigned ID can be added – so tested devices should naturally be able to have a valid Manufacturer Assigned ID for each radio configuration – 3GPP should not encourage untested configurations to come to market)
Agreement Proposal 4: Standardise that the PLMN assigned IDs are associated in UCMF to a TAC value and that the
Manufacturer assigned IDs transition granularity is per TAC