## Slide 1: Summary of eLCS offline discussion (Tuesday Morning coffee break)
CATT
SA WG2 Meeting #136
Nov 18 - 22, 2019, Reno, USA
S2-1912211

## Slide 2: Papers related to Interaction with Network Slicing
S2-1911829 | DISCUSSION | Discussion on LCS service in slice. | Nokia, Nokia Shanghai Bell
S2-1911832 | CR | 23.273 CR0058R2 (Rel-16, 'F'): Update to AMF Location Service and GMLC Location Service to support LMF selection based on S-NSSAI | Nokia, Nokia Shanghai Bell
S2-1911838 | CR | 23.502 CR1851R2 (Rel-16, 'F'): Update to AMF Location Service and GMLC Location Service to support LMF selection based on S-NSSAI | Nokia, Nokia Shanghai Bell
S2-1911741 | CR | 23.273 CR0078 (Rel-16, 'F'): Clarification on location request considering slicing | Huawei, HiSilicon
S2-1911493 | CR | 23.273 CR0072 (Rel-16, 'F'): Update LMF selection relating to Network Slice | Samsung Electronics
S2-1911419 | CR | 23.273 CR0065 (Rel-16, 'F'): LMF selection based on network slicing information | CATT
S2-1911437 | CR | 23.502 CR1913 (Rel-16, 'F'): LMF selection based on network slicing information | CATT

## Slide 3: Options on the table
Option 1: Nokia
  MT- LR procedure:
    GMLC derive the Slice information according Application information(by local policy);
    AMF select LMF by GMLC provide Slice information, or by allow an allowed S-NSSAI;
  Deferred 5GC-MT-LR procdures:
    The NEF invokes the Nglmc_Location_ProvideLoacation_Request service operation to the (H)GMLC, which contains the attributes received from the AF request and may contain network slicing information derived from the AF-Service-Identifier in the AF request using the local policy.
Option 2: CATT
  MT-LR procedure
    App Id is sent to AMF, and AMF invoke PCF service, and PCF decides the S-NSSAI based on App ID and UE’s NSSP;
  MO-LR procedure
    UE decides the S-NSSAI related to the application based on NSSP and includes the S-NSSAI in the UL NAS TRANSPORT message
  LMF change procedure
    If no S-NSSAI is provided by UE in step 25 in clause 6.3.1, the AMF shall use one of the S-NSSAI(s) marked as default in the Subscribed S-NSSAIs to select LMF;
Option 3: Huawei and Samsung
  HUAWEI: AF does not provide slicing information for a location request.
  SAMSUNG: LMF selection does not consider Network Slicing network information;

## Slide 4: Summary of the discussion:
Participant:
  Ericsson, Huawei, China Mobile, Samsung, Nokia, CATT
How to handle LMF selection for MT-LR procedure has been discussed;
Some companies want to have a solution in rel-16:
  Application information is used as input to candidate NFs to get corresponding Slicing information
  Candidate NFs: GMLC, NEF, AMF, PCF;
    Single NF, e.g. GMLC or NEF or AMF, is preferred by some companies;
      But which one?
    For PCF, some companies have concerns;
  Some companies want to keep rel-16 simple, i.e. no solution.

## Slide 5: Possible Way forward
Whether we need solutions in Rel-16?
  Yes: then, which option to go?
    Option1: AFid is mapped to network slicing info at the NEF/GMLC based on local configuration
    Option2: AFid is mapped to network slicing info at AMF based on local configuration
    Option3: AFid is provided to the AMF, and AMF selects the slices based on AFid.
  No:
    Rel-17 may not be possible to handle this due to the FS_eLCS_ph2 is “in*”;