## Slide 1: WID S2-2003106: IEEE Compatible Ethernet Switching
Jeffrey Zhang
Juniper Networks

## Slide 2: R16 FASMO Issue #1.3 for TSN
7 out of 9 parties voted for supporting multiple ports on NW-TT
2 parties pointed out that currently Ethernet Switching services (5.8.2.5.3 and 5.8.2.13) do NOT allow multiple N6 interfaces
Even if we allow multiple ports on NW-TT via FASMO for R16, it won’t actually take effect until the single-N6 restriction is removed
  How to remove it - R16 FASMO? TEI17? R18 SID/WID?
TEI17 proposal S2-2001806 was to remove that (among other enhancements)
  Feedback was “more study needed”

## Slide 3: TEI17 S2-2001806 Background
To remove known limitations in current 5G-LAN
  That had been discussed and well documented
Three enhancements for the routing/switching based autonomous forwarding model, in the order of complexity
  #1: IEEE-compatible Ethernet Switch
    Loop-prevention mechanism in particular – needed to support multiple N6
  #2a: UPF-UPF tunneling
    Again with loop-prevention considerations
  #2b: Integration with IETF IP/E-VPN solutions
    Single mature solution across wireline/wireless
    Take advantages of all existing/future features/enhancements of IP/E-VPN

## Slide 4: What’s New in This S2-2003106
S2-2001806 was on hold – people preferred “more study”
Why this new S2-2003106
  Need to remove the single-N6 restriction for the R16 FASMO issue 1.3 for TSN
  What if we remove #2b in S2-2001806 and limit to switching only
    Do we still need “more study”
    If that is acceptable, do we want to handle it as R16 FASMO
But why is 5G-LAN involved here
  Isn’t TSN bridging applicable in the context of 5G-LAN as well?
  (Routing/)Switching function is the same w/ or w/o 5G-LAN
    5G-LAN just allows different groups of PDU sessions and N6 interfaces
  Let’s solve the problems for TSN w/ or w/o 5G-LAN, and solve the problems for Ethernet Switching w/ or w/o TSN

## Slide 5: Backup Material
5.8.2.5.3 “Support of Ethernet PDU Session type”
  Specifically about Ethernet Switching – implicitly treat UPF as switch
  No mentioning of 5G-LAN, though it is just a special case of 5G-LAN
5.8.2.13 “Support for 5G VN group communication” – two models:
  Implicit switching based autonomous forwarding (based on 5.8.2.5.3)
  PDR/FAR based forwarding controlled by SMF
Routing/switching functions are the same with or without 5G-LAN
  Both old and new TEI17 proposal is for the (routing/)switching model
Slides for previous WID S2-2001806 after this slide

## Slide 6: WID 2001354/2001806: 5G-VN and IEEE/IETF Solutions
Jeffrey Zhang
Juniper Networks

## Slide 7: Background
5G LAN-type Services
  For IP/Ethernet virtual network services
    IP or Ethernet PDU Session
  Each virtual network is referred to as a 5G-VN (group)
Currently two models of group communication
  Forwarding based on SMF-programmed PDR/FAR
    5.8.2.13.1, 5.8.2.13.2, 5.8.2.13.3.2
  UPF autonomous forwarding based on learnt IP/MAC routes
    5.8.2.5.3, 5.8.2.13.3.1, S2-2001673
    Referred to as routing/switching model
      PDU sessions treated as logical interfaces of a router/switch instance for the 5G-VN
      N6 interfaces also belong to the router/switch instance

## Slide 8: WID 2001354  2001806
For the routing/switching model
  The PDR/FAR-based model can independently evolve
Motivations
  Removes current limitations
  Optimize group communications
  Reuse existing/future features/optimizations of wireline IEEE/IETF solutions
    A service level, 5G-VN is no different from IP/E-VPN
    Good for 3GPP, operators, and vendors

## Slide 9: Enhancement #1
When not using UPF-UPF tunneling
  N6 interface could connect to a DN instantiated by IP/E-VPN
For an Ethernet 5G-VN, the switch is IEEE compatible
  Use STP or other methods to prevent looping
  Based on study in S2-1905040
Explicitly calling out routing/switching to allow routing/switching related features and optimizations
  E.g. multicast optimizations based on IGMP/PIM routing/snooping
UE1
UPF1
UE2
UPF2
UPF3
UE3
DN
N6
N6
N6

## Slide 10: Enhancement #2a
When using UPF-UPF tunneling
N19 tunnels treated as N6 interfaces
  i.e. as logical interfaces of router/switch instance for the 5G-VN
  MAC learning on N19 tunnels
  Similar to #1
Use STP to prevent looping among more than two UPFs
  sub-optimal UPF-UPF traffic
Loop prevention alternative: N19 traffic not forwarded back to N19
  This is then similar to E-VPN
UE1
UPF1
UE2
UPF2
UPF3
UE3
CN
N19

## Slide 11: Enhancement #2b
Integrating with IP/E-VPN
  UPFs become IP/E-VPN PEs
  PDU sessions and N6 interfaces are interfaces of IP/MAC VRFs/BDs on PEs
    A VRF/BD is a router/switch instance for a 5G-VN
  UPF-UPF tunneling managed by IP/E-VPN
UE1
PE1/
UPF1
UE2
PE2/
UPF2
PE3/
UPF3
UE3
CE2
N6
CE3
N6
CE1
N6
IP/E-VPN

## Slide 12: Simple Summary
3GPP procedures establish IP/Ethernet PDU sessions for 5G-VNs
PDU sessions treated as logical interfaces of:
  Standalone router/switch instances on UPFs
    #1, #2a
  Or, IP/MAC VRFs/BDs on IP/E-VPNs PEs
    #2b
Routing/switching functionality (w/ or w/o IP/E-VPN) used mainly to determine where to forward traffic based on IP/MAC addresses
  PDFs/FARs can still be used for other functions
    Reporting, per-UE/flow QoS treatment, etc.

## Slide 13: Isn’t #1/#2a enough? Do we really need #2b?
#1 requires an N6 interface to connect to remote group members via IP/E-VPN
  In some scenarios it is desired to integrate UPF and PE w/o using N6
#2a with STP leads to sub-optimal forwarding among UPFs
  #2a without STP becomes very similar to E-VPN (#2b)
#2b is required for some scenarios, to integrate UPF and PE functionality
In other words, why not using IP/E-VPN since:
Integrating with IP/E-VPN is desired for some scenarios
Integrating with IP/E-VPN is required for some scenarios
IP/E-VPN is already there
  Supported by all major vendors (at least on their wireline product line)
  Deployed by many operators including MNOs (e.g. for backhaul)
  Features/optimizations can apply for both wireline and wireless deployments

## Slide 14: Proposed 23.501 text changes
S2-2001807
  Minor changes expected based on feedback
No need to worry about the detailed wording for now
The key for now is to agree this qualifies as a TEI17 item
  The concept in the WID
  The possibility of reaching consensus
    With 0.5 TU online
    Plus offline effort

## Slide 15: Backup Slide: Ethernet Multi-homing
UE1
PE1
UE2
UPF2
UPF3
UE3
EVPN
N6
N6
PE2
LAG - all-active
multihoming
UE1 is multi-homed to PE1 (wireline) and UPF2
  All-active multihoming
  Some flows go PE1 while some to UPF2
A broadcast/multicast frame is sent to PE1 then PE2/PE3 then UPF2/UPF3
UPF2 will send traffic to UE2 and back to UE1
  UPF2 can’t block traffic based on source mac address
    Traffic could be from a device behind UE1 and unknown to UPF2
    UPF2 learning the source mac could also be delayed for many reasons
If UPF2 is integrated into PE2, EVPN procedures will prevent traffic from being sent back to UE1
PE3