## Slide 1
Devaki Chandramouli
Rapporteur, Nokia
Vertical_LAN
Way forward for SA2 CC on April 20th, 2020

## Slide 2: Item #1
1) Parameters for UPF selection upon PDU Session establishment.
Current text refers to: DNN, Traffic classes, VLANs.
Options in submitted papers:
1A: remove Traffic classes and VLANs (2782 (Ericsson), 3036 (ZTE), 3173 (Nokia), QCOM)
1B: keep existing parameters (3049 (CATT), 3050 (CATT), 3109 (CMCC), 2960/2961 (Samsung), 3079/3080 (Huawei))
1C: remove Traffic classes and VLANs, but add Bridge identifier stored in subscription (3156 (Intel), 3044 (Intel), 3083(Intel)).
1D: remove Traffic classes and VLANs, but add Bridge identifier provided by DS-TT (3156 (Intel), 3101, 3105 (Intel)).
Way forward proposal: Seems like 1B is simply copying existing text to UPF selection section. Commonality between 1A, 1B, 1C is removal of Traffic Class, VLAN ID for UPF selection section.
Determine whether Traffic Class, VLAN ID are needed for UPF discovery and UPF selection by show of hands.
Discuss separately if there is a need for Bridge ID for UPF discovery & selection.

## Slide 3: Item #2
2) Port and Bridge Management Information.
Current text: 23.501 Table Port Management Information table contains information that is both port and bridge specific.
Options in submitted papers:
2A) Split of the Port Management Information table into Port-specific and Bridge-specific tables (2706).
2B) Essential enhancements on the existing table (e.g. 3211, 3172) to address the gaps.
Way forward proposal: show of hands during the call.
Note: use the outcome as the basis to determine which paper should be used as the baseline for revisions to the table.

## Slide 4: Item #3
3) Bridge ID and Bridge MAC address
Current text: states that Bridge ID is derived from the “Bridge MAC address”.
Options in submitted papers:
3A) define Bridge ID as independent parameter, but keep “Bridge MAC address” (2716 (Ericsson), 3081 (Huawei)).
3B) define Bridge ID as independent parameter as in 2716, 3081 but remove “Bridge MAC address” (no proposal?).
3C) continue to use Bridge ID derived from ‘Bridge MAC address’
Way forward proposal: show of hands during the call.

## Slide 5: Item #4
4) DS-TT MAC address and session binding in PCF.
Current text: DS-TT MAC address is provided by DS-TT. A “UE MAC address” is used for session binding in PCF.
Options in submitted papers:
A) Removal of DS-TT MAC address. Session binding based on (Bridge ID, port number) tuple (2716, 2717, 2718).
B) Session binding is performed with DS-TT MAC address (e.g. 3204).
Consideration:
Option B is an essential correction to existing spec while Option A is a radical change to current approach.
Way forward proposal: Go with Option B?

## Slide 6: Item #5
5) PSFP based Hold and Forward buffering (for per stream H&F buffering)
SA2 Moderated email discussion outcome/Working assumption:
Support for PSFP based Hold and Forward Buffering rule
  Given no clear majority this functionality will not be supported in Rel-16.
3082, 2841 proposes to support this in Rel-16 (not compliant to agreed working assumption)
As a consequence following papers propose to fix the 5GS Bridge delay reporting to avoid the issue of lack of in-order delivery and incorrect Qbv enforcement:
2889, 3121, 3035
Way forward proposal: Note 3082, 2841 for Rel-16 to be aligned with working assumption. Merge 2889, 3121, 3035.
If the group wishes to re-open the working assumption, then do informal show of hands to determine one way or the other.

## Slide 7: Item #6
6) Reporting CAG ID list over N2
Options:
5A) S2-2003076, S2-2003077 – Proposes Reporting of CAG ID list per cell over N2
5B) S2-2002845 – The NG-RAN reports supported CAG ID(s) per TAI over N2
Consideration:
Neither of the proposal has been agreed in RAN3 yet. This is still being discussed in RAN3.
Given that we agreed S2-2001614, which says
NOTE 2: It is assumed that the AMF is made aware of the supported CAG Identifier(s) of the CAG cell by the NG-RAN.
it should be clear that the ball is now in RAN3’s court. Let us avoid parallel discussions, time and effort in two WGs, postpone the discussion in SA2 and leave the discussion to RAN3, align TS 23.501/2 after they conclude.
Way Forward proposal: Postpone 3077/2845 for SA2#138E.