## Slide 1: SA2#141E MUSIM CC Conclusion proposal for Notification type of solutions
LG Electronics

## Slide 2: Conclusion proposal for Notification type of solutions
Advantage of Push notification
  No RAN impact
    Whether all RAN nodes can support MUSIM feature (e.g. changing UE_ID) is FFS.
    RAN based solution (e.g. scheduling gap) may not be supported by all types of devices due to limited capability.
Notification type of solutions (#7, #8, #12, #13, #27)
  Sol #8 only applicable to 5GS
  Sol #13 benefit is not clear as SIP forking is already supported for IMS service
  Sol #7, #12 ,#27
    similar concept, i.e. MME/AMF notifies paging to paging server and paging server sends notification to the UE
      Sol #7: via user plane
      Sol #27: via user plane + considers NAT issue
      Sol #12: via SMS (can be delivered either via control plane (i.e. NAS) or user plane(i.e. IMS))
Proposal
  MME/AMF notifies paging to AF (e.g. paging server) and AF sends Push notification to the UE.
    Which protocol is used to send Push notification is FFS. Can be defined in stage 3 or during the normative work.