## Slide 1: Discussion on Probability Improvement of informing the MT call to the UE in very poor SNR conditions
NEC
3GPP TSG SA WG2 Meeting #161 S2-2401954
Athens, 26 February – 1 March 2024 revision of S2-24xxxxx
Agenda item: 30.1

## Slide 2: Introduction
RAN sends a LS (RP-234075/S2-2400036 LS on Robust Notification Alert for NTN-NR Rel-19) to SA2:
RAN#102 discussed a candidate features of a robust notification/paging proposed for the Rel-19 RAN2 led NR-NTN-ph3 WI. The robust notification/paging should be addressed to a particular UE in a cell. The intent is to maximise the probability for a UE to be informed of a mobile terminated call when in very poor SNR conditions which prevent to receive a normal paging message.
This feature should:
be triggered by the network upon e.g. paging failure (i.e. when no paging response from the UE has been received by the network), or other criteria; and
apply only for mobile terminated calls; and
inform the user of a mobile terminated call so the user could then try and move to a location with better coverage.
It is noted that this feature is highly desirable for satellite networks to reach users experiencing low SNR or NLOS channel conditions.
Before some standardisation activity can be started in RAN on the subject, some inputs, guidance and requirements would be needed from relevant SA WGs.

## Slide 3: Problem Statement
RP-230272 Paging Alert Channel for NR NTN Downlink Coverage Enhancement:
  Satellite to User Equipment (UE) transmission typically has very limited power margin and usually requires line of sight for best performance. For Mobile Originated calls, users are aware of the channel quality and can achieve LOS communication by consciously adjusting the spot of signal transmission/reception. For Mobile terminated calls, users are unaware of its channel condition and might miss important paging messages even within the LOS coverage area.
  When UE is inside a pocket or backpack, and/or inside a car, or being blocked by building and/or foliage, the additional path loss causes very low signal to noise ratio (SNR) at the receiver.
  It is important to ensure that paging messages are successfully received by the destined users. But, when the Core Network or the gNB pages such UE in IDLE or INACTIVE mode, the UE may be in a very poor channel condition and may miss the 5G NR paging message due to very low SNR, even though it is still in the beam coverage of the NTN system.
In TN-NR, the UE (e.g., in the garage, basement, elevator) may also be in very poor SNR conditions which prevent to receive a normal paging message. It is identified that the intention should be not only in NTN-NR, but also in TN-NR, i.e., how to improve the probability of informing the MT call to the UE in very poor SNR conditions should be applied in both NTN-NR and TN-NR.
Since this intention is common for NTN-NR and TN-NR, and has improvements to the current and future commercial real deployments, it is worthy to address this urgent and long-term intention in Rel-19.

## Slide 4: Potential Solution 1: NB-IoT
S2-2400391:
Proposal 1: NTN NB-IoT is considered as a suitable transport for a robust alert/notification.
Proposal 2: The relation/interaction between robust alert/notification and IMS incl. IMS call control is investigated, incl.
- Relation between SIP INVITE and the intended alert/notification (See NOTE)
- Interactions with the Caller UE (user) while the system tries to reach the Called UE (user)
Proposal 3: If necessary, depending on the outcome of proposal 2:
- the support of IMS Call control signalling over NTN NB-IoT is considered.
NOTE: An alert signal is intended to be emitted by the Called UE upon reception of the [SIP INVITE/alert/notification] before resource reservation for the call is finalized. The remaining IMS transactions complete once the UE regains coverage of NTN NR.
Comments:
This solution may have no impacts to RAN1.
This solution has the restriction and requirement that the UE and network have NB-IoT capability.

## Slide 5: Potential Solution 2: MUSIM
S2-2400792:
Option #2: Explore alternative methods of notifying the user. For instance, if the UE supports MUSIM, when the paging of USIM-1 is failure, the alert message can be sent through another access of USIM-2 (e.g., terrestrial access, IoT NTN access, etc.), which requires the AMF to be aware of the binding relationship between USIM-1’s ID (e.g. SUPI, IMSI, GPSI, MSISDN etc.) and USIM-2’s ID.
Comments:
This solution may have no impacts to RAN1.
This solution may have the privacy issue for the interactions between USIM-1 and USIM-2, and between two PLMNs. This privacy issue should be studied during the study phase and should be discussed with SA3.
This solution has the restriction and requirement that the UE is a MUSIM UE with 2 in-use USIMs.

## Slide 6: Potential Solution 3: PAC
RP-230272:
allocate a dedicated Paging Alert Channel (PAC) in the current 5G NTN downlink spectrum
Paging Alert Channel will be used to notify UE when normal paging calls and messages can’t be delivered to UE successfully in 5G NR paging channel
Proposal 1: Consider in 3GPP work program, the definition of NR_NTN enhancements (e.g., a dedicated channel for alert) optimized to allow for reception of alert messages in very low SNR conditions (e.g., vehicles/boats/blockage).
Note: the intent is to alert the UE to move to a better signal reception location for communication.
Comments: This solution has RAN1 impacts, and may or may not have SA2 impacts. The E2E solution can be studied during the study phase.

## Slide 7: Way-forward proposal
SA2 starts a new Rel-19 SID to study maximising the probability for UEs in NTN-NR and UEs in TN-NR to be informed of a mobile terminated call when in very poor SNR conditions which prevent to receive a normal paging message.
  SA2 studies the without-RAN1 impact solution related with NB-IoT and MUSIM.
  SA2 does not study the with-RAN1 impact solution until RAN decides to study PAC.
SA2 sends LS Reply to RAN and cc SA1/SA to sync up and ask for comments.

## Slide 8: SA2 SID Objective and TU plan Proposal
Work Task ID | TU Estimate (Study) | TU Estimate (Normative) | RAN Dependency (Yes/No/Maybe) | Inter Work Tasks Dependency
WT1 | 2 | 2 | Maybe | 
WT1.1 | 1 | 1 | Maybe | 
WT1.2 | 1 | 1 | Maybe | 
WT2 | 0 | 0 | Yes | 
4 Objective
The study aims at investigating to maximise the probability for a UEs in NTN-NR and UEs in TN-NR to be informed of a mobile terminated call when in very poor SNR conditions which prevent to receive a normal paging message. After receiving the notification alert of the incoming call, the UE tries to find an available NTN-NR or TN-NR access to complete the incoming call.
NOTE 1: SA2 will consider the SA1 requirements if received.
  WT1: Study the notification alert via the available access without RAN1 impact:
    WT-1.1: Study on the notification alert via the available NB-IoT of NTN and TN.
    WT-1.2: Study on the notification alert to the (U)SIM via the available access while the incoming call is calling another (U)SIM for the MUSIM UE.
  WT2: Study the notification alert via the NTN-NR and TN-NR with RAN1 impact.
  NOTE 2: SA2 will not start WT2 until RAN decides to study Paging Alert Channel (PAC).
  TU estimates and dependencies
  Total TU estimates for the study phase: 2
  Total TU estimates for the normative phase: 2
  Total TU estimates: 4