## Slide 1: Rel-19 FS_Ambient IoT Status
Huawei
SA WG2 Meeting #166 Orlando
November 18 – November 22, 2024

## Slide 2: Status of the study and TR conclusion, after SA#165
85% study complete after SA2#165 (Oct, 2024).
Latest TR 23.700-13 v1.1.0 includes the conclusions:
  Key issue 1:
    Architecture options for T1 and T2 (2 options for T1, 4 options for T2)
    General aspects for both T1 and T2, e.g. new NF “AIOTF” , et al
  Key issue 2:
    Permeant AIOT Device ID
    Temp ID issue leaves to SA3
  Key issue 3:
    AIoT Services to be supported
    NEF exposure to AF for AIoT

## Slide 3: Status of the study and TR conclusion, ongoing in SA2#166
Target for 100% study complete after SA2#166
Highlights of latest TR conclusion discussion:
  Way forward of architecture options conclusion: to support the following options:
    T1 (2 options): Direct interface option and Indirect interface option
    T2 (2 options): UP option and RRC indirect option
  Promising conclusion principles will be agreed:
    AIOT NAS protocol between AIoT Device and AIOTF
    Identification of permanent AIoT Device
    Subscription-like information management
    NEF exposure to AF for AIoT
    Assistance information provided by CN to Reader based on information from AF
    Principles of BS/UE Reader selection, e.g. AIOTF selects the Reader
    Principle of UE reader authorization
    Principles of AIoT Service procedures
    Others…

## Slide 4: Issues to be coordinated with other WG in the normative phase
Issues to be coordinated with SA3:
  Architecture aspects to support security e.g. Authentication, ID Validation.
  Whether the temporary ID in the AIoT NAS layer is required for the privacy protection is FFS and is pending SA WG3 decision.
  Whether and how to support enabling temporarily disabled AIoT devices. (In the approved SP-231806/240969, it is stated that enable/disable device operation will be handled by SA3)
Issues to be coordinated with RAN WG:
  What information and how to provide it to Readers for topology 2.
  For RRC based option of topology2, whether the gNB performs the down selection of UE readers provided by AIOTF.
  AIoT Reader control by AIOTF
  NOTE: Final list will be worked out at the end of the meeting

## Slide 5: Issues will be re-visited in SA2 in the normative phase
Based on the agreed TR conclusions, further work needed to finalize:
Information stored in the AIoT Device subscription-like data (static information).
Information stored in AIoT Device context data (dynamic information).
Which network entity(ies) to store the AIoT Device subscription-like data and/or the AIoT Device context
AIoT Reader selection by AIOTF.
UE Reader authorization.
Aggregation of data reported by AIoT Device.
Core network control on the PDU session establishment for the UP-based option in topology 2.
  NOTE: Final list will be worked out at the end of the meeting

## Slide 6: Status on Rel-19 Ambient IoT work item
Target for approval of the WID in this meeting
  Some companies view: to endorse the WID
WID was discussed in Ambient IoT session and currently under revision.
Highlights of the WID discussion:
  Coordination with RAN is expected to finalize the scope of the work item
  WI objectives will be aligned with the agreed TR conclusions
  Approximate TU estimation to be given at the end of the meeting
    7 TU suggested by Rapporteur
    Some companies view: higher number of TU preferred