## Slide 1: VFL inference parameters
Thomas Belling
Nokia

## Slide 2: Problem statement
An NWDAF as VFL server is triggered by an analytics request or subscription to perform inference
The request can contain parameters as defined in Clause 6.1.3 of TS 23.288
The provided analytics can also provide response parameters as defined in Clause 6.1.3 of TS 23.288
It needs to be determined which of those parameters can be handled by the VFL server alone, and which parameters require related interactions with the VFL clients
This issue is reflected in the following EN: Editor's note: It is FFS whether additional parameters are needed to send from the VFL server to VFL client, e.g. parameters used in training phase and parameters from Analytics request. Editor's note: It is FFS additional parameters are needed to send from the VFL client to VFL server
The author believes that the parameters listed in slides 3 and 4 may need to be propagated to / received from VFL clients. Feedback is invited

## Slide 3: From TS 23.288 Clause 6.1.3 Contents of Analytics Exposure: Parameters that may need to be propagated to VFL clients
The consumers of the Nnwdaf_AnalyticsSubscription_Subscribe or Nnwdaf_AnalyticsInfo_Request service operations described in clause 7 provide the input parameters listed below.
Analytics Reporting Information with the following parameters:
  [OPTIONAL] Dataset Statistical Properties: information in order to influence the data selection mechanisms to be used for the generation of an Analytics ID
  [OPTIONAL] Preferred granularity of location information: "TA level", "cell level" or "longitude and latitude level".
  [OPTIONAL] Preferred orientation of location information: ("horizontal", "vertical", "both").
  [OPTIONAL] Analytics metadata request: indicates a request from one NWDAF to another NWDAF to provide the "analytics metadata information" related to the produced output analytics. This input parameter indicates which parameters in "analytics metadata information" are required to aggregate the output analytics for the requested Analytics ID(s).
Data selection is up to VFL clients
If a VFL client is concerned with the location determination feature, it would need that informarion
Another NWDAF can aggregate analytics from several NWDAFs, among them a VFL server.
As the analytics metadata relate to properties of input data, the VFL clients handling the input data need to provide the information, and the VFL serevr can then aggregate it

## Slide 4: From TS 23.288 Clause 6.1.3 Contents of Analytics Exposure: Parameters that may need to be returned by VFL clients
Nnwdaf_AnalyticsInfo_Request service operations described in clause 7, the output information listed below, using a Nnwdaf_AnalyticsSubscription_Notify service operation or the Nnwdaf_AnalyticsInfo_Request response, respectively:
  Confidence: probability assertion, i.e. confidence in the prediction.
  [OPTIONAL] Analytics metadata information: additional information required to aggregate the output analytics for the requested Analytics ID(s). This parameter shall be provided if the "Analytics metadata request" parameter was provided in the corresponding Nnwdaf_AnalyticsSubscription_Subscribe or Nnwdaf_AnalyticsInfo_Request service operation.
  - Number of data samples used for the generation of the output analytics;
  - Data time window of the data samples;
  - Dataset Statistical Properties of the analytics output used for the generation of the analytics;
  - [OPTIONAL] Data source(s) of the data used for the generation of the output analytics;
  - [OPTIONAL] Data Processing, if applied on the data collected for the generation of the output analytics;
VFL clients could report confidence for their predictions for certain features. Confidence is dependent on available input data that can only be assed by clients
As the analytics metadata relate to properties of input data, the VFL clients handling the input data need to provide the information, and the VFL server can then aggregate it