## Slide 1
3GPP TSG SA2 Meeting #168 S2-2503486
Goteborg, SE, April 07-11, 2025
Agenda Item: 20.1.1
Source: vivo
Title: Discussion paper on CP/UP-based solutions
Work Item/Release FS_5GSAT_Ph4-ARC / Rel-20
Document for: Information/Discussion

## Slide 2
Contents
Assumptions for CP/UP based discussions
Starting point on CP and UP
Baseline examples for UP
Baseline examples for CP
Qualitative considerations
  IMS signalling efficiency
  IMS voice efficiency
  Qualitative summary
Annex-Example of SIP message size obtained from VoNR log
S2-2503486

## Slide 3
I. Assumptions for CP/UP based examples
As approved in SP-250400, the discussion of IMS voice calls using NB-IoT (GEO) satellite access connected to the EPC is limited to scenarios utilizing the SGi interface, as illustrated in Fig.1. It has been observed that both Control Plane (CP) and User Plane (UP)-based solutions can support Non-IP Data Delivery (NIDD) as well as IP-based data transmission.
To streamline the discussion on CP/UP-based solutions, the following assumptions are established as foundational points:
Assumption #1: Only IP-based solutions are considered in this study, while NIDD-based solutions remain FFS.
Assumption #2: IMS signaling and IMS voice data are assumed to be transmitted exclusively via either the Control Plane (CP) or the User Plane (UP), without any hybrid approach.
Assumption #3: IMS signaling is assumed to follow VoLTE SIP procedures as specified in TS 23.228. Any optimizations, including compression or substitution mechanisms, will be addressed in the IMS optimization Key Issue (KI) study and are assumed to be independent of this discussion.
Fig.1 Example of IMS voice transmission path over NB-IoT (GEO) satellite access
S2-2503486
Notes: Pre-condition 流程要删减掉

## Slide 4
 | Option#a: 1 default EPS bearer | Option#b: 1 default EPS bearer + 1 dedicated EPS bearer
UP |  | 
CP |  | 
Option 1a
Option 1b
Option 2b
Option 2a
II. Starting point on CP and UP
As approved in SP-250400, WT#1.1 focuses on evaluating whether and how QoS requirements for IMS voice calls can be met over NB-IoT (GEO) satellite access. Currently, VoLTE voice operates as a VoIP service, requiring the establishment of a PDN connection to the IMS APN. This setup typically involves two EPS bearers: a default EPS bearer for IMS signaling with QCI=5 (non-GBR) and a dedicated EPS bearer for IMS voice transmission with QCI=1 (GBR).
However, as specified in clause 4.7.2.1 of TS 23.401, the EPS bearer serves as the granularity level for QoS control. Since NB-IoT does not support dedicated EPS bearers, alternative approaches must be explored to ensure QoS compliance for IMS voice services in this context.
Proposal#1: From the core network perspective, since the EPS bearer serves as the granularity level for bearer-level QoS control, the following two options are proposed as starting point for addressing the limitation of "no dedicated EPS bearer support in NB-IoT“:
NOTE: Regarding SRB usage in the CP, the decision to reuse the existing SRB-1bis or define new SRBs (one or more) depends on RAN considerations. The examples provided here are solely for facilitating discussions on EPS bearers
S2-2503486
Notes: Pre-condition 流程要删减掉

## Slide 5
III. Baseline examples for UP
1-8: Exisiting procedures: UE-1 attach with IMS APN PDN establishment via UP (S1-U, Default EPS bearer established), IMS registration via the default EPS bearer, and UE initiates call set up.
9. Dedicated EPS bearer establishment for IMS voice
Opt#1a: step 9 is skipped, since IMS voice is via the default EPS bearer.
Opt#1b: step 9 is executed, since IMS voice is via dedicated EPS bearer. Existing step 2-11 as specified in clause 5.4.1 of TS 23.401 [x] can be directly reused.
10-13. Existing procedures: call setup procedures.
Default EPS bearer established
Dedicated EPS bearer established (Opt#1b)
 | Option#1a: 1 default EPS bearer | Option#1b: 1 default EPS bearer + 1 dedicated EPS bearer
UP |  | 
Observations
  QoS control for IMS voice data:
  Opt#1a does not provide a separate QoS guarantee, whereas Opt#1b ensures QoS for IMS voice data
  Call setup time:
  Opt#1a results in a shorter setup time since no RRC reconfiguration via the Uu interface is required, unlike Opt#1b
  Note: The call setup time in Option 1b can be optimized by executing steps 9 and 12 in parallel
  Media plane VoLTE efficiency transmission mechanism (SPS & ROHC):
  Opt#1a relies on the RAN to determine whether and how to support SPS and ROHC. In contrast,
  Opt#1b enables SPS and ROHC for IMS voice data by current TN VolTE mechanisms
Fig.2 example procedure of UP-based solutions
S2-2503486
Notes: Pre-condition 流程要删减掉

## Slide 6
IV. Baseline examples for CP
1-8: same to UP, only difference is the IMS PDN is established via CP EPS CIoT Optimizations.
9. Dedicated EPS bearer establishment for IMS voice
Opt#2a: same to UP Opt#1a
Opt#2b: step 9 is executed. However, there is no dedicated EPS bearer establishment procedure for CP in 23.401, which should be study in TR, and it depends on RAN about whether and how to deal with dedicated QoS requirements and via whether and how to establish new SRB(s).
11-13. Same to UP.
 | Option#2a: 1 default EPS bearer | Option#2b: 1 default EPS bearer + 1 dedicated EPS bearer
UP |  | 
Observations
  QoS control for IMS voice data: same observation as UP
  Call setup time: Both Opt#2a, Opt#2b are a little bit longer than UP due to additional NAS layer protocol overhead. However, new procedures/mechanism is expected on RAN considering Opt#2b
  Media plane VoLTE efficiency transmission mechanism (SPS & ROHC): both Opt#2a and Opt#2b relies on the RAN to determine whether and how to support SPS and ROHC.
Default EPS bearer established
Dedicated EPS bearer established (Opt#2b)
Fig.3 example procedure of CP-based solutions, Same to Fig.2
S2-2503486
Notes: Pre-condition 流程要删减掉

## Slide 7
V-a). IMS signalling efficiency
Observations:
The impact of protocol overhead on IMS signaling transmission shows that CP offers slightly lower efficiency compared to UP, which is mainly caused by NAS layer protocol overhead, which results in call setup time for CP is a little bit longer than UP in general ;
The signalling efficiency advantage of UP over CP becomes more pronounced with the signaling message size decreases.
Fig.4 example protocol of signalling of UP and CP based solutions
Signalling efficiency ratio
The relationship among protocol overhead, signalling message size, and transmission data rate is as below. As implied by Assumption #1, the protocol stack for IMS signaling over CP or UP can follow the structures shown in Figures 4. When transmitted via UP, IMS signaling requires 32 bytes protocol overhead, which is 12 bytes less than the 44 bytes protocol overhead required via CP. No compression mechanism is assumed in this analysis.
 | Original SIP INVITE (Annex-1) | Reduce 50% | Reduce 90%
 | 2480 bytes | 140 bytes | 248 bytes
UP 32 bytes protocol | 98.72% | 97.48% | 88.57%
CP 44 bytes protocol | 98.25% | 96.57% | 84.93%
Legacy UP header
Legacy CP header
Tab.1: signalling efficiency ratio
S2-2503486
Notes: Pre-condition 流程要删减掉

## Slide 8
V-b). IMS voice efficiency
The relationship among protocol overhead, ptime (frame length), and codec bitrate is as below. Given ROHC mechanism can be introduced in both CP and UP, tab.1,2,3 show the IMS voice efficiency examples and the required PHY data rate:
NOTE: the efficiency calculation is assumed no rounded-up, no additional codec header
Voice payload efficiency ratio
Observations:
The impact of protocol overhead on IMS voice transmission shows that CP offers clear lower efficiency compared to UP, which is mainly caused by NAS layer protocol overhead.
The voice efficiency advantage of UP over CP becomes more pronounced if with ROHC mechanism.
NOTE: ptime=80ms (the 3GPP allowed maximum value as defined in TS 26.114) is taken as reference for calculation
S2-2503486
Notes: Pre-condition 流程要删减掉

## Slide 9
V-c). Qualitative summary
 | UP |  | CP | 
 | Opt#1a | Opt#1b | Opt#2a | Opt#2b
QoS control on IMS voice | No, IMS voice is carried via default EPS bearer | Yes, IMS voice is carried via dedicated EPS bearer | Same to UP Opt#1a | Same to UP Opt#1b
Call setup time | Shorter than Opt#1b, since no RRC reconfiguration | Longer than Opt#1a, but can be optimized to offer same call setup time | a little bit longer than Opt#1a due to additional NAS layer protocol overhead | a little bit longer than Opt#1b due to additional NAS layer protocol overhead
Estimated enhancements on dedicated resource reservation in RAN | Yes, the resource reservation procedures will be skipped during SDP negotiation. | No, existing resource reservation procedures can be reused during SDP negotiation. | Same to UP Opt#1a | Yes, a new dedicated EPS bearer establishment procedure for CP should be studied. RAN should decide whether and how to deal with dedicated QoS requirements and whether and how to establish new SRB(s).
Estimated enhancements on SPS&ROHC in RAN | Yes, whether and how to enable SPS and ROHC | No, existing SPS and ROHC mechanism can be reused | Same to UP Op#2b | Yes, whether and how to enable SPS and ROHC
Signalling efficiency | UP slightly higher than CP, which results in call setup time for CP is a little bit longer than UP in general ; If message size is reduced, UP clear higher than CP |  |  | 
Voice efficiency | UP clear higher than CP; If with ROHC, much higher than CP |  |  | 
S2-2503486
Notes: Pre-condition 流程要删减掉

## Slide 11
Annex: example of SIP message size obtained from VoNR log
NOTE: The size of SIP message is derived based on a lab tested VoNR log.
In total: ∼ 10980 bytes