## Slide 1: Proposed scope for 6G study item
Source: Qualcomm

## Slide 2: 6G study scope - overview
Evolve 5GS to a service delivery-friendly and efficient to operate system for 6G radio.
Approach
Study enhancements to 5GS in selected areas (see remainder of this deck)
All other existing 5GS functionality will continue to be supported as-is for 6G, e.g.
  Non-public networks
  TSN
  Wireline access integration
  …
The following on-going studies are assumed to also cover support for 6G
  Integrated Sensing and Communication (SP-250401)
  Core Network Enhanced Support for AIML Phase 2 (incl. UE Data collection for UE-side model training) (SP-250413 )

## Slide 3: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#1 | Common framework for operator services over the user-plane | WT#1: Study a common framework for supporting operator services over the user-plane including UE configuration and discovery of operator services, authentication, authorization and security establishment; binding of operator services to specific DNNs and slices. UE identification in presence of NAT | While 3GPP defines many services over NAS, there are operator services that may be better served over the user plane, particularly services that require transfer of large amounts of data or that require frequent signaling exchanges. The benefit of that is that these services can be G-agnostic. Existing examples include IMS and more recently LCS-UPP. Future examples may include AI/ML related UE data collection and sensing. For each new operator service over the user-plane the same challenges need to be solved and are typically re-designed slightly differently each time by 3GPP: UE configuration and discovery of operator services; Authentication, authorization and security establishment; Binding of operator services to specific DNNs and slices; UE identification in presence of NAT. Typically, 3GPP solves these challenges each time slightly differently when 3GPP decides to define an operator service over the user-plane. This is not only inefficient and leads to unnecessary impacts but also delays the introduction of new operator services. This justifies studying a common framework for supporting operator services over the user-plane. | SA3 for authentication, authorization and security establishment for access to operator services over the user-plane

## Slide 4: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#2 | Forward compatibility of NAS procedures, for flexible evolution and addition of new NAS services. | WT#1: Study solutions to enable operators to introduce new NAS services without having to upgrade the AMF for each new NAS service. WT#2: Study mechanisms for enabling signaling between new NFs and NG-RAN without having to upgrade the AMF specifically for each new NF - NG-RAN signaling. | Today, introducing a new NAS service requires an AMF upgrade even if AMF is not terminating the new NAS service. For each new NAS service the AMF needs to be upgraded to support a new payload type in NAS; subscription check for the new NAS service; selection of the (new) NF that terminates the new NAS service; routing new NAS messages to the new NF; relaying information between the new NF and RAN (if needed). This constitutes an unnecessary burden for MNOs and delays the introduction of new NAS services. Therefore, it is worth studying solutions to avoid the need for upgrading AMF when introducing a new NAS service. | Coordination with CT1 on details of NAS; coordination with RAN3 on NF - NG-RAN signaling; coordination with SA3 on security aspects as needed.

## Slide 5: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#3 | Harmonized UE tracking and paging solution | WT#1: Study a harmonized UE tracking, paging and data buffering solution for RRC states other than RRC_CONNECTED. | 5GS has two UE tracking and paging solutions: one for RRC_IDLE in the core network (AMF) and one for RRC_INACTIVE in the RAN. This duplication requires operators to configure multiple separate area IDs and requires network and UE to support multiple periodic timers and the different paging mechanisms. It is important to emphasize that this not only results in increased implementation complexity but also testing and integration effort for operators. This duplication also led to different concepts for buffering downlink data in CM-IDLE and CM-CONNECTED. This justifies studying a harmonized UE tracking and paging solution for RRC states other than RRC_CONNCTED. | Coordination with RAN2 on RRC states

## Slide 6: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#4 | Network Slicing for 6G | WT#1: Study how to reduce the overhead for network slicing WT#2: Study how to enable exposure of KPIs per Network Slice to the UE. | The current network slicing design has two drawbacks: Unnecessary signaling overhead for scenarios where only a single data session is used There are some scenarios, e.g., LPWA, that typically do not require multiple data sessions. However, the current network signaling design is not very efficient for these scenarios (i.e., when only a single data session is used) due to unnecessary signaling overhead. Lack of awareness of Network Slice capabilities at the UE In 5G Network Slicing, the UE is unaware of the KPIs and capabilities that are provided by a PLMN for a given S-NSSAI. This is an issue for scenarios where the binding of applications to slices is not done based on AppID but using other means. For instance, there have been efforts to enable operators to bind slices to traffic categories (NSSP in URSP), and the HLOS to then bind applications to those traffic categories. GSMA has attempted to define semantics (KPIs and capabilities) for those traffic categories. However, a standardized approach turned out to be too inflexible as it prevents operators from deciding which KPIs to support per traffic category based on deployment, area, etc. This justifies studying means for PLMNs to provide the UE with the KPIs allocated to each network slice, and this information to be exposed to the UE’s upper layers to facilitate binding of applications to network slices. | Coordination with CT1 on WT#1

## Slide 7: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#5 | Direct communication between RAN and CN NFs | WT#1: Study framework for direct communication procedures between RAN and CN network functions for non-UE associated procedures (e.g., fetching radio capability mapping, data collection, exposure). WT#2: Study framework for direct communication procedures between RAN and CN network functions for UE associated procedures (e.g., LCS, sensing) | New network services typically lead to additional data and signaling exchange between RAN and CN network functions. Current 5G system architecture defines NG-AP over N2 as the only transport for RAN-CN interactions. This implies that any additional data and signaling exchange between RAN and CN NFs is unnecessarily funneled through AMF. This means that each time a new service is introduced that requires a RAN-CN interaction, the AMF needs to be upgraded to support relaying of this information between RAN and the respective CN NF. Moreover, in some cases the amount of data can be quite large, e.g., for data collection. This may result in an overload of N2 and AMF congestion. Examples for non-UE associated procedures that would benefit from direct RAN-CN NF communication: RACS: Enable RAN to fetch radio capability mapping directly from UMCF. Data collection: Supports exchange of large volumes of data between RAN and the corresponding CN NF. Exposure: Enable RAN to expose capabilities, and other RAN related information, directly to multiple CN NFs. Examples for UE associated procedures that would benefit from direct RAN-CN NF communication: Especially for cases where the Network Function or Service can be deployed close to the RAN, e.g., for sensing management or a locally deployed LMF for positioning in industrial applications, there is a benefit to provide direct communication between RAN and the NF managing the feature or service, bypassing the need to communicate via the AMF, which may be deployed at a more centralized location in the network. Therefore, a framework for direct communication between RAN and CN network functions for both non-UE associated, and UE associated procedures should be studied. | Coordination with RAN3 and CT4 on RAN-CN interaction and related protocol aspects, respectively.

## Slide 8: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#6 | Non-3GPP access for operator voice service | WT#1: Study how to support operator voice service over non-3GPP access | Driven by the desire of an access agnostic core and a common RAN-CN interface, 5GS introduced N3IWF which enabled NAS as the common control plane between UE and network for both 3GPP and untrusted non-3GPP RATs. However, this led to unnecessary complexity on UE and NW side since many of the NAS concepts are specific to 3GPP access and are not applicable to non-3GPP accesses. This observation is even more important given that the only commercial use case for 3GPP-WiFi interworking is still only operator voice over Wi-Fi which is being addressed by ePDG today. It is worth noting that the ePDG solution does not suffer from the same complexity drawbacks as N3IWF. It is therefore important for 6G to study a lean solution for non-3GPP access for operator voice service following the key principles of the ePDG solution, i.e., a secure entry point into the operator’s core network without involving access and mobility management functions. ​ | 
#7 | Migration to 6G | WT#1: Study 5G/6G service steering and aggregation solutions that allow MNOs to leverage both 5G and 6G bands in scenarios where MRSS is not available | It is to be expected that 6G rollouts will include a mix of new spectrum and existing 5G spectrum. It is crucial to be able to dynamically utilize 5G bands for 6G wide-area rollouts without disrupting existing 5G services. While Multi-RAT Spectrum Sharing (MRSS), expected to be defined in RAN WGs, can provide a tightly integrated 6G-based robust low band coverage anchor for 6G mid to higher bands, it is unlikely to cover all operator deployment scenarios and needs. Therefore, it is important to study Multi-RAT connectivity solutions that leverage both the 5G-based robust low band coverage as well as 6G bands in scenarios when MRSS is not available. These solutions not only need to support traffic steering and switching but also aggregation. | RAN3 for RAN-based aggregation solutions

## Slide 9: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#8 | Voice support | WT#1: Specify IMS voice support over 6G radio WT#2: Study transitional solutions to enable MNOs to rely on previous Gs (potentially including 4G) for voice support | While it is important to specify voice support for the new 6G RAT, historic evidence indicates that there has not been voice support from Day 1 in most real deployments of a new G. Instead, a transitional phase has been required for every new G since 4G (CS fallback for the 3G to 4G transition and EPS fallback for the 4G to 5G transition). Given these learning from previous Gs, relying on IMS voice on 6G to be available at Day 1 is therefore unlikely to work for all deployments. Also, given the slow uptake of 5G SA, some MNOs may still support voice only on 4G by the time they are launching 6G. Therefore, a transitional phase for 6G to rely on previous Gs for voice support, potentially including 4G, is likely needed. | 
#9 | Traffic steering and switching for non-migration scenarios | WT#1: Study solutions for traffic steering and switching over two 3GPP access networks for non-migration scenarios | There are scenarios in which traffic steering and traffic switching between two 3GPP access networks is beneficial. For example, traffic switching between a terrestrial (TN) and a non-terrestrial network (NTN) can be used when the UE goes out of coverage of the terrestrial network and no other terrestrial networks are available. Similarly, traffic switching between a standalone non-private network (SNPN) to a PLMN can be used when a UE moves out of a stadium and loses the coverage of the SNPN. | 

## Slide 10: 6G SID Scope: Technical areas to be studied.
S.NO. | Title | Key Objectives | Justifications | Potential dependencies
#10 | Converged data management for 6G | WT#1: Study a converged, generic data management framework for 6G, which includes procedures for data collection from different data sources; data storage; data exposure. | Data collection and storage of historic data are supported for eNA in 5GC. However, the data collection was also discussed in SA2 for various other features, e.g., LCS, EnergySys. Beyond SA2, also other working groups (e.g., SA5, RAN2, RAN3) discussed different data management frameworks for 5GS. Some gaps between different WGs were also identified. For example, there was no interaction to collect data from RAN to NWDAF in 5GC, and there was also no support for exposing data from NWDAF to RAN. Therefore, it is beneficial to define a converged data management framework which covers data collection from different data sources (UE, RAN, CN, OAM and AF), data storage and data exposure to address data management requirements across WGs and for all 6G features. | Coordination with SA5, RAN2 and RAN3 on procedures for data collection